## Slide 1: Local Protection Systems: Magnets and Interceptice Devices interlocks
Manuel Zaera-Sanz
ICS/Machine Protection Systems – Slow Interlocks
www.europeanspallationsource.se
6 December 2015

## Slide 2: Table of contents
Introduction
Mission statement
Protection Functions
Our proposal of LPS for Magnet Powering
Our proposal of LPS for Interceptive Devices
Conclusions
Further work

## Slide 3: 1. Introduction
Machine Protection shall provide global protection of the ESS machine
Base document: “Preliminary hazard analysis of the ESS Machine Protection System with emphasis on production and property losses in the ESS-LINAC”
  Identification of protection functions, PIL and response time
  Additional protection functions defined during meetings with the relevant experts
  Several Local Protection Systems are needed for e.g. Magnets, Target, Vacuum, interceptive devices (collimators, FCs, wire scanners,…)
  Slow Local Protection Systems => PLC based
  High availability requirements for ESS must be fulfilled

## Slide 4: 2. Mission statement
(Slow) Local Protection System for Magnet Powering:
“ To protect equipment (investment) in case of a failure in the cooling or powering systems, taking the appropriate action to minimize risk for damage and time for recovery”
(Slow) Local Protection System for Interceptive Devices:
“To protect equipment (investment) in case of wrong machine configuration, preventing damage to the devices, pollution in the LINAC or even destruction of cavities in case of e.g. a wire that is destroyed due to too high beam power”
How?
  - Using PLC technology: safety and/or standard due to the low response time required
  - Critical protection functions: require hardwired signals (current loops)

## Slide 5: 3. Protection Functions
LPS for Magnet Powering Interlocks:
  Loss of power supply: misaligned beam (dipole), PIL3
  Loss of water cooling: magnets overheating, PIL2
  Malfunction of power supply: misaligned beam (dipole), PIL3
  Malfunction of local sensors (temperature, flow switch), PIL1-2
  Malfunctions of the LPS-MPI itself: SW, HW, parameterization, PIL3
LPS for Interceptive Devices Interlocks:
  Pulse “too long” and an interceptive device is IN, PIL2-3
  Full beam power and interceptive device is IN, PIL3
  Malfunction of the interceptive device position sensor, PIL3
  Malfunction of the interceptive device itself, PIL2
  Malfunction of the LPS-IDI itself: SW, HW, parameterization, PIL3

## Slide 6: 4. Our proposal of LPS for magnet powering
ESS magnets and power supplies (approx):
Description | Magnet op. mode | Magnet cooling | #Magnets | #Power Supplies
Ion Source solenoid coils | DC | Water | 3 | 3
LEBT solenoid | DC | Water | 2 | 2
MEBT quadrupole | DC | Water | 10 | 10
DTL PMQ (50mm AND 80mm) | Permanent | Water | 89 | 0
DTL single-plane corrector | DC | Water | 30 | 30
Spoke LWU quadrupole | Pulsed | Air | 26 | 26
Spoke LWU dual-plane corr. | DC | Air | 13 | 26
Elliptical LWU quad | Pulsed | Air | 95 | 95
Elliptical LWU dual-plane corr. | DC | Air | 55 | 110
Dogleg quad | Pulsed | Air | 12 | 12
Dipole | DC | Water | 2 | 1
A2T dual-plane corrector | DC | Air | 4 | 8
A2T quad | DC | Water | 6 | 6
Raster | Pulsed | Air | 8 | 8
TOTAL | 125 DC 141 Pulsed 89 Permanent | 142 Water 213 Air | 355 | 337
DTL PMQ do NOT require power converter Dogleg dipoles are powered by a single power converter (not decided yet)
A2T dual-plane correctors are powered by two power converters
All other magnets are powered by a single power converter
Courtesy from Edgar Sargsyan and Carlos Martins

## Slide 7: Our proposal of LPS for magnet powering
Use same principle that is currently used at CERN for warm magnets interlocks
Magnet 1
Power Converter
Magnet 2
Status info
Thermoswitches
Water Flow
Red button…
Several thermo-switches @ 60°C
Power Permit
Warm magnet
Interlock
Controller
Courtesy from Pierre Dahlen(CERN)

## Slide 8: Our proposal of LPS for magnet powering
  HW signals between LPS for Magnets Powering – Slow Beam Interlock
Slow Beam Interlock
LPS for Magnet Powering
magnets/flow status
Beam Permit
Stop Beam
Powering Permit/Abort
Power Converter
Powering Failure
Essential/Auxiliary
circuits signals

## Slide 9: 5. Our proposal of LPS for interceptive devices
  ESS interceptive devices (approx)
 | Faraday Cups | Allison Scanners | Wire Scanners | Slit & Grid | LBM | Vacuum gate valves | TOTAL
LEBT | 1 | 2 |  |  |  | 2 | 5
RFQ |  |  |  |  |  | 1 | 1
MEBT | 1 |  | 3 | 2 | 1 |  | 7
DTL | 2 |  |  |  |  | 5 | 7
Spokes | 2(BS) |  | 3 |  | 1 | 26 | 32
Medium Beta | 1(BS) |  | 3 |  | 1 | 18 | 23
High Beta |  |  | 1 |  |  | 42 | 43
HEBT |  |  | 3 (fast wire) |  | 1 | 12 | 16
A2T |  |  | 1 |  |  | 4 | 5
TOTAL | 7 | 2 | 14 | 2 | 4 | 110 | 139
Courtesy from B. Cheymol, I. Kittelmann, H. Spoelstra, M. Eshraqi and E. Laface

## Slide 10: Our proposal of LPS for interceptive devices
  Relationship between the Local Protection System for Interceptive devices and other systems

## Slide 11: Our proposal of LPS for interceptive devices
  States Machine

## Slide 12: Our proposal of LPS for interceptive devices
  Full Power Interlocks
  Prototype

## Slide 13: 6. Conclusions
Our proposal for Local Protection Systems is
  Simple
  Mostly hardware based (use of current loops 15 to 20mA)
  Current loops mechanism works well (proof of concept from other facilities)
These architectures fulfill the protection functions requirements
These architectures fulfill the mission statements
Our solution provides the needed flexibility
Increases the availability requirements for ESS LINAC

## Slide 14: 7. Further work
Continue prototyping, programming and measuring response times of our local protection systems
Start developing the local protection system for the Target as soon as the protection functions are defined, with potential use of ITER RT-CIS (currently under development) as base architecture of our Target Local Protection system
Possible presentation of the main results in our third PLC workshop at CERN in Feb 2016

## Slide 15
THANK YOU !!!