## Slide 1: DIAGNOSTICs LEBT STATUS
Franck Senée BI FORUM
Lund 2019-02-10

## Slide 2: ESS LEBT
ESS ion source parameters:
Protons beam
75 keV
Current max = 100 mA
Pulse length = 6 ms
Repetition rate = 14 Hz
Duty cycle 8%
Nov. 3rd 2015
BEAM
LEBT tank
FC
EMU V
EMU H
NPM H
DOPPLER
CEA: 2 emu (H & V) & 1 doppler unit

## Slide 3: Beam profil and Commissioning phases at catania
Phase 3: EMU design
(Ø min = 6 mm)
DBOX
DBOX
DBOX
TANK
Phase 2: Doppler design (Ø max = 80 mm)
DBOX
1- delivery at CEA Saclay for EMU and Doppler acceptance tests
2- send to Catania for the 3 phases using the « commissioning Diagnostic BOX » entirely equipped

## Slide 4: EMU: Allison scanners type EMU @ IRFU: philippe abbon - philippe daniel-thomas - jean-françois denis - patrick girardot - françoise gougnaud - tom joannem - nicolas misiara - jerome neyret - FRANCK SENÉE - Olivier tuske

## Slide 5: Principle
y3
y1
y2
y’3
y’1
y’2
z
y
x
y1
y2
y3
Beam Axis
y’1
y’3
intensity
Angle y’
y’1
y’2
y’3
intensity
Angle y’
intensity
Angle y’
y’2

## Slide 6: Allison scanner
thermal
screen
U: kinetic energy (eV) of the beam particles (H+)
I (µA)
0.39 π.mm.mrad
with =

## Slide 7: Design overview
7
Beam-Stopper
CF
Deviation plates
100 µm Slit for beamlet selection
Actuator
repeler

## Slide 8: Thermo-mechanical calculations
Hypothesis
  gaussian power deposition
  Beam characteristics
  (Réf : « L5_LEBT_EMU » 2015/30/01)
  Nodal power deposition
  Material physical datas :
    Advanced Energy Technology Group
http://aries.ucsd.edu/LIB/PROPS/PANOS/cu.html
  Steady-state based + transient thermal analysis
Description | Value | Unit
Beam energy | 75 | kV
Beam intensity at peak | 100 | mA
Repetition rate | 14 | Hz
Duty cycle | 8 | %
MINIMAL radius beam size (rms) | 3 | mm
MAXIMAL beam size diameter | 80 | mm
Average power absorbed | 625 | W
DOC réf: ESS-0036400
N. MISIARA

## Slide 9: Tmc: TZM entrance slit
1
2
3
1
2
3
Elasticity limit [MPa] for Copper (left) and for TZM (right) versus temperature [k]
TZM
selected
TZM alloy: Titanium – Molybdenum – Zirconia
Von Mises (MPa) stress
Cu

## Slide 10: Tm calculations: BEAM STOPPER
6 bars
Thickness
W= 5 mm
Cu= 20 mm

## Slide 11: Tm calculations: BEAM STOPPER
ANSYS simulation: Von Mises [Mpa] stress

## Slide 12: Tm calculations: BEAM STOPPER
W+Cu
Cu
1
2
4
3
5
4
W+Cu
selected

## Slide 13: HIP TECHNIQue: EMIT-4d example
Assembly by HIP of W-Cu
Works before assembly:
- New design for assembly whole parts
- Machining W plates and Copper
- Nickel-W face being in contact with the Copper
- Manufacturing of the water box
- Machining of the Carbon inserts and stainless steel container
HIP cycle: 950°C/1400bars/2h
Goal improving the mechanic contact
Machining after HIP:
- Remove the container
- Final machining
Positioning the assembly inside the container and closing it with TIG soldering
Exploded view of the necessary
whole parts

## Slide 14: I/V Converter + splitter for Read-Out Faraday Cup EMU
Boite blindée
FAR : 278956
Commutateur rotatif BCD
RS : 639-4783
Alimentation +/- 15V
FAR : 1550964
Kit développement SO8 OPA129
FAR : 2334129
Kit PGA AD8250
RS : 794-6717
IN
OUT
Gain2: 1,10,100,1000
I/V converter
PGA
AD8253
Trans
OPA129
+/-15V 50mA
Keithley
I max=5mA
Buffer
OPA547
4,7nF
Commutateur rotatif
Coudé BCD
FAR : 2374799
Gain 1,10,100,1000
IN
OUT
100pF
4,7pF
1pF
Diode protection
BAS416
1K //
10k / /
200k //
2M //
Gain1: A,B,C,D
RF
Proto checked on the IFMIF injector at Rokkasho in December 2015
PCB is in manufacturing progress
SCOPE
DACQ
Splitter 3 voies
A
B
C
D
Gain1RF(Ω) | Gain2 | Vout (V)
A 1 103 | 1 | 10V/10mA
 | 10 | 10V/1mA
 | 100 | 10V/0,1mA
 | 1000 | 10V/0,01mA
B 104 | 1 | 10V/1mA
 | 10 | 10V/100uA
 | 100 | 10V/10uA
 | 1000 | 10V/1uA
C 2 105 | 1 | 10V/50uA
 | 10 | 10V/5uA
 | 100 | 10V/0,5uA
 | 1000 | 10V/50nA
D 2 106 | 1 | 10V/5uA
 | 10 | 10V/500nA
 | 100 | 10V/50nA
 | 1000 | 10V/5nA

## Slide 15: Status and schedule
Delivery of the Actuators  May 2016
Delivery of the mechanic (TZM slits, deviation plates…)  June 2016
Delivery of the Beam-stoppers (W+Cu & HIP technics)  June 2016
Electrotechnics: Study and cabling specifications  in progress (CEA is waiting for the EMU cabinet layout at Catania)
Epics Command System  in progress
I/V converter  in progress
Acceptance test at CEA Saclay: Oct-Nov 2016,
then send to Catania

## Slide 16: THE DOPPLER UNIT DOppler @ IRFU: françoise gougnaud - pierre mattei - yves lussignol - FRANCK SENÉE- Olivier tuske

## Slide 17: THE DOPPLER UNIT: principLe
DlH3+
DlH2+
DlH+
Hydrogen beam
H0(H+) H0(H2+) H0(H3+)
Plasma H0 (light emission excited residual gas)
656.3 nm
θ
θ
Doppler shift of the Hα ray
expected  versus angle, for 75 keV beam
measured by a spectrometer which is able to separate the species
The intensity of the spectroscopics rays is proportional to the species quantity produced, but the production rate of the Hα ray by the residuel gas interaction is different for each species

implying that corrections using recombined cross sections must be applied
Spectrometer

## Slide 18: THE DOPPLER UNIT: principLe
IFMIF species fraction measurements

## Slide 19: THE DOPPLER UNIT: optimisation
Optimisation of the light which comes from the beam in order to make species fraction measurement inside pulse length of 5 ms
INPUTS:
EPICS compatible Hardware : ANDOR company
Magnification=2,86
Optical fiber NA=0,22 and L=25 m
Monochromator characteristics

## Slide 20: THE DOPPLER UNIT : optimisation by optical coupling
F: Incident light flux
R: apparent radiance of the light
G: etendue
In order to optimize the light collection we have to move closer to the source detector to increase .
but the NA of the optical fiber necessitates a minimal distance L.
L mini for Flux maxi
problem, L is inside the vacuum chamber!
OF
Inside vacuum chamber outside

## Slide 21: THE DOPPLER UNIT : optimisation by optical coupling
Needs an optical system for shifting the image of the optimal point downstream to the viewport (outside the source)
Afocal system:
Single lens:

## Slide 22: The doppler unit: APILUX SIMULATION
distance (mm) between the beam and the optical fiber

## Slide 23: THE DOPPLER UNIT : optimisation of the optical fiber
injector side
spectrometer side
12% of the collected light will then be cut off by the height size of the active CCD sensor (6.7 mm)
Magnification F/# = 2,86
(2,66 mm before and 7,6 mm after the F/# )
1,9 mm « theoretical »
2,66 mm in reality

## Slide 24: THE DOPPLER UNIT: first measurements
Spectrometer calibration
Bundle image (16/19 → 16% lost)

## Slide 25: THE DOPPLER UNIT: future measurements
Photometry measurements and transmission measurements are in progress in the LIDO laboratory at CEA Saclay

## Slide 26: Status and schedule
Spectrograph  checked
Fiber bundle  checked
Mechanical interface between the viewport and the optical system  in progress
EPICS Control System  in progress
Photometry measurements and transmission measurements  in progress
Acceptance test: June - July 2016 at CEA Saclay
Interface Viewport / Optical system