## Slide 1: Update on Work Package 12 Beam Transport Modules (LWUs) - UK-A-6
Dr Paul Aden, STFC Daresbury Laboratory
ESS Beam Diagnostics Forum, Lund, 11th February 2016

## Slide 2: STFC
UK Astronomy Technology Centre
Edinburgh, Scotland
Polaris House
Swindon, Wiltshire
Chilbolton Observatory
Stockbridge, Hampshire
Daresbury Laboratory
Sci-Tech Daresbury Warrington, Cheshire
Rutherford Appleton Laboratory
Harwell Didcot, Oxfordshire
Boulby Underground Laboratory
North Yorkshire

## Slide 3: STFC, Daresbury Laboratory

## Slide 4: 3 Onsite Accelerators
EMMA
ALICE
VELA
Notes: ALICE (Accelerators and Lasers In Combined Experiments) is an accelerator which has been designed and built at Daresbury Laboratory. It was formerly known as ERLP (Energy Recovery Linac Prototype).
EMMA (Electron Model for Many Applications) is a non-scaling FFAG (Fixed Field, Alternating Gradient) accelerator and is currently under operation at Daresbury Laboratory. It is the first time to demonstrate this type of accelerator.
The Versatile Electron Linear Accelerator (VELA)

## Slide 5: CLARA - under construction
Notes: Compact Linear Accelerator for Research and Applications
Uk X-ray Free Electron Laser (FEL),
Part of ASTeC’s future strategy is to develop a next-generation light source test facility to be constructed at Daresbury Laboratory. This new proposed test accelerator will be known as CLARA (Compact Linear Accelerator for Research and Applications). The CLARA project aims to build on the UK’s existing expertise and experimental experience in free electron lasers, to pave the way for a state-of-the-art FEL facility in the UK, while simultaneously contributing to international R&D.

## Slide 6: BTM WP Scope
To design, procurement and assemble;
  2 Prototypes
  3 Test Chambers
  75 LWUs
  52 Beam pipe modules
  2 Differential pumping systems
  2 mobile installation cleanrooms
Particle control only on 52/75 LWUs
BPM work package
  Only electrical centre measurement
  BPMs are to be supplied by DESY
Notes: Over the next four years we have been asked to delivery …

## Slide 7: Schedule
BTM Assembly
2015 | 2016 | 2017 | 2018 | 2019 | 2020
BP Assembly
Prototypes
LWU Assembly
Differential Pumping System 2
Installation Cleanrooms
Differential Pumping System 1
PDR Nov 15
CDR June 16

## Slide 8: Design Progress

## Slide 9: Latest Design Work
Aluminium slotted girder
BPM on entrance or exit
Semi–kinematic
girder adjustment
Pedestals
Quadrupole Magnets
Fiducials, laser tracker alignment
-50µm Accuracy
Built in lifting points
‘Particle Free’ Chamber
- ISO 5 or better

## Slide 10: Design
Based on many years experience developing accelerator modules
Slotted girders allows for versatility
Optimised for ground vibrations
Fiducial mounts for survey and alignment
  ±50µm alignment to local girder network
Girder adjustment ±25mm
Magnet/Chamber adjustment ±25mm, ±5mm due to other items
Large space between pedestals for access/egress

## Slide 11: Space is tight - Elliptical

## Slide 12: Space is tight - Elliptical
10mm
8mm
12mm

## Slide 13: Example

## Slide 14: Example
Space requirements?

## Slide 15: Example

## Slide 16: Need to know ASAP
Dimensions will be fixed in March
Dimensions needed by end of March
Changes after this point will possibly impact delivery
Changes after June WILL impact delivery

## Slide 17: Differential Pumping Sections
Design work not yet started on HEDP
Pumping ratio to be 100:1 (1 x 10-9 mbar on cryo side)
Early concepts;
Notes: Similar to previous work at stfc

## Slide 18: Mobile Installation Cleanrooms

## Slide 19: Design
Vacuum Requirements:
  1 x 10-9 mbar
  UHV Cleanliness
  Particle free to ISO 5 or better
Vacuum requirements within STFC Vacuum Specs & inc.
  Cleaning
  Baking
  RGA Scanning
  Particle counting
STFC Vacuum Specs: ASTEC-VAC-QCD-SPC001-008
Notes: Well defined UHV specs

## Slide 20: Assembly locations & Facilities
Engineering technology centre
Notes: Engineering technology centre

## Slide 21: ETC Build Area
Soft wall cleanrooms
& Assembly Area
Notes: Large Volume Assembly area with overhead crane, softwall cleanroooms, ISO 4 Cleanrooms, large vacuum laboratory,

## Slide 22: Vacuum Laboratory
Cleaning vacuum components to UHV standards with aqueous and solvent base systems
Pre clean with Auto Wash (industrial dish washer)
Solvent cleaning with HFE 72 DE capability 0.3 m cube, 3 m long chambers possible.
A demin water plant > 2 x Auto washers,
Alkali degrease bath, Power wash bay.
3 x Solvent cleaning HFE72DE Slurry blaster,
Drying cabinet, Cranes.

## Slide 23: Vacuum Laboratory
4 x ovens to 250oC
vacuum furnace to 1100oC
Air oven to 150oC
Leak detection & test facilities.

## Slide 24: Cleanrooms
Change area
6m2 - ISO 7
Outer area
80m2 - ISO 6
Inner area
12m2 - ISO 3
(at rest)

## Slide 25: Low particulate experience on ALICE
ALICE Cathode in
ISO 4 Cleanroom

## Slide 26: New Temperature Controlled Survey Alignment Room
Temperature Range 20 - 26°C
Stability ± 1°C over the full area of the room
A fixed 3D survey network
Capacity to align 6 BTM modules in the room
4 x Steel Survey Pillars
Filled with Sand
ALICE @ Daresbury
11 x Floor mounted nests
Survey & Alignment Room
Notes: rj

## Slide 27: On-going Similar builds at Daresbury
Extreme Light Infrastructure – Nuclear Physics Facility
Delivery to Romania – over 18months period from 04/16
21 Modules
21 Racks
ELI - NP
Notes: And Also 4 CLARA modules,
PSUs, Vacuum equipment, No Diagnostics, No RF.,
Racks include - PSUs, control, instrumentation, with EPICs,
Everything can be operated without overall control system

## Slide 28: Need to know ASAP
Dimensions will be fixed in March
Dimensions needed by end of March
Changes after this point will possibly impact delivery
Changes after June WILL impact delivery

## Slide 29: Thank You
ESS BI Forum, Dr Paul Aden, 11-02-16

## Slide 30: Elliptical LWU

## Slide 31: ETC Floor Plan
Electrical
Lab.
Vacuum Laboratory
Precision Machining Centre
CMM
CAM
Meeting
Room
Reception
Magnet Test
ISO 3,4,5
Cleanrooms
Survey
& Alignment
UHV Cleaning
Ovens
23 m
30 m
40 m
15 m
21 m
92 m
30 Tonne Crane coverage
Large Systems Assembly Area
ISO 4 Soft wall
Clean Room

## Slide 32: Vacuum Test Facilities
Delivered to ESS July 2015

## Slide 33: Vacuum Test Facilities
Delivered to ESS July 2015
Notes: Particle test facility to ESS will be a ‘particle free’ accelerator and this.
Outgassing system to provide in vacuum material characterisation

## Slide 34: Overview In/Out
In
  Girder design & procurement
  Chamber design (within given parameters) & procurement
  Vacuum design & procurement
  Survey & Alignment
  Particulate Control
Out
  BPM Procurement & Design
  BCM Design
  Bolt in diagnostics
  Magnet Design & Procurement
  Installation & Onsite testing
Full excluded / included list in stfc document tdl-1224-meng-spec-0005

## Slide 35: Schedule
Prototype
  FDR 10/11/15
  Build to start 10/2/16
  Delivery July 16
Production Units
  PDR 10/11/15
  Beam pipe build to start 8/8/16
  LWU Build to Start 1/2/17
Notes: Prototype 2 - FDR 14/7/16