## Slide 1: Spallation
Eric Pitcher
Head of Target Division
www.europeanspallationsource.se
February 19, 2016

## Slide 2: Outline
Preliminaries
  Units of energy and length
  Basic nuclear physics
  Length scales and wavelengths
Spallation physics
  Intranuclear cascade
  Evaporation
Spallation neutron sources
  Neutron production
  Neutron thermalization
  Energy balance
  Radiation shielding

## Slide 3: Units of energy
Electron-volt: eV 1 eV = 1.6×10–19 joules 1 MeV = 1.6×10–13 joules 1 GeV = 1.6×10–10 joules
Binding energy of the electron in a H atom ~10 eV
Binding energy of a neutron in a nucleus ~10 MeV
Nuclear forces are about a million times greater than atomic forces.

## Slide 4: To understand spallation, we need to start with some basic nuclear physics
The nucleus of an atom is a collection of neutrons and protons bound together by the strong nuclear force
Neutrons and protons bound together within a nucleus are called nucleons
Each nucleon is bound to the nucleus with a binding energy of about 8 MeV
A hadron is a class of sub-atomic particle to which neutrons and protons belong

## Slide 5: Length scales and wavelengths
DeBroglie wavelength λ = h/p h = the Planck constant p = particle momentum
A particle’s interaction length is on par with its wavelength
Wavelength of a 25-meV “thermal” neutron = 2 Å (same scale as the atomic spacing in a crystal lattice)
Wavelength of a 200-MeV proton = 2 fm (close to the distance between nucleons in a nucleus)

## Slide 6: Nuclear spallation
Spallation is a nuclear reaction whereby a high-energy hadron strikes a nucleus and imparts energy to the nucleus, leading to the emission of a number of nucleons from it
Spallation proceeds in two stages:
second stage: evaporation
first stage: intranuclear cascade

## Slide 7: First stage: intranuclear cascade Reaction probability
When passing through matter, a 200-MeV hadron with a 2-fm wavelength interacts only with individual nucleons within a nucleus
The probability of a spallation reaction occurring depends only on the average density of nucleons and not on nuclear properties.
Material | Nucleon density (per cm3)
Water | 0.6 x 1024
Aluminum | 1.6 x 1024
Tungsten | 11.5 x 1024
Mercury | 8.1 x 1024

## Slide 8: First stage: intranuclear cascade Reaction outcome
The incident hadron transfers a fraction of its kinetic energy to the struck nucleon
The hadron-nucleon interaction may:
  Transfer energy to the nucleus as a whole through subsequent interactions with neighboring nucleons, leaving the nucleus in a highly excited state
  Produce pi mesons as reaction products
  Eject the energetic and forward directed nucleon from the nucleus
first stage: intranuclear cascade

## Slide 9: Second stage: evaporation
The highly excited nucleus “boils” off nucleons, mostly neutrons, or clusters of nucleons as nuclei and hydrogen and helium atoms
For each nucleon emitted, the nucleus de-excites by the binding energy of the nucleon, which is about 8 MeV
Each emitted neutron has 2 or 3 MeV kinetic energy
These evaporation particles are emitted nearly isotropically
second stage: evaporation

## Slide 10: Neutron thermalization: Slowing down energetic neutrons
Most neutrons produced via spallation have kinetic energies of a few MeV for which the deBroglie wavelength is 10 to 20 fm
For neutron scattering applications, neutrons need wavelengths in the range of 1 to 30 Å  energies of 1 to 80 meV
Spallation neutrons must be slowed by nine orders of magnitude in energy
Energy distribution of neutrons produced via spallation by 1.7-GeV protons on tungsten

## Slide 11: Spallation sources: Potential applications
Neutron scattering research
Nuclear waste transmutation / energy production
Isotope production
  Rare isotopes for nuclear physics research
  Medical isotopes
  Research isotopes
Neutron source for nuclear physics research and nuclear cross section measurement
Irradiation facility for radiation damage studies

## Slide 12: Neutron production versus beam energy
After a few hundred MeV, neutron production is linear with energy up to a few GeV
Some loss occurs at high energies for finite-sized targets
Neutron production versus beam energy for a 50-cm-diam by 200-cm-long tungsten cylinder bombarded on axis by protons.

## Slide 13: Neutron production versus beam power
From 1 – 3 GeV, neutron production is linear with beam power and independent of beam energy

## Slide 14: Proton passage through matter
Due to their electric charge, protons lose energy as they pass through matter due to interactions with bound electrons
Bragg peak at the end of the track is prominent at low energy
Protons are also removed from the beam through nuclear interactions

## Slide 15: Energy Balance
Spallation is an endothermic reaction: A portion of the proton beam’s kinetic energy is converted to mass
Mass conversion is equal to the amount of energy that goes into releasing neutrons from the nucleus
For the ESS operating at 5 MW beam power, Heating of structures 4.0 MW Conversion to mass 0.9 MW  At full power, target station increases Neutrinos 0.1 MW in mass by 0.2 mg/year

## Slide 16: Neutron thermalization: The Maxwell-Boltzmann distribution
Neutron thermalization is the process of reaching thermodynamic equilibrium with the scattering medium
We use hydrogenous media to slow and thermalize neutrons
  Water at ~room temperature (300 K)  thermal moderator
  Liquid hydrogen at cryogenic temperature (20 K)  cold moderator
A neutron can transfer nearly all of its energy to a hydrogen nucleus in a single collision
It takes typically 15 to 25 collisions with hydrogen to slow a 2-MeV neutron to near thermal energy

## Slide 17: The target station produces neutrons, slows them, and leaks them to neutron guides
tungsten target
2-GeV proton
Beryllium reflects neutrons that might otherwise escape, boosting performance by a factor of 5
Liquid hydrogen
moderator at 20 K
produces about 60 neutrons per proton ≈ 1018 neutrons per second
neutron guide (start of the neutron scattering instrument)
conversion efficiency ~ 10–5
cold neutrons

## Slide 18: Shielding a spallation source
High-energy neutrons have a relatively small probability of interaction (denoted by σT) with matter

## Slide 19: High-energy neutrons are not only penetrating, they cause high dose
Source: D. Filges and F. Goldenbaum, Handbook of Spallation Research, Wiley-VCH, 2009.

## Slide 20: Concrete is most effective for shielding low-energy neutrons
Source: D. Filges and F. Goldenbaum, Handbook of Spallation Research, Wiley-VCH, 2009.

## Slide 21: Practical solution for shielding a spallation source: Lots of steel and concrete
Steel effectively attenuates high energy neutrons and gammas
Concrete attenuates lower energy neutrons but creates gammas in the process
Often, laminated shields of steel and concrete are most effective
Dose as a function of depth in a 1.5-m-thick iron shield followed by 50 cm of concrete. The source is a pencil beam of 600-MeV protons normally incident on the iron slab.

## Slide 22: Radioactivity and Decay Heat
Radioactivity is a byproduct of the spallation process
The emitted particles, mostly betas and gammas, deposit heat in the radioactive material and surrounding structures

## Slide 23: For further reading on spallation and spallation neutron sources
D. Filges and F. Goldenbaum, Handbook of Spallation Research, Wiley-VCH, 2009.

## Slide 24: Thanks for your attention!