## Slide 1: Neutron Instruments I: Sources and Basics
Ken Andersen
ESS Engineering Lectures
22nd February 2016

## Slide 2: Summary
Neutron facilities
  overview & trends
Reactor-based sources
Fission vs Spallation
Neutron source time structure
  the time of flight method
Long-pulse neutron sources

## Slide 3: Main European neutron sources 2016
ISIS
ILL
LLB
TUD
HZB
FRM2
PSI
BNC
JEEP-II

## Slide 4: Major neutron sources in the world
ILL (F) |  |  | 
HZB (D) |  |  | 
LLB (F) |  |  | 
PSI (CH) |  |  | 
FRM-II (D) |  |  | 
HFIR (USA) |  |  | 
NIST (USA) |  |  | 
JRR-3 (J) |  |  | 
PIK (RU) |  |  | 
IBR-2/2M (RU) |  |  | 
ISIS-1 (UK) |  |  | 
ISIS-2 (UK) |  |  | 
LANSCE (USA) |  |  | 
SNS (USA) |  |  | 
J-PARC (J) |  |  | 
ESS (SE) |  |  | 
2000
2010
2020
Continuous
Pulsed

## Slide 5: Major neutron sources in the world
ILL (F) | X |  | X | 
HZB (D) | X |  | X | 
LLB (F) | X |  | X | 
PSI (CH) |  | X | X | 
FRM-II (D) | X |  | X | 
HFIR (USA) | X |  | X | 
NIST (USA) | X |  | X | 
JRR-3 (J) | X |  | X | 
PIK (RU) | X |  | X | 
IBR-2/2M (RU) | X |  |  | X
ISIS-1 (UK) |  | X |  | X
ISIS-2 (UK) |  | X |  | X
LANSCE (USA) |  | X |  | X
SNS (USA) |  | X |  | X
J-PARC (J) |  | X |  | X
ESS (SE) |  | X |  | X
Fission/Spallation
Continuous/Pulsed

## Slide 6: The first neutron source
James Chadwick:
used Polonium as alpha emitter on Beryllium

## Slide 7: Evolution of neutron sources
Berkeley 37-inch cyclotron
350 mCi
Ra-Be source
Chadwick
1930
1970
1980
1990
2000
2010
2020
105
1010
1015
1020
1
1940
1950
1960
Thermal flux n/cm2-s
(Updated from Neutron Scattering, K. Sköld and D. L. Price, eds., Academic Press, 1986)

## Slide 8: Nuclear Fission

## Slide 9: Evolution of neutron sources
Berkeley 37-inch cyclotron
350 mCi
Ra-Be source
Chadwick
1930
1970
1980
1990
2000
2010
2020
105
1010
1015
1020
1
ILL
X-10
CP-2
Reactor Sources
HFBR
HFIR
NRU
MTR
NRX
CP-1
1940
1950
1960
Thermal flux n/cm2-s
(Updated from Neutron Scattering, K. Sköld and D. L. Price, eds., Academic Press, 1986)

## Slide 10: Evolution of neutron sources
Berkeley 37-inch cyclotron
350 mCi
Ra-Be source
Chadwick
1930
1970
1980
1990
2000
2010
2020
105
1010
1015
1020
1
ILL
X-10
CP-2
Reactor Sources
HFBR
HFIR
NRU
MTR
NRX
CP-1
1940
1950
1960
Thermal flux n/cm2-s
(Updated from Neutron Scattering, K. Sköld and D. L. Price, eds., Academic Press, 1986)
FRM-II

## Slide 11: Nuclear Spallation

## Slide 12: Evolution of neutron sources
Berkeley 37-inch cyclotron
350 mCi
Ra-Be source
Chadwick
1930
1970
1980
1990
2000
2010
2020
105
1010
1015
1020
1
ISIS
Pulsed Sources
ZINP-P
ZINP-P/
KENS
WNR
IPNS
ILL
X-10
CP-2
Steady State Sources
HFBR
HFIR
NRU
MTR
NRX
CP-1
1940
1950
1960
Thermal flux n/cm2-s
(Updated from Neutron Scattering, K. Sköld and D. L. Price, eds., Academic Press, 1986)
FRM-II
SINQ
SNS
J-PARC

## Slide 13: Evolution of neutron sources
Berkeley 37-inch cyclotron
350 mCi
Ra-Be source
Chadwick
1930
1970
1980
1990
2000
2010
2020
105
1010
1015
1020
1
ISIS
Pulsed Sources
ZINP-P
ZINP-P/
KENS
WNR
IPNS
ILL
X-10
CP-2
Steady State Sources
HFBR
HFIR
NRU
MTR
NRX
CP-1
1940
1950
1960
Thermal flux n/cm2-s
(Updated from Neutron Scattering, K. Sköld and D. L. Price, eds., Academic Press, 1986)
FRM-II
SINQ
SNS
J-PARC
ESS

## Slide 14: Slow Neutrons vs Light
 | light | neutrons
λ | < μm | < nm
E | > eV | > meV
penetration | ~ μm | ~ cm
θc | 90° | 1°
B | 1018 p/cm2/ster/s (60W lightbulb) | 1014 n/cm2/ster/s (60MW reactor)
spin | 1 | ½
interaction | electromagnetic | strong force, magnetic
charge | 0 | 0

## Slide 15: Why neutrons?
Thermal neutron have wavelengths similar to inter-atomic distances
Thermal neutrons have energies comparable to lattice vibrations
Neutrons are non-destructive
Neutrons interact weakly
  they penetrate into the bulk
Neutrons interact via a simple point-like potential
  amplitudes are straightforward to interpret
Neutrons have a magnetic moment
  great for magnetism
Neutrons see a completely different contrast to x-rays
  e.g. hydrogen is very visible

## Slide 16: Why neutrons?
100 keV

## Slide 17: ILL Reactor Neutron Source
Highly-enriched uranium
Compact design for high brightness
Heavy-water cooling
Single control rod
57MW thermal power
Cold, thermal, hot sources
2 m

## Slide 18: ILL Reactor Neutron Source
 | cold | thermal | hot
moderator | liquid D2 | Liquid D2O | graphite
moderator temperature | 20K | 300K | 2000K
neutron wavelength | 3→20Å | 1→3Å | 0.3→1Å
Highly-enriched uranium
Compact design for high brightness
Heavy-water cooling
Single control rod
57MW thermal power
Cold, thermal, hot sources
2 m

## Slide 19: ILL Reactor Neutron Source
1st guide hall
(20 instruments)
2nd guide hall
(7 instruments)

## Slide 20
ILL Reactor Neutron Source

## Slide 21
ILL Reactor Neutron Source
VCS
HCS
Thermal beam tubes
HS

## Slide 22: ILL Moderator Brightnesses

## Slide 23: Spallation Sources
Spallation: 10x higher neutron brightness per unit heat
1 MW spallation source = 10 MW reactor
  e.g. 800 MeV at 1.25 mA (PSI)
  e.g. 3 GeV at 0.4 mA (J-PARC)
Peak brightness >> time-average brightness
log(Intensity@λ=5Å)
0 20 40 60 80 100 120
time (ms)
1
0.1
ISIS-TS1 128kW
100μs
0
ILL 57MW

## Slide 24: Spallation Sources
Spallation: 10x higher neutron brightness per unit heat
1 MW spallation source = 10 MW reactor
  e.g. 800 MeV at 1.25 mA (PSI)
  e.g. 3 GeV at 0.4 mA (J-PARC)
Peak brightness >> time-average brightness
log(Intensity@λ=5Å)
0 20 40 60 80 100 120
time (ms)
1
0.1
ISIS-TS1 128kW
100μs
0
ILL 57MW
ISIS-TS2 32kW

## Slide 25: Spallation Sources
Spallation: 10x higher neutron brightness per unit heat
1 MW spallation source = 10 MW reactor
  e.g. 800 MeV at 1.25 mA (PSI)
  e.g. 3 GeV at 0.4 mA (J-PARC)
Peak brightness >> time-average brightness
log(Intensity@λ=5Å)
0 20 40 60 80 100 120
time (ms)
1
0.1
ISIS-TS1 128kW
ISIS-TS2 32kW
ILL 57MW
ESS 5MW
long pulse
3ms

## Slide 26: De Broglie Relations
Particle | Wave

## Slide 27: The Time-of-Flight (TOF) Method
distance
time

## Slide 28: ISIS Spallation Source
ISIS, UK (160kW)

## Slide 29: SNS, Oak Ridge, USA (1MW)

## Slide 30: J-PARC, Tokai, Japan (500kW)

## Slide 31: J-PARC, Tokai, Japan (500kW)

## Slide 32: ESS, Lund, Sweden (5MW in 2025)

## Slide 33: ESS target
2.5m tungsten wheel

## Slide 34: ISIS TS2 Target
Target: 66mm W

## Slide 35: Target-Reflector-Moderator Neutronics
Target produces neutrons in > MeV range
Moderators contain H to thermalise neutrons
  largest scattering cross-section (80b)
  lower mass: same as neutron
  on average, ½ energy lost per collision
  100 MeV -> 10 meV requires about 25 collisions
Moderators embedded in reflector, usually D2O-cooled Be
  minimal absorption
  large scattering cross-section (8b)
  little thermalisation

## Slide 36: Target-Reflector-Moderator Neutronics
Be
Target plane
Target
protons in

## Slide 37: Target-Reflector-Moderator Neutronics
protons in
Be
10cm above/below Target

## Slide 38: Target-Reflector-Moderator Neutronics
protons in
Be
10cm above/below Target

## Slide 39: Target-Reflector-Moderator Neutronics
protons in
Be
10cm above/below Target

## Slide 40: Target-Reflector-Moderator Neutronics
0
100μs
200μs
protons in
Be
10cm above/below Target

## Slide 41: Target-Reflector-Moderator Neutronics
Cd
0
100μs
200μs
Cadmium absorption
Decoupling
protons in

## Slide 42: Target-Reflector-Moderator Neutronics
Cd
0
100μs
200μs
Cadmium absorption
Decoupling

## Slide 43: Target-Reflector-Moderator Neutronics
Cd
0
100μs
200μs
Cadmium absorption
Gd
Decoupling
Poisoning
Gadolinium absorption

## Slide 44: Time-of-flight (TOF) resolution
distance
time
Δt

## Slide 45: Time-of-flight (TOF) resolution
distance
time
Δt

## Slide 46: Moderator Decoupling and Poisoning
Peak Structure at 5meV
Coupled
Decoupled
Poisoned
J-PARC H2 moderators at 1MW

## Slide 47: Moderator Decoupling and Poisoning
Intensity
λ=1Å
λ=2Å
λ=5Å
0 100 200 300
time (μs)

## Slide 48: SNS moderators
decoupled poisoned H2
coupled H2
coupled H2
decoupled poisoned H2O
Top
Bottom
20 cm

## Slide 49: ISIS TS2 Target
coupled solid CH4
coupled H2
decoupled poisoned solid CH4

## Slide 50: Moderator Temperature
ISIS-TS1 moderators at 160kW

## Slide 51: Long-pulse performance
4
time (ms)
Brightness (n/cm2/s/sr/Å)
x1013
ISIS TS1
128 kW
ISIS TS2
32 kW
SNS
1-2 MW
JPARC
0.3-1 MW
ILL 57 MW
ESS 5 MW
2015 design
0
1
2
3
15
5
10
λ = 5 Å
Possibilities of pulse shaping

## Slide 52: Thank You!