## Slide 1: NMX uTPC detector overview and algorithms
01.02.2016
Dorothea Pfeiffer

## Slide 2: NMX detectors

## Slide 3: Gd-GEM backwards setup
neutron
conversion electron
Start of track

## Slide 4: α particle and electron tracks
Whereas α particles leave straight tracks, conversion electrons from Gd leave curvy track
Centroid calculation not sufficient to determine position
α particle track from 10B4C
electron track from Gd

## Slide 5: Tracking algorithms
Used for 10B4C

## Slide 6: Tracking algorithms
Analog chip like APV (development option)
  Best results in determining the start of the track are obtained with last-local-maximum algorithm: start of the track is the strip with the latest local maximum
  Falling-flank or global-maximum possible but lead to slightly worse results
Digital chip like VMM3 (base line):
  Available modes:
    TtP (threshold to peak)
    ToT (time over threshold)
    PaP (pulse at peak) = global maximum
    PtT (peak to threshold)
  When chips and data available, modes have to be evaluated
  Suitable task here to get involved in!!
=> In general: per strip one time stamp and one amplitude

## Slide 7: Reconstruction of start of track
Reconstruction of start of tracks in x and y
Cathode of 250 um of Gadolinium

## Slide 8: Position resolution
Position resolution: σ <= 350 um
Scattering spread: σ ≈ 175 um
Divergence of beam: σ ≈ 1700 um
Region | σ [μm] | +/- error [μm]
1 (Tape) | 248 | 20
2 (Tape) | 341 | 22
3 (Tape) | 320 | 21
4 (Tape) | 242 | 17
5 (Beam) | 1542 | 46
6 (Beam) | 1949 | 58
7 (Beam) | 2053 | 55
8 (Beam) | 2312 | 72
9 (Beam) | 1924 | 54
10 (Beam) | 2417 | 100

## Slide 9: Natural Gadolinium (baseline)
Baseline:
Backwards and forwards mode:
Optimum thickness 6 um. Thinnest available foil 10um:
20% efficiency at 1.8 A
Alternative:
Backwards mode, one detector:
Optimum thickness 50 um or greater:
14% efficiency at 1.8 A
neutron
Backwards detector
Forwards detector
Gd
e-
e-

## Slide 10: Comparison of baseline and upgrade
 | Gd | 1.8A | 3.5A | 157 Gd | 1.8 A | 3.5A
1 readout backwards, foil | 100 um | 14% | 20% | 10 um | 31% | 36%
2 readouts, freestanding foil | 10 um | 20% | 28% | 10 um | 38% | 42%
One readout:
Cheaper
mechanically simpler (thicker foil, foil can be supported)
less efficient
Two readouts (base line):
Expensive
mechanically complicated (freestanding 10 um thin foil)
rare cases where electrons from one neutron are detected in both detectors (which position is taken ?)
more efficient

## Slide 11: Electronics per detector
3 detectors (60 cm x 60 cm)
One readout: 4 modules (30 cm x 30 cm) per detector, two readouts 8 modules (30 cm x 30 cm)
24 chips per module
24*4*3 = 288 chips or 576 chips for two readouts
64 channels per chip
288* 64= 18432 channels or 576*64 = 36864 channels for two readouts
McSTAS simulations (diffraction spots) needed for module size
and rate calculation !

## Slide 12: Data before uTPC algorithm
Per hit/strip (raw data):
VMM3 data: up to 38 bits (depending on exact mode)
Channel-ID
Amplitude (10 bit)
Time stamp (12 bit)
Per neutron (intermediate data):
Average: 10 strips in x, 10 strips in y (3.8 kBit)
VMM3 data decoded into:
  Strip ID (16 bit): Detector number (0-2), Module number (0-7), chip number (0-24), strip number (0-63)
  Amplitude (10 bit), Time stamp (12 bit)
Clustering (also over several chips) has to be studied!
Exact data length/definition depends on chip type!

## Slide 13: Data after uTPC algorithm
Per neutron (processed data):
Strip x, strip y, time (44 bit):
  Strip ID (16 bit): Detector number (0-2), Module number (0-7), chip number (0-24), strip number (0-63)
  Time stamp (12 bit)
Data rate:
VMM3: 0.9 MHz maximum rate per channel with a multiplicity of 4.7 strip
Less for our multiplicity of 10 strips, realistically let’s assume 1 0 MHz per chip due buffer and readout
Simulations needed to deduce real rate and architecture