## Slide 1: EPICS Heartbeat Extension for PV Monitoring at the CLS
Michael Bree
Control Systems Engineer
Canadian Light Source

## Slide 2: PV Monitor Motivation
Quick Diagnosis
  - Common Problem: Lost PV!
  - Which IOC/App is responsible?
Reactive --> Proactive
  - Monitor system health
Notes: Why Monitor PVs?

## Slide 3
Poll
Generate CA_PROTO_SEARCH
Monitor
CA_PROTO_SEARCH
Generate PV List
Acquire Client Statistics
Determine PV Server & Status

## Slide 4: PV Polling Issues
Inefficient
Slow to detect PV status changes
Must poll all PVs to get accurate status
Difficult to map PVs to Beacons; Beacons to Apps
  Beacon ports change,
  PVs appear, move, disappear, etc.

## Slide 5: EPICS Heartbeat
An “enhanced beacon” added to App
  - Does not replace beacon
Addresses all polling issues:
  - Efficient & Fast – No polling
  - Real-time status of all PVs
  - Real-time status of all Apps
Maps PVs to Apps:
  - No crawling, no grepping, no macros

## Slide 6
E
Poll
Generate CA_PROTO_SEARCH
Monitor
CA_PROTO_SEARCH
Generate PV List
Acquire Client Statistics
Determine PV Server & Status
EPICs Heartbeat
Generate Complete PV List
Map PVs to Apps

## Slide 7: Heartbeat Format
UDP broadcast every 30 seconds
JSON String with:
  - EPICs App command line args – to identify App
  - Sequence Number
  - App Uptime
  - Host System Time
  TCP Port
API (Get PV List)

## Slide 8: Example - Add to EPICs App

## Slide 9: Example - Process Heartbeats

## Slide 13: Heartbeat API
UDP (simple - fast - extensible)
Query: Four 32-bit fields:
  Last Heartbeat Sequence Number
  Handle
  Command (CMD.PV_LIST = 0x4DA3F927)
  - Command Specific (e.g., PV List Offset)
Response: JSON string with:
  10 PV names from specified offset
  Handle (from Query)

## Slide 14: Example - Query PV List

## Slide 15: Conclusion
Makes PV Monitor Fast, Efficient, Complete (All PVs)
Maps PVs to Apps with no crawling/grepping/macros
Extreme Simplicity.... Not restricted to PV Monitor
  - Beamline Lead can easily display status of their Apps/PVs
  - GUI can display status of Apps upon which it depends