## Slide 1: Embedding Matlab Codes into the EPICS server
Pavel Chevtsov, Paul Scherrer Institute
Miroslaw Dach, M. Dach Consulting GmbH
Trivan Pal, Paul Scherrer Institute
M.Dach Consulting GmbH

## Slide 2
The objective of this presentation is to discuss the way how to enrich EPICS servers with mathematical capabilities of Matlab.

## Slide 3: Close loop control in EPICS env.
EPICS server
Channel “Ch:IN1”
Channel “Ch:IN2”
Chan. “Ch:OUT1”
Chan. “Ch:OUT2”
Sensors
Actuators
Basic Calculation

## Slide 4: Typical use of Matlab in EPICS env.
Matlab program
Algorithm
caget “Ch:IN1”
caget “Ch:IN2”
EPICS server
Chan. “Ch:OUT1”
Chan. “Ch:OUT2”
Sensors
Actuators
Basic Calculation
Channel “Ch:IN1”
Channel “Ch:IN2”
caput “Ch:OUT1”
caput “Ch:OUT2”
Internet

## Slide 5: Goal to achieve
Matlab program
EPICS server
Chan. “Ch:OUT1”
Chan. “Ch:OUT2”
Sensors
Actuators
Channel “Ch:IN1”
Channel “Ch:IN2”
Algorithm
caget “Ch:IN1”
caget “Ch:IN2”
caput “Ch:OUT1”
caput “Ch:OUT2”
Matlab Algorithm
Internet

## Slide 6: Main idea is to:
make use of EPICS aSub (formerly GenSub) record with the original MATLAB program converted to “c” code.

## Slide 7
The aSub Record is a custom record, which requires for operations a user defined function. The function acts on data coming from Inputs links and places calculation results into output links.
User defined Function
aSub record
Input links
Output links

## Slide 8
To realize the idea, an automatic procedure was developed.
The procedure is implemented in 3 steps:
MATLAB program pre-processing
MATLAB program to “C” code conversion
“C” code post-processing

## Slide 9
1. MATLAB program pre-processing:
Analyses the MATLAB program and extracts the names of all EPICS channels used by caget and caput function calls.
caget Inputs:
Ch:IN1 Ch:IN2
caput Outputs:
Ch:OUT1 Ch:OUT2

## Slide 10
1. MATLAB program pre-processing:
Connects at run time to EPICS server(s) and collects the information about record types and number of elements for all EPICS channels used in MATLAB program.
caget Inputs:
Names
Ch:IN1 Ch:IN2
Type Nr.
Double 1 Long 100
caput Outputs:
Names
Ch:OUT1 Ch:OUT2
caput Outputs:
Names Type Nr
Ch:OUT1 Long 1 Ch:OUT2 Long 1

## Slide 11
1. MATLAB program pre-processing:
Generates automatically EPICS DB with aSub record configuration
record (aSub,”$(NAME):GENSUB”){ field(INAM,”myTest_CInit”) field(SNAM,”myTest_CProcess”) field(INPA,”Ch:IN1”) field(FTA,”DOUBLE”) field(NOA,”1”) : }

## Slide 12
1. MATLAB program pre-processing:
Generates startup.script to load EPICS DB
require “myTest8_C” “test” dbLaodTemplate(“myTest8_C.subs”)

## Slide 13
1. MATLAB program pre-processing:
Substitutes in MATLAB code caget and caput function calls with equivalent “C” entries
IX=caget(‘Ch:IN1’);
IX=struct(‘val’,zeros(1,1,’double’); coder.ceval(‘myCaGetCh__IN1’,coder.ref(IX));

## Slide 14
2. MATLAB program to “C” code conversion
MATLAB coder converts pre-processed MATLAB code to “C”.

## Slide 15
3. “C” code post-processing
“C” generated code is parsed and all caget and caput function calls are substituted with suitable aSub record input and output links

## Slide 16
3. “C” code post-processing
Make file to build user defined function for aSub record use is generated
[optionally] User defined function is compiled (cross-compiled) and installed in the default place (PSI require function specific)
[optionally] EPICS DB which contains aSub record config. and corresponding startup.scritp is installed to the IOC boot location

## Slide 17
How it works in practice
From user’s point of view all steps described previously are transparent and are governed by the automatic procedure.

## Slide 18
Creating myTest8_C.m based on myTest8.m Inserting functions name myTest8_C Examining EPICS server(s) to substitute caget calls Examining EPICS server(s) to substitute caput calls Substituting caget and caput with coder.ceval entries 1. myTest8.m -> myTest8_C.m [READY] 2. myTest8_C.subs [READY] 3. myTest8_C.template [READY] Starting Matlab ver. 2015a with the command: codegen -config:lib -report myTest8_C Please be patient it can take a while Matlab coder has generated "c" code myTest8_C.c successfully Generating EPICS aSub record header and dbd files: 1. codegen/lib/myTest8_C/myTest8_CInit.c [READY] 2. codegen/lib/myTest8_C/myTest8_C.dbd [READY] 3. codegen/lib/myTest8_C/Makefile [ c -> compile | ENTER -> exit ]
coderProcessing.sh myTest8.m
[dach@localhost]$

## Slide 19
MATLAB FFT Algorithm
PC/Linux client
IOXOS/Linux EPICS srv.
Channel “CH:WF_IN1”
Channel “CH:WF_OUT1”
EPICS DB
Simple Example

## Slide 20
record(waveform,”CH:WF_IN1”){ field(NELM,”1024”) field(FTVL,”DOUBLE”)
}
record(waveform,”CH:WF_OUT1”){ field(NELM,”1024”) field(FTVL,”DOUBLE”)
}
PC/Linux client
IOXOS/Linux EPICS srv.
record(aSub,”CH:GENSUB”){ field(INAM,”myFFT_CInit”) field(SNAM,”myFFT_CProc”) field(INPA,”CH:WF_IN1”) field(FTA,”DOUBLE”) field(NOA,”1024”) field(OUTA,”CH:WF_OUT1”) field(FTVA,”DOUBLE”) field(NOVA,”1024”)
}
myFFT_C.m
myFFT_C.c
coderProcessing myFFT.m
myFFT_C.m
myFFT.m
myFFT_C.so

## Slide 21
record(waveform,”CH:WF_IN1”){ field(NELM,”1024”) field(FTVL,”DOUBLE”)
}
record(waveform,”CH:WF_OUT1”){ field(NELM,”1024”) field(FTVL,”DOUBLE”)
}
PC/Linux client
IOXOS/Linux EPICS srv.
myFFT.m
myFFT_C.so
Channel “CH:WF_IN1”
Channel “CH:GENSUB”
Channel “CH:WF_OUT1”
IOXOS/Linux EPICS srv.
EPICS DB
Channel “CH:WF_IN1”
Channel “CH:WF_OUT1”
EPICS DB

## Slide 22
Conclusions
The procedure is automatic but not all MATLAB functions could be converted to “C” code.

## Slide 23
Real Applications
Normalization algorithm for Beam Arrival Monitor.
It was originally implemented and tested in Matlab environment.
Finally it was converted to „c” and bound to EPICS server.
It runs in the close loop at 100Hz. The CPU load is 8%.

## Slide 24
Thank you for your attention