## Slide 1: Introduction to the ESS Integrated Control Systems
Henrik Carling
ESS/ICS
Date: 2016-06

## Slide 2: What is ICS about?
The ESS facility is a large and complex machine with very, very much equipment that needs to work in synchronization - and with well-known configurations
For this purpose almost all equipment at the ESS facility is connected to the Integrated Control System
The control system is the ”central nervous system of ESS”
Examples:
  Voltage supplies for magnets
  Vacuum systems
  Cryogenic equipment
  RF equipment
  Air conditioning in the tunnel
An estimated 1.5 million control points will be needed

## Slide 3: ICS Project scope
Work package 01 Management and administration
Work package 02 Software Applications
Work package 03 Software core
Work package 04 Hardware core
Work package 05 Machine protection
Work package 06 Equipment
Work package 07 Control system infrastructure
Work package 08 Physics
Work package 09 Personnel safety systems
Work package 10 Integration - Accelerator
Work package 11 Integration - Target
Work package 12 Integration - Instruments
Work package 13 Integration - Conventional facilities
Work package 14 Test Stands
Work package 20 Installation
Software
Electronics
Infrastructure
Safety & protection

## Slide 4: Technology scope for ICS
The span of technical scope and the competencies needed in ICS is enormous
From analog signals to Java-based high-end, big-data GUI:s in high performance, high availability
PLC systems
Safety and protection systems
Infrastructure: networking, data centre, control room
Systems integration, Installation
Project management and administration
Electronics hardware
Software
PLC
Infrastructure
Analog electronics
Digital electronics
FPGA firmware
Digital communication
PCB, packaging
Test and validation
Industrialization, maintenance
Kernel drivers
Operating systems (RT)
Development environments
EPICS
CSS/Eclipse
Applicatoins (GUI, Web, Services)
Databases
Availability, performance
Test and validation
Safety and protection

## Slide 5
ESS ERIC BOARD OF DIRECTORS DIRECTOR GENERAL
MACHINES DIRECTORATE
SCIENCE DIRECTORATE
ACCELERATOR
TARGET
PROJECT SUPPORT & ADMINISTRATION DIRECTORATE
Communication
Operations, ES &H and QA
CONVENTIONAL FACILITIES
HUMAN RESOURCES
GENERAL SERVICES
SCIENTIFIC PROJECTS
SCIENTIFIC ACTIVITIES
NEUTRON TECHNOLOGIES
NEUTRON INSTRUMENTS
INTEGRATED CONTROL SYSTEM
SYSTEMS ENGINEERING
DATA MANAGEMENT SOFTWARE CENTRE
ENGINEERING & INTEGRATION SUPPORT
COMMUNICATIONS & EXTERNAL RELATIONS
FINANCE
INFORMATION TECHNOLOGY
LEGAL
SUPPLY, PROCUREMENT & LOGISTICS

## Slide 6: ICS Organization 2016-05-01
Henrik Carling
Division head
Anna Gillberg
Team assistant
Annika Nordt Safety and protection
Daniel Piso
Hardware and integration
Hector Novella
Deputy project manager
Susanne Regnell
Control Software
Timo Korhonen Chief engineer
Emanuele Laface
Accelerator physicist
Karin Rathsman Senior scientist
Leandro Fernandez Senior software engineer
Ricardo Fernandes Senior software engineer
Claudio Rosati
Software engineer
Javier Cerejo PhD Student
Angel Monera
FPGA Engineer
Denis Paulic
PLC Engineer
Manuel Zaera-Sanz
PLC Engineer
Morteza Mansouri
Safety Engineer
Riccard Andersson PhD student
Stuart Birch Senior safety engineer
Ben Folsom
PhD student
Remy Mudingay Infrastructure engineer
Thilo Friedrich
PhD Student
Temporary employee
Employee
Consultant
Consultant off-site
Nick Levchenko
Integrator
Benedetto Gallese
Integrator
Yong Kian Sin IEC61508 engineer
?
Deputy chief engineer
(Vacant)
François Bellorini
Integrator
David Brodrick
Integrator
?
IT/Infrastructure ?
(Vacant?)
Position under consideration
Vacant Engineer?
Vacant Engineer?
Vacant Engineer?
Vacant Engineer?
Alexander Söderqvist
Integrator
Niklas Claesson Integrator
Jeong Han Lee Integrator
Consultants
Vacant Engineer?
Vacant Engineer?
Julen Etxeberria
Intern
Vacant
Software engineer

## Slide 7: ICS - construction phase value envelope (tentative)
The ICS value envelope for the construction phase shows the aggressive project schedule
A majority of the ICS value is labor based effort (i.e. not equipment)
The ICS estimated headcount envelope reveals large in-kind/supplier opportunities
2016 2017 2018 2019

## Slide 8: ESS In-kind Goals
Chart: 
| Controls | Target | Instruments (NSS) | Accelerator
IKC | 36.5 | 101 | 228 | 382
Cash | 36.5 | 54 | 122 | 128
€ 510 M
€ 350 M
€ 155 M
€ 73 M
Construction cost: € 1.84 Billion
In-kind: € 747.5 Million
M€
ICS

## Slide 9: ICS In-kind partners
Agreement signed
Agreement waiting for signature
Early discussions
Collaboration agreement
Partner Institutes
Atomki, Hungary
CEA, France
CNRS, France
Elettra, Italy
ESS Bilbao, Spain
IFE, Norway
INFN Catania, Italy
INFN Legnaro, Italy
PSI, Switzerland
Tallinn Technical University, Estonia
ÚJV Řež, Czech Republic
University of Łódź , Poland
Uppsala University, Sweden
ZHAW, Switzerland
Notes: Projects can put small dots wherever they have a partner.

## Slide 10: Commercial procurements within ICS
The overwhelming majority of value within ICS’s scope is represented as manual labor
Over the construction phase we see a strong need for skilled personnel to be recruited, in-kinded and contracted for work within ICS
We see a strong need to fill transient positions with consultants
  New framework agreements are being created for
    Software development services ~5 M€ Closed
    Hardware development services (electronics) ~1.2 M€ Q2 2016
    PLC programming services ~2.9 M€ Q3 2016
    ”Integration” >4 M€ Q2 2016
The ICS equipment procurement plan is still realtively immature - to be presented in break-out sessions

## Slide 11
ICS SOFTWARE ACTIVITIES

## Slide 12: Software team scope description
Controls configuration tools
  Controls Configuration Database (CCDB)
  Naming Server for naming convention
  Cable Database (CDB)
  IOC Factory
  CS Entry
  Role Based Access Control (RBAC)
Clients
  Alarm Handling
  E-logbook
  Archiving System
  Save, Compare & Restore
  Scenario management
  GUI/HMI (Control System Studio)
Core controls software
  Development/contributions to core EPICS
  Timing applications
  Post-mortem diagnostics
Physics modelling
  Open XAL
  ESS Linac Simulator
  Beam Physics Applications
Operation tools – Scripting frameworks
  iPython
  Scripting Execution Environment
  Macroserver
Software development environment
  Vagrant for virtualization
  Ansible for automation of deployment and configuration of our software infrastructure
  Jenkins for continuous integration support

## Slide 13: Software team status
The software scope is being reworked
When the scope definition has matured, we believe that significant parts of the software development scope can be packaged for in-kind contributions
A call for tender for software development services is ongoing
Collaboration within open communities are very important for ICS going forward.

## Slide 14
ICS Hardware platforms

## Slide 15: Three layer strategy - control systems at ESS
ICS has adopted a three layer strategy for implementing the control system based on signal speed
  A custom made platform based on microTCA for applications with data acquisition exceeding 100 kHz
  The CPU will run EPICS and the FPGA will have a complete application development environment
  For slower signals, EtherCAT will be used as a real-time fieldbus with good price/performance ratio
  Synchronization and event information are key for applications where a full custom platform solution would be too costly
  Low speed signals are handled with commercially available PLC systems from Siemens
  This is a cost-effective solution that addresses ESS reliability and maintainability requirements
  The PLC:s will be connected to EPICS for further integration into the control system
Signal speed
10 Hz
1 Hz
0.1 Hz
100 Hz
1 kHz
10 kHz
100 kHz
1 MHz
10 MHz
Electronic front-end platform
EtherCAT
Industrial automation (PLC)
A custom made microTCA board with a powerful FPGA and a CPU. A FPGA framework constitutes the development environment. The CPU runs EPICS
EtherCAT I/O modules that are connected to commercial or open-source EtherCAT master controllers which are in turn connected to the EPICS based control system
Slower signals are handled by industrial automation (PLC) for reliability and cost reasons. The standardized platform for ESS applications comes from Siemens

## Slide 16: “Other” I/O
ICS is trying to standardize control solutions wherever possible
  Serial devices
    Use MOXA – almost de-facto standard
  Ethernet-based devices
    Ethernet as a fieldbus connected to EPICS
  Detectors
    EPICS AreaDetector supports a large device base
  Motion control
    Working together with our NSS colleagues

## Slide 17: Hardware development status
Development of the high-end electronic platform is started as an in-kind activity with Switzerland
Development of EtherCAT-specific modules for ESS/ICS usage is being initiated as an in-kind activity with Estonia
More in-kind opportunities exist for development of microTCA electronics and platform management
A call for tender for hardware development services and automation software development services will open soon

## Slide 18
SAFETY AND PROTECTION

## Slide 19: Personnel safety and Machine protection
Machine protection shall prevent and mitigate damage to the machine in accordance with beam and facility related availability requirements
Machine protection shall protect the machine from unnecessary beam-induced activation having a potential to cause long-term damage to the machine or increase maintenance times
The Personnel safety system shall prevent and mitigate any risk for damage or danger to personnel as identified by risk analyses and assessments
The Personnel safety system shall be designed and implemented in compliance with safety standards such as IEC61508

## Slide 20: Safety and protection status
ZONE 4
ZONE 5
ZONE 6
ZONE 7
ZONE 3
ZONE 2
ZONE 1
The Personnel safety system is nearing design completion and implementation of subsystems has started. The PSS will be an ESS in-house activity
The machine protection architecture is being enhanced and clarified as recommended by an external review committee in 2015-12
Meanwhile, parts of the Machine protection system, and the Fast beam interlock system in particular, is being developed as an in-kind collaboration with Switzerland
We are looking for a solution for radiation monitors and oxygen depletion monitors

## Slide 21
Control SYSTEM
INFRASTRUCTURE

## Slide 22: Control system infrastructure
In the scope for the control system infrastructure is infrastructure required for the Control System to operate
A centralized ESS Control Room, which allows the entire facility to be controlled from the same location
Operations consoles, servers and file storage required for operation
Networks between Control boxes, Timing system units, Control Room, Data Centre and other control equipment
Efforts and material required for connecting devices to the ICS

## Slide 23: Control system infrastructure status
The design and implementation of the control room has been initiated as an in-kind collaboration with Norway
We are investigating possibilities of creating in-kind collaborations for the data centre associated to the control system
Design and planning of the control system network is ongoing. Some specialized tasks such as cyber security issues may be possible to implement as in-kind contributions