## Slide 1
Nuclear Physics Institute
Czech Academy of Sciences
J. Šaroun
Nuclear Physics Institute of the CAS, Řež
Neutron optics and shielding options for BEER
Beamline for European Material Engineering Research

## Slide 2
Beam requirements
bi-spectral extraction, l = 1 .. 8 Å
adjustable beam size: 0.5x0.5 to 10x10 mm2
adjustable Dl/l resolution, 0.07 .. 0.8 %
adjustable divergence, 1 x 1 .. 10 x 30 mrad2
S/N > 3 for diffraction
background < 1 n/s @ SANS detector
BEER – ToF diffractometer for material engineering
Situation plan with floor levels
Scientific requirements
1. In-situ & in-operando experiments with large SE
fast data collection (< 1s) = high intensity
medium gauge volume (~ 0.2 cm3)
microstructure evolution: SANS
2. Residual strain mapping
small gauge volume (> 1 mm3)
,
high flux (beam modulation method)
Bragg edge imaging ()

## Slide 3: BEER – Materials Engineering Diffractometer
Beamline for European materials Engineering Research
Beamline overview
length 159 m
divergence
exchangeable
beam-shaping optics
pulse shaping
pulse modulation
chopper system for wide range of resolutions
bi-spectral extraction optics
detector banks
+
sample environment

## Slide 4: Neutron optics – vertical guide profile
All guide sections follow the same ballistic vertical profile.
The profile results from numerical optimization and subsequent trade-off between cost and performance.
Focused at the top moderator ( 3cm). The bottom moderator gives ~ 20 % lower flux at the sample.
z, mm
m=2.5
m=4 to 2.5
m=2.5 to 5
Vertical divergence at the sample ~ 30 mrad.

## Slide 5: Neutron optics - monolith insert
Horizontal guide profile with the monolith insert.
Focusing at the thermal moderator:
beam axis angle: + 0.295 deg
beam axis shift: -30 mm at the entry -10 mm at the shutter
bi-spectral extraction
Si blades, m=4, t=0.5 mm
narrow beam section with choppers
beam axis
y, mm
2.12 m
m=4
m=4
m=0 ?

## Slide 6: Neutron optics – horizontal guide profile
Option 1 (preferred)
DLS closed twice outside the bunker (dashed cyan lines).
The curved guide starts in the bunker (at 20 m):
width = 4 cm
length = 123.5 m
R = -16 km
beam expansion, w= 2 cm -> 4 cm, length=10 m
Option 2
DLS closed once inside the bunker, 2nd closure is outside (dashed cyan lines).
Guide 1:
width = 2 cm
length = 18 m
R = -2.5 km
Guide 2:
width = 4 cm
length = 105.5 m
R = 25 km

## Slide 7: Neutron optics – vertically focusing guide
sample axis
guide exchanger
wall
Beam shaping optics:
vertically focusing guide with exchangeable end section
2 adjustable divergence slits (S1, S2)
adjustable slit S3 for gauge volume definition, variable distance
S1
S2
S3
absorbing side walls
bounce statistics for 1A
m-value

## Slide 8: Neutron optics – performance
Beam brightness at the sample
dashed curves: beam axis focused near the moderators boundary
Option 2 yields less thermal neutrons (as expected)

## Slide 9: Neutron optics – performance
Brilliance transfer ratio
DW = 2x2 mrad2
DW = 5x30 mrad2

## Slide 10: Neutron optics – performance
Beam brightness at the sample, option 2 / option 1
Option 2:
gives by 10 % to 25 % less intensity in the most important wavelength range of 1 to 2 Å

## Slide 11
Simulation of neutron escape intensity
SIMRES v. 6.3.4
Monitoring of neutron events in the guide coating
a) capture in the NiTi coating => conversion to g
b) scattering or transmission => escaped neutrons
To be used for the assessment of the focusing guide shielding …

## Slide 12: Neutron optics – transported neutron flux and intensity
Estimation of thermal neutron flux and integrated intensity at various places along the beamline (ray-tracing simulation) |  |  | 
position | x [m] | flux [109/s/cm2] | integral [1010 / s]
sample | 157 | 6.1 | 4.6
slit 2 | 154 | 2.6 | 5.5
slit 1 | 150.5 | 2.0 | 5.6
2nd shutter | 78 | 1.9 | 6.3
bunker wall | 28 | 2.1 | 6.9
monolith wall | 6 | 11.4 | 15.7
Example for Option 1, full pulse (choppers stopped)
At least 10 x lower values are expected during normal operation

## Slide 13: Options for guide shielding
Option 1
Option 2

## Slide 14: Options for guide shielding
Before DLS
After DLS
hd concrete
std. concrete
Shutter and chopper cave (option 1)
Proposal for the 1st iteration

## Slide 15
Thank you for your attention