## Slide 1: Development of compact accelerator neutron source
A. Marchix, H. Tran, N. Chauvin, A. Letourneau, J. Schwindling
Irfu, CEA-Saclay, Université Paris-Saclay
A. Menelle, F. Ott
LLB, CEA-Saclay, université Paris-Saclay

## Slide 2: Scenarios for neutrons in Europe
Source: Neutron scattering facilities in Europe, ESFRI report (2016)
Main reactor-based neutron sources would stop in the next decade
  Very unlikely to be any new research reactors built in Europe
  “Low-cost” sources (200-500M€) to be affordable by individual countries
Opportunity for Compact Accelerator Neutron Source (CANS)

## Slide 3: Neutron sources in France
Instrument.days
  French community is strongly affected
  No new facility expected in a near future
IPHI-NEUTRON & SONATE projects launched at CEA Saclay
  Keep knowledge in neutron scattering
  Training (university)
  Demand from industrial users
  Development of instruments
  Preparation of experiments for high brilliance neutron sources

## Slide 4: Main Challenges for CANS developments
Accelerator
  Strong space charges (emittance growth, beam halo… and beam losses)
  Beam dynamics can be challenging
  Even very small losses can be harmful and can cause: activation, quench of SRF cavities, machine damages due to power deposition
   Need expertise in high intensity accelerator technology
Target/Moderator/Reflector
  Heat removal from the target
  Optimize the target/moderator assembly for required neutron production
   Validated and Predictive Monte-Carlo simulation tools

## Slide 5: Tests AT Saclay with IPHI injector
3 MeV proton beam and the current set to ~3 µA (~1.8E+13 proton/s),
Moderator in polyethylene (blue): 30 x 30 x 40 cm3,
Angle of detector 38 degrees,
The distance from the target to detector (violet) : 840 cm.
4 days of measurements at ~3 µA (3.6 1017 protons on Be target)
Proton beam 3 MeV
840 cm

## Slide 6: TEST Experiment with IPHI
3He detector shielded with polyethylene and B4C (8 m from the target)
Polyethylene Moderator
Be target (inside)

## Slide 7: GOLD foils activation inside the moderator
198Au isotopes/µC
  Good agreement data & GEANT4 simulation with Howard’s angular distribution
  New experiment planned next July to confirm primary neutron angular distribution

## Slide 8: 3He measurements: TOF @ 8.4 meters
  Good agreement on the shape of the distribution (GEANT4 simulations)
  Discrepancies on absolute values: could be explained by wrong alignment between 3He detector and collimator
Neutron counts (a.u)

## Slide 9: NEUTRON flux
Neutrons/cm2//µC
  Exit neutrons mainly come from the bottom surface of the collimator
  IPHI-NEUTRON project (50 kW) -> a factor 2000 larger

## Slide 10: Conclusions
  Experiment performed with IPHI (3MeV proton) in order to test & qualify the concept
  Good agreement observed between data and GEANT4 simulations for Gold foils activation inside the moderator
  Good agreement on the shape of the TOF distribution for thermal neutrons with GEANT4 simulations
  Discrepancies on data for primary neutron angular distribution @ 3 MeV
  Discrepancies on absolute values for TOF measurements
  Perspectives:
    GEANT4 moderation process validated
    New experiment planned next July
Under study: concept of compact thermal moderators (simulations)
Development of 50 kW target (heat removal challenge)
Project IPHI-Neutrons (2020): 3 MeV proton, Be target, 50 kW
Project SONATE (2025): 20 MeV proton, Be target, 80 kW

## Slide 11: PERSPECTIVES: SONATE
Technique | Flux on sample | Reference spectrometers
Reflectivity | 0.8x107 n/s/cm² | HERMES@LLB 1x107 n/s/cm² POLREF@ISIS ~1x107 n/s/cm²
SANS | 0.7x106 n/s/cm² (low Q) 2.2x106 n/s/cm² (med Q) 6.7x106 n/s/cm² (high Q) | PAXE@LLB (low Q) 0.7x106 n/s/cm² SANS2D@ISIS 1x106 n/s/cm²
Low resolution powder diffraction | 2x106 n/s/cm² | G41@LLB 2x106 n/s/cm²
Imaging (white beam) | 1.5x106 n/s/cm² (for L/D = 240) 1.3x107 n/s/cm² (for L/D = 80) | ICON@PSI 1x107 n/s/cm² CONRAD@PSI 1x107 n/s/cm² (for L/D = 240)
Imaging (time resolved) | 1x105 n/s/cm² (for L/D = 500) dl/l = 1% | ANTARES@FRM2 5x105 n/s/cm²
Spin-Echo | 2x106 n/s/cm² | MUSES@LLB 2x107 n/s/cm² (at 5A°)
TOF | 6x107 n/s/cm² | OSIRIS@ISIS 3x107 n/cm²/s
SONATE’s reference baseline for design studies
  Ep = 20MeV, Ipeak = 100mA, duty cycle = 4%, P = 80kW
  Beryllium target

## Slide 12: Neutron production in Be(n,p)

## Slide 13: Geant4 Neutron production in 9Be(p,n)

## Slide 14: Status of Accelerator-based Neutron sources in the world
SONATE

## Slide 15: DRF Irfu DPhN LEARN
Commissariat à l’énergie atomique et aux énergies alternatives
Centre de Saclay | 91191 Gif-sur-Yvette Cedex
T. +33 (0)1 69 08 xx xx | F. +33 (0)1 69 08 99 89
  Etablissement public à caractère industriel et commercial | RCS Paris B 775 685 019