## Slide 1
Nuclide production in spallation reactions:
How useful are the simulations?
Jean-Christophe David
SPhN
(Nuclear Science Division)

## Slide 2
Nuclide production in spallation reactions:
How useful are the simulations?
Introduction
Spallation reactions
4 topics addressed about nuclide production
    Design (optimisation) EURISOL – DS
    Predictive power (reliability) Megapie
    Feasibility (uncertainty estimate) ESS
    Mitigating the lack of experimental data Meteorite study
Recurrent tool: INCL model (often associated to Abla)
~150 MeV < Projectile Energy < ~2 GeV
(0 MeV < Projectile Energy < ~20 GeV)
cem, cascade-x, cascade-04, cascade-asf, BIC, Bertini (geant4, mcnp, phits), incl, isabel, jam, jqmd, …
gem, smm, gemini++, abla, dresner(+fission), …

## Slide 3
Nuclide production in spallation reactions:
How useful are the simulations?
Design and optimisation
EURISOL-DS

## Slide 4
Nuclide production in spallation reactions:
How useful are the simulations?
EURISOL-DS
EUropean Isotope Separation On-Line Radioactive Ion Beam Facility
Design Study
Design and optimisation

## Slide 5
Nuclide production in spallation reactions:
How useful are the simulations?
EURISOL-DS
One of our tasks (direct target)
  Production rate of using INCL4.2-Abla and CEM2k (MCNPX)
  Which isotopes in Be, Li, Mg, Ar, Ne, Ni, Ga, Kr, Sn, Hg, Fr (NuPPECC)
  Which target material of Table below
  Which size (considering a cylinder)
direct target
fission target
(GeV)
(cm)
(kW)
(g/cm3)
320 configurations!!!
Design and optimisation
EUropean Isotope Separation On-Line Radioactive Ion Beam Facility
Design Study

## Slide 6
Nuclide production in spallation reactions:
How useful are the simulations?
EURISOL-DS
Example of results
Thanks to fast/benchmarked codes
Exotic physics cases can be studied
in Safe facilities
for a given budget
(The best compromises can be obtained)
S. Chabod et al., EPJ A45, 131 (2010)
Design and optimisation
With comments, for future works (models evolve)
R1: Nuclei from a long evaporation process:
overestimated by CEM2k
underestimated by INCL4.2/ABLA
R3: A specific benchmark should be done for light targets to disentangle between both models.

## Slide 7
Nuclide production in spallation reactions:
How useful are the simulations?
Predictive power and reliability
Megapie

## Slide 8
Nuclide production in spallation reactions:
How useful are the simulations?
Megapie
Liquid Pb-Bi target Prototype
Irradiated at SINQ (PSI)
4 months in 2006
Proton - 575 MeV and 1.4 mA (~0.8 MW)
One of our tasks
  Estimate of residual nucleus production
   Safety (Activation, volatiles)
Predictive power and reliability
p

## Slide 9
Nuclide production in spallation reactions:
How useful are the simulations?
Megapie
Target
  Liquid Pb-Bi in Ta cylinder
  (L=20 cm, r=1 cm)
Projectile
  Proton beam: 1.0 and 1.4 GeV
proton
Volatile
An ancillary experiment @ ISOLDE:
    Volatile release from a Pb-Bi target (He, Ne, Ar, Br, Kr, Cd, I, Xe, Hg, Po and At)
Predictive power and reliability

## Slide 10
Nuclide production in spallation reactions:
How useful are the simulations?
Megapie
At
Results in 2007
Release of all elements rather well described, except astatine!
No model able to reproduce the A distribution!
Predictive power and reliability
Volatile
An ancillary experiment @ ISOLDE:
    Volatile release from a Pb-Bi target (He, Ne, Ar, Br, Kr, Cd, I, Xe, Hg, Po and At)
An interesting case: Astatine release
      At volatile (more than Po in Pb-Bi) and decays into Po
      Po: safety issue (long-lived a emitters)

## Slide 11
Nuclide production in spallation reactions:
How useful are the simulations?
Production mechanisms of At from Bi
Direct channel (p- emission)
Secondary reaction (He)
Megapie
INCL4.2 | n, p, p
Abla | n, p, a
INCL4.6 | n, p, p, d, t, 3He, a and A ≤ 8
Abla07 | n, p, d, t, 3He, a and IMF
( and pion potential: Vp(t) )
So INCL and Abla improved/extended
particle emitted
Benchmarks of the elementary processes…
Light At
Heavy At
Predictive power and reliability

## Slide 12
Nuclide production in spallation reactions:
How useful are the simulations?
Megapie
Direct production
Not bad for low masses
At from Bi
a-induced: great
a
a
alpha production
OK
Predictive power and reliability

## Slide 13
Nuclide production in spallation reactions:
How useful are the simulations?
Megapie
However results
remained BAD!!!
But calculation results in the target
and exp. data outside…
Generally time release negligible (Kr, Xe, …)
What about At???
If a release time included...
OK with T ~ 5 or 10h
Reliable tool  new assumption made possible
 new information obtained (Trelease)
… to be measured now...
Predictive power and reliability
J.-C. David et al., EPJ A49, 29 (2013)

## Slide 14
Nuclide production in spallation reactions:
How useful are the simulations?
Feasibility and uncertainty estimate
ESS

## Slide 15
Nuclide production in spallation reactions:
How useful are the simulations?
ESS
Technical Design Report (2013)
Our tasks:
  Target activity calculations
  Uncertainty estimates
geometry in MCNPX
p
Feasibility and uncertainty estimate

## Slide 16
Nuclide production in spallation reactions:
How useful are the simulations?
ESS
Activities from INCL4.6-Abla07 and CEM03
This ratio:
a “crude” estimate of uncertainties
Uncertainties:
What are the reasons of those differences? Can they be assessed?
Feasibility and uncertainty estimate

## Slide 17
Nuclide production in spallation reactions:
How useful are the simulations?
ESS
Feasibility and uncertainty estimate
Differences in Activities
Differences in Contributors
(produced isotopes)
Method

## Slide 18
Nuclide production in spallation reactions:
How useful are the simulations?
ESS
Method
Projectile Fluxes
Elementary sproduction
Feasibility and uncertainty estimate
Differences in Activities
Differences in Contributors
(produced isotopes)

## Slide 19
Nuclide production in spallation reactions:
How useful are the simulations?
ESS
Method
Projectile Fluxes
Mainly n and p
spectra ~well simulated
Elementary sproduction
Feasibility and uncertainty estimate
Differences in Activities
Differences in Contributors
(produced isotopes)

## Slide 20
Nuclide production in spallation reactions:
How useful are the simulations?
ESS
Method
Projectile Fluxes
Mainly n and p
spectra ~well simulated
Elementary sproduction
sp-induced : when exp. data  scalc benchmarked! ratio C/M
sn-induced : En < 25 MeV from CINDER (database)  OK
25 < En < 200 MeV Few data… (issue)
200 MeV < En n = p (assumed)
negligible
Feasibility and uncertainty estimate
Differences in Activities
Differences in Contributors
(produced isotopes)

## Slide 21
Nuclide production in spallation reactions:
How useful are the simulations?
ESS
Method
Projectile Fluxes
Mainly n and p
spectra ~well simulated
Elementary sproduction
sp-induced : when exp. data  scalc benchmarked! ratio C/M
sn-induced : En < 25 MeV from CINDER (database)  OK
25 < En < 200 MeV Few data… (issue)
200 MeV < En n = p (assumed)
negligible
negligible
Tricky and rests on elementary exp. data
Feasibility and uncertainty estimate
Differences in Activities
Differences in Contributors
(produced isotopes)

## Slide 22
Nuclide production in spallation reactions:
How useful are the simulations?
ESS
Results
Done for 9 years of cooling (total activity)
    primary result 8.95 1014 Bq
    method applied 7.95 1014 Bq (correction: 12%)
This method helps correcting the calculated value using exp. data (elementary processes)
BUT does not give uncertainties!!!
From GUM (JCGM 100:2008; http://www.bipm.org/fr/publications/guides/gum.html)
    uncertainty: "parameter, associated with the result of a measurement, that characterizes the dispersion of the values that could reasonably be attributed to the measurand”
    error: "result of a measurement minus a true value of the measurand”
Both are important/useful, but the way to assess them are different! And difficult!
Feasibility and uncertainty estimate

## Slide 23
Nuclide production in spallation reactions:
How useful are the simulations?
Mitigating the lack of exp. data
Meteorites

## Slide 24
Nuclide production in spallation reactions:
How useful are the simulations?
Meteorites
« Was erzählen uns Meteorite über das frühe Sonnensystem ? »
(Ingo Leya – Univ. Bern)
Used to study
. the meteorite history
. the GCR spectra
s production of
isotope i
with projectile k
on target nucleus j
from Experiments
or Models
GCR spectra
H
He
spallation
(87%)
(12%)
Mitigating the lack of exp. data

## Slide 25
Nuclide production in spallation reactions:
How useful are the simulations?
Meteorites
p+Fe 36Cl
a+Fe 57Co
N+Fe 54Mn
n
p
INCL Results
proton
alpha
neutron
secondary reactions
INCL4.6-Abla07 significantly improved
INCL4.6 reliable with
a-induced reactions
INCL4.6 covers a large range…
Improving residual nucleus calculations
can play a role in topics like meteorite study
Mitigating the lack of exp. data
a=2p+2n

## Slide 26
Nuclide production in spallation reactions:
How useful are the simulations?
Conclusion
Nuclide production simulation in spallation reactions
can be done by numerous models in several
transport codes (from J.-C. David EPJ A51, 68 (2015))
For the last 20 years significant improvements
done in nuclide production
Reliability/uncertainties-errors is still a difficult question
 benchmarks are necessary
    already done
        by transport code developers
        as project (e.g. IAEA benchmark (2010) https://www-nds.iaea.org/spallations/ )
    to be done (new ones…)

## Slide 27
Nuclide production in spallation reactions:
How useful are the simulations?
Outlook
Some models give “good” results, BUT improvements and extensions are still needed!
e.g. in INCL model (since the last IAEA Benchmark)
    Clusters (as projectiles and emitted particles)
    Extension toward low and high energies (smooth transition over a large energy range)
    Specific cases ( (p,2p), (p, pn) reactions) --- D. Mancusi / J.L. Rodriguez-Sanchez
    Uncertainties (Bayesian method) --- G. Schnabel
    Strangeness (Hypernucleus) --- J. Hirtz

## Slide 28
Nuclide production in spallation reactions:
How useful are the simulations?
INCL team
A. Boudard, J. Cugnon, J. Hirtz, S. Leray, D. Mancusi,
A. Marchix, J.L. Rodriguez-Sanchez, G. Schnabel

## Slide 29
Nuclide production in spallation reactions:
How useful are the simulations?
Thank you!
Tack!