## Slide 1: Status of ICS standards
Timo Korhonen
Integrated Control System Division
www.europeanspallationsource.se
27 September 2016

## Slide 2: Outline
Standards catalogue
  ICS Handbook and related
Conventions
  Naming, GUI, version control, issue handling
Hardware standards
  BI, RF standardization on MTCA.4
  EtherCAT, motion control etc
  PLC development
Services
  Archiver, Save&Restore, alarms,model
Software development & deployment
  Languages, pvAccess (V4) EPICS bindings
  Development Environment
  ESS EPICS Environment
Applications
  CS-Studio, iPython, jupyterHub
Summary

## Slide 3: Standards Catalogue (central ones)
ICS Handbook
  First draft version has been released
  CHESS Document ESS-0067637
  Reviewed and accepted version targeted by end 2016
Hardware platforms definition
  Has been out for a while
  Good acceptance by users (accelerator, target)
  CHESS document ESS-0037909
ESS EPICS Environment
  Already established practice
  CHESS document ESS-0067642

## Slide 4: ICS Handbook
Overview and dictionary of standards and practices, including:
  ICS DIVISION MISSION STATEMENT
  SYSTEM DESIGN PHILOSOPHY
  SYSTEM LIFE CYCLE
  SYSTEM architectural Description
  System Software Standards and Specifications
    Computing Infrastructure
    ESS Software Development Environment
    EPICS development
  ICS Configuration Management Tools and Services
    User Interface and other end user tools
  System Hardware Standards and Specifications
    Hardware platforms
    Global Timing System Specification
  ICS Network and Server Infrastructure specifications
  INTERFACE SPECIFICATIONS
  MACHINE PROTECTION SPECIFICATION
  PERSONNEL SAFETY SPECIFICATION
  DEVIATIONS POLICY
Not yet in final form but contains most of the central standards and definitions

## Slide 5: Conventions
ESS Naming Convention
  CHESS Document ESS-0000757
  Widely followed but not yet fully settled in the whole organization
  ICS integrators in charge of naming
GUI development guidelines
  Preliminary work done and documented but needs refinement
To be done:
  EPICS conventions
    Use of display, alarm, archiving limit fields
    Guidelines for EGU, DESC and other metadata
    Standardization of macros & substitutions (partly done but incomplete)
  Archiving, alarm guidelines
    advice and guidance for stakeholders

## Slide 6: Hardware standards
Digital Platform Card(s)
  Commitment from major stakeholders to use this platform
    Beam Instrumentation, RF
  New personnel hired for support, also PSI has committed manpower
EtherCAT
  Motion control, field I/O when appropriate
  Already in use (Proton Source & LEBT)
  https://ess-ics.atlassian.net/wiki/display/HAR/EtherCAT+-+ESS+support
PLC
  Siemens S7-1500 established as the standard
    https://ess-ics.atlassian.net/wiki/display/HAR/PLC
  Used by contractors & in-kind
  So far no essential deviations
    But need to keep an eye on this

## Slide 7: Services
Archiving
  Archive Appliance
    Packaged for delivery for use by remote partners (in-kind etc)
    Central installation TBD
      No heavy use until site installations start
Alarms
  Started work on strategy
    Use CS-Studio BEAST unless/until new requirements appear
Channel Finder
  Very useful for management of PVs
  Just starting
Save&restore (aka SCORE)
  Use CS-Studio PVTable until requirements are clear
No particular issues with user acceptance so far

## Slide 8: Development Environment
ESS EPICS Environment (EEE)
  Documented in CHESS document: ESS-0067642
  Used to develop and deliver systems
    Running systems in Catania and other IKC sites
    See also CEA report in EPICS meeting at Lund
  Local users and stakeholders
    Users in different groups in Lund
  Some adjustments need to be done and and internal standards have to be settled
    However, the system is operational and in use.
Configuration tools
  CCDB, CableDB, IOC Factory in initial use
    So far, mostly good feedback
    Bulk use is still unproven
Development environment package
  In production, issues are fixed as they come up

## Slide 9: EPICS V4 standardization
EPICS V4 set as the standard protocol
  pvAccess server included in IOCs
  Trainings done & planned
    Lund EPICS meeting, hope to repeat the training session
  Some initial applications tested
  Integration testing to be done
  A lot of “missionary work” still required
  Infrastructure testing is crucial

## Slide 10: Applications
Control System Studio
  Set of generic tools, widely accepted
    BOY -> Display Builder
iPython/jupyterHub
  Python accepted as the standard scripting language
OpenXAL
  A lot of work invested in the physics model
  Working with accelerator physicists
Apart from CS-Studio, still early steps
  CS-Studio acceptance looks good so far
  Instruments are going their own way, though
    Different requirements. To be discussed

## Slide 11: Summary
Documentation status
  Struggling with time but there is progress
Hardware
  Acceptance looks good, still critical and needs attention
Services
  Partially settled, development needed
  Initial feedback positive
Software development
  Still early stages, needs to be ramped up
Handbook
  First draft release out, to be finalized