## Slide 1: Raster Scanning of the ESS Beam
Heine Dølrath Thomsen

## Slide 2: The HEBT (28.05 2012)
Dipoles,
Quadrupoles
Octupoles
UHB: Energy upgrade + movable collimators.
ACH: Achromatic elevation. Tune-up lines below.
A2T: Beam expander system (non-linear) + fixed collimator.

## Slide 3: Exploiting the target footprint area!
Lowering the max. current density J => increasing target life!
J [µA/cm2]
Notes: Target + PBW: critical components in the facility

## Slide 4: Beam Expander Systems I: DC Magnets
ESS2003-LP ESS2003-SP, CSNS, IFMIF
Notes: Octupole:
‘Simple’ tuning (1 button)
Limited fields per aperture
Overfocusing
SFMs:
4 x dipoles
Less flexible (step)

## Slide 5: The HEBT (28.05 2012)
Dipoles,
Quadrupoles
Octupoles
Notes: Beam optics constraints:
- Large beam aspect ratio in multipoles!

## Slide 6
Notes: Trade-off: compromising SCL beam quality and reducing cost

## Slide 7: Beam Expander Systems II: 1D Rastering

## Slide 8: Beam Expander Systems II: 1D Rastering
Notes: Beamlets

## Slide 9: Beam Expander Systems II: 1D Rastering

## Slide 10: Beam Expander Systems II: 1D Rastering

## Slide 11: Beam Expander Systems II: 2D Rastering
Traditionally: Hor. MPS: Slow
Ver. MPS: Fast
Notes: Currents need to be controlled (and monitored?)

## Slide 12: Beam Expander Systems II: 2D Rastering
Notes: Raster scanning: Dependence of SCL beam quality: octupole > SFM >> Raster scanning
AC magnets sweep beam
IGBT-based modulators -> triangular current waveforms, electronic (resonant) generation of frequencies
J-LAB (2 systems) + APT

## Slide 13: Beam Expander Systems II: LANL APT
x,y [arb. units]
One ESS pulse
fy/fx = 5:4
Notes: Raster scanning:
Pattern determined by frequency ratio
AC magnets sweep beam footprint within 1 ESS pulse
Fields vs. frequency (1.4 kHz and 1.75 kHz), nx = 4, ny = 5, ny/nx = 1.25,
Dependence of SCL beam quality: octupole > SFM >> Raster scanning

## Slide 14: Linear optics: 10 RMS beam size
ACH A2T
triplet 4+4 r.m. doublet
Notes: Triplet + 2 x 4 raster magnets + doublet
Only slight coupling of steering and expansion in expander quads!
Maximum deflection in both directions, x_max = 75 mm, y_max = 17 mm
RMS beam sizes: 6 mm, 5 mm -> will depend on scanning pattern and thus freq.s!
COMPARISON
Simpler tuning – 5 vs. 10 quads.
One extra UHB period or weaker magnets!
NO monster-magnets?!
Eric’s backshine shield feasible!
Small divergence vs. double waists

## Slide 15: Multiparticle: 1 Mparticles of SCL output
Notes: ~Linear optics!
Losses: 0 / 1E6!

## Slide 16: Monte Carlo Simulation: 5:4 pattern
10 Mparticles - time-lapse:
http://users-phys.au.dk/heinetho/raster_anim_MC.gif

## Slide 17: Choice of frequencies?
f0 = 1 / Δt = 350 Hz
fx = nx × f0
fy = ny × f0
Conditions:
nx, ny are integers
nx/ny as irrational as possible?
Intensity modulations at instruments?
Frequency stability
Modest phase stability
Notes: Footprint fully illuminated within 0.3-0.5 ms
Neutron yield modulation at instruments?
Target stress & fatigue?

## Slide 18: High Frequencies?
Existing Systems
J-LAB:
  B = 40 G, L =15 cm
  f = 10-45 kHz
  Air-coils of Litz-wire
  H-bridge of MOSFETs
LANL APT (1.7 GeV, 100 mA):
  B = 500 G, L = 4 x 30 cm
  f = 0.5-0.6 kHz
  Ferrite-based magnets
  H-bridge of IGBTs
LANL MTS:
  f = (20 + 60) kHz (sinus.)
ESS?
  B = 250 G, L = 4 x 30 cm?
  f = 5-20 kHz? (TD + Science)
  Air-coils?
Notes: Ceramic beam tube should also be considered!
Eddy current heating could be air-cooled
Ferrite: larger inductance + remanent field
Air-coils: no remanent field due to hysteresis
Feasible set of magnet + modulator?
B = 150 G – 250 G, 250 G ~ 0.7 mrad / magnet @ 2.5 GeV

## Slide 19: ESS Lissajous System
Linear optics!
All feasible magnetic elements
Losses: 0 / 106 particles!
Choice of frequency set?
  Neutron yield modulation at instruments?
  Target stress & fatigue?
  …

## Slide 20: Development of the Lissajous System
AC Magnets
Modulator
Beam Optics
HDT, ISA
2013.06: CDR for Lissajous system
2013.10: Comparison of beam expanders
2014: TDR + prototype
Design partner
Notes: Comparison of beam expander systems:
Risks? Impact of magnetic element-failure? Can component-failure cause breaking of target?
Carlos: many years of experience at CERN in charge of the pulsed power group