## Slide 1
Detector and Front End Electronics
For ESS nBLM
Philippe Legou
CEA Saclay - France
ESS Meeting 2016 - Lund - 2016 July 25th

## Slide 2
Thin gas chamber Low ionization probability for electrons compare to recoil ions
Fast response
(Spectroscopy based on time of flight technique in counting mode)
Recoils charged particles liberate ionization electrons in two gas filled gaps defined by three planar electrodes. In the electric fields, electrons are multiplied and drift up to the strips. Electrons produced by g-rays pass through the detector with a lower ionization probability.
 Insensitivity to g-rays
ESS nBLM concept

## Slide 3
Technical corridor ?
PI Room
BEAM
Cables
Up to 20 m
Ancillary rack
ESS Network
Laptop in the PI room drive the Acquisition via NETWORK
Detectors
ESS nBLM setup
Does a map of the experiment hall already exists an available ?
Distances between nBLM detection boxes and ancillary racks?

## Slide 4
Preamplifiers
Connectors
Gas flow
       Board (multi-layer PCB) including :
         Detections area
         Preamplifiers (plugged on the board)
         Hybrid connectors to reduce the space requirement
Example of setup for neutrons detection

## Slide 5
Coaxial connectors for analog
signals
preamplifiers
Reading strips
The 4-layers PCB
Strips, spacers and the mesh are sticked
on the PCB by a single process.
Strips, preamplifiers and connectors :
good signals integrity
Cables for :
 Signals
 Low voltage / High Voltage
 Temperature sensor
Type of cables authorized at ESS
( non flammable ….) ?

## Slide 6
Size: 22 x 20 x 5 mm
weight : 4g
Power supply : + 5V -5V
Consumption  50 mW
Noise: 600 µV rms
In few figures …
Input: positive or negative
Rise time : < 1ns
The new front-end : FAMMAS
( Fast Amplifier Module for Micromegas ApplicationS)
Example of Front end electronics used
in neutron detection
Radiation hardness capabilities for detector and electronics?

## Slide 7
Préamplificateur Minicircuits
1GHz ZFL-1000LN
Temps de montée
10% - 90%
Temps de descente
90% - 10%
Largeur à mi-hauteur
Amplitude
1.08ns
2.16ns
3.07ns
Temps de montée
10% - 90%
Temps de descente
90% - 10%
Largeur à mi-hauteur
Amplitude
1.50ns
1.11ns
2.57ns
Préamplificateur CEA – FAMMAS
(Ph.Legou)
Comparison preamplifier
Minicircuits / CEA

## Slide 8
Size: 60 x 22 x 5 mm
weight : 8g
Power supply : + 5V -5.2V
Consumption  400 mW
Noise: 700 µV rms
In few figures …
Input: positive or negative
Output : ECL differential
Buffer area
Preamplifier with differential output

## Slide 9: DEMIN AND ANCILLARY RACK LOCATIONS
DEMIN
ANCILLARY RACK
Example of experimental conditions in neutrons detection and measurement (Inertial Confinement Fusion)
NY- USA

## Slide 10
Measurement are performed in a large background
  Neutrons ; Photons ; EMP effects
n
n
Before 14 MeV neutrons :
g-rays induced by (n, g)
After 14 MeV neutrons :
g-rays (n, g)
+ scattered neutrons in the bay
DT shot
Measurement of neutrons
What about the noise and perturbations sources?

## Slide 11
70cm=27.5’’
180cm=71’’
   Digitizers for pramp cards
   GPIB/Ethernet interface
   Power supplies for digitizers
   Gas flow regulator
   PC (drives the gas regulator)
   NIM crate :
     High volyage unit
    (cathodes & Meshes)
     Power supplies for preamps
Ancillary rack

## Slide 12
Thank You …