## Slide 1: Simulation of Gamma Ray response of Detectors
Anton Khaplanov
www.europeanspallationsource.se
September 05, 2016

## Slide 2: Introduction
A. Khaplanov et al. "Investigation of gamma-ray sensitivity of neutron detectors based on thin converter films", Journal of Instrumentation 8, P10025 (2013); doi:10.1088/1748-0221/8/10/P10025; arXiv:1306.6247v1.
A.Khaplanov, PhD thesis, “Position-sensitive germanium detectors for gamma-ray tracking, imaging and polarimetry”
Trita-FYS, ISSN 0280-316X ; 2010:04
What is gamma sensitivity?
Gamma interactions
Low-energy effects
High-energy effects
Definition of gamma-sensitivity

## Slide 3: Gamma “efficiency” vs “sensitivity”
The same thing.
Except we aim to minimize gamma efficiency and maximize neutron efficiency
(in neutron detectors…)

## Slide 4: Gamma detection in neutron detectors

## Slide 5: Gamma interactions
Pair production
Rayleigh scattering for γ energies:
Forward-focused
Inelastic
Low cross section
 Usually neglected

## Slide 6: Gamma Interactions
M.J. Berger et al.,
XCOM: Photon Cross Sections Database
http://www.nist.gov/pml/data/xcom/index.cfm

## Slide 7: Gamma detection in neutron detectors
Gas
Solid
Solid
γ
e-
Energy deposited in gas:
few 10 keV
few 10 keV
0
few 10 keV
0
e+
e-
Examples of γ interactions:
close to surface
Compton in gas
No interaction
Pair production in wall
Compton in wall,
far from surface
Photo effect in gas
X-ray
few 10 keV

## Slide 8: Low energy effects
Momentum of e- before Compton or photo- interaction
Production / tracking of x-rays
Production / tracking of Auger electrons
Al x-rays detection
Ar x-ray escape

## Slide 9: Gamma interaction simulation
if (particleName == "gamma") {
pmanager->AddDiscreteProcess(new G4PhotoElectric);
pmanager->AddDiscreteProcess(new G4ComptonScattering);
pmanager->AddDiscreteProcess(new G4GammaConversion);
if (particleName == "gamma") {
pmanager->AddDiscreteProcess(new G4LowEnergyPhotoElectric);
pmanager->AddDiscreteProcess(new G4LowEnergyCompton);
pmanager->AddDiscreteProcess(new G4GammaConversion);
if (particleName == "gamma") {
pmanager->AddDiscreteProcess(new G4PenelopePhotoElectric);
pmanager->AddDiscreteProcess(new G4PenelopeCompton);
pmanager->AddDiscreteProcess(new G4GammaConversion);
S. Chauvie et al.,
Geant4 low energy electromagnetic physics,
IEEE NSS Conf. vol .3 (2004) 1881 - 1885.
J. Sempau et al.,
Experimental benchmarks of the Monte Carlo code PENELOPE,
Nucl. Instr. Meth. B 207 (2003) 107-123.

## Slide 10: e- / e+ interactions
Ionization
Multiple scattering
Bremsstrahlung
e+ / e- anihilation

## Slide 11: e- / e+ interaction simulation
if (particleName == "e-") {
pmanager->AddProcess(new G4eMultipleScattering,-1, 1, 1);
pmanager->AddProcess(new G4eIonisation, -1, 2, 2);
//pmanager->AddProcess(new G4LowEnergyIonisation, -1, 2, 2);
//pmanager->AddProcess(new G4PenelopeIonisation, -1, 2, 2);
pmanager->AddProcess(new G4eBremsstrahlung, -1, 3, 3);
}
else if (particleName == "e+") {
pmanager->AddProcess(new G4eMultipleScattering,-1, 1, 1);
pmanager->AddProcess(new G4eIonisation, -1, 2, 2);
pmanager->AddProcess(new G4eBremsstrahlung, -1, 3, 3);
pmanager->AddProcess(new G4eplusAnnihilation, 0,-1, 4);
}
Include or not include Low-energy models?
Depends on statistics needed, energy ranges

## Slide 12: High energy effects
From ~10MeV, e+/e- production is main effect
e- (or e+) range enough to traverse several volumes
Example: 8 MeV pair-production event

## Slide 13: Gamma energy dependence
Spectra vs. γ-ray energy
For high enough energy (here, 8 MeV), electrons cross more than one cell. This can be rejected in data acquisition

## Slide 14: Where gammas interact
Detected interaction energy (deposited in gas):
low γ energy – most interactions in gas
medium/high γ energy – most interactions in wall

## Slide 15: Gamma detection in neutron detectors
Spectra vs. gas pressure

## Slide 16: Gamma efficiency in neutron detectors Measurement

## Slide 17: Gamma “sensitivity”
Same detector filled with He3,
or coated with B10
B10 coating (~1um), He3 (Z=2) have negligible effect on γ
Choice of threshold and γ
sensitivity – the same
N spectra can be very different
Overlap between n and γ spectra defines gamma sensitivity.

## Slide 18: Pile-up effects
Rate:
Individual γs under threshold, but if rate is extremely high – pile up of signals may be above threshold
Coincident gammas
Nucleus emitting many gammas at once
Ex. Cd113, Gd155/157

## Slide 19: Conclusion
Take your simulation of the detector and shoot gammas at it
At low energy – consider x-ray energies of materials involved
- if significant check which model is used
At high energy – consider how far e- can travel through detector
- compare to volume of common readout
Gamma response depends on detector geometry, not on neutron converter
Overlap between n and γ spectra define threshold and sensitivity