## Slide 1: Simulation of Gd Gem for NMX detector
05.09.2016
Dorothea Pfeiffer

## Slide 2: Gd-GEM backwards setup
neutron
conversion electron
Start of track

## Slide 3: Detector Model in Geant4
neutron
conversion electron
Gas region where Garfield++ is used
Garfield used:
  for creation of ionization clusters
  drifting the electrons and ions (diffusion)
Amplification, charge collection at readout and signal not yet simulated

## Slide 4: Simulated detector parts
The complete detector geometry implemented in Geant4
  Gd cathode, frame, readout board, GEM foils (without holes), ArCO2 filled drift, transfer and induction
Cathode: Neutron capture and creation of gammas and conversion electrons
Primary ionization
Formation of ionization clusters and the subsequent drift of the electrons (Geant4/Garfield interface)

## Slide 5: Simulation of GEM amplification and read out?
Very slow (field maps)
Usually done only for a few holes or parts of holes using symmetry
Due to track length of conversion electron difficult
Behaviour of GEM itself well understood
Solution: Use of gain function to multiply signal and convolute with pulse shape function to simulate the read out
GEM foil
Electrical field in holes

## Slide 6: Geant4 Gd simulation problems
Impossible to get the conversion electrons and the gamma emission correctly at the same time
To produce conversion electrons, the photo-evaporation model flag has to be used. This model conserves the Q value, but produces a gamma spectrum that differs very much from measured gamma spectra.
If one uses the final state model, there are no conversion electrons, the Q value is wrong, but the gamma spectrum agrees with the measured ones.

## Slide 7: Geant4 Gd simulation problems
  https://zzz.physics.umn.edu/lowrad/_media/meeting8/ychen_gdgammas_aarm2015.pdf

## Slide 8: Geant4 Gd simulation problems
  https://zzz.physics.umn.edu/lowrad/_media/meeting8/ychen_gdgammas_aarm2015.pdf

## Slide 9: Geant4 Gd simulation problems
Conversion electrons, literature and Geant4:
  155Gd: 0.61 - 0.79 (Geant4 1.25)
  157Gd: 0.60 - 0.61 (Geant4 0.45)
  Nat Gd: 0.6 – 0.66 (Geant4 0.66)
For natural Gd the combined results looks ok (by accident? Isotope composition and cross sections seem to balance out the error), about 0.66 conversion electrons per neutron.
For the efficiency not only the conversion electrons per neutron is interesting, but in how many cases at least one conversion electron is produced.
In some cases 2,3 or 4 ce are produced, maybe not correct in Geant4?
Spectra of ce look correct though

## Slide 10: CE Spectrum in Gd converter
For all simulation, thermal neutrons and a natural Gd converter were used. The gas in the detector is ArCO2 (70%/30%)

## Slide 11: Efficiency simulations

## Slide 12: CE Spectrum in drift

## Slide 13: Percentiles of deposited energy ce

## Slide 14: CSDA Range and maximum penetration depth of ce

## Slide 15: CE track

## Slide 16: Mean deposited energy gammas

## Slide 17: Detection efficiency gammas

## Slide 18: Detection efficiency gammas based on threshold
Threshold where 10% of ce are lost
Threshold where 25% of ce are lost

## Slide 19: Outlook
The efficiency and ce simulations and measurements have been published
D. Pfeiffer et al., First measurements with new high-resolution gadolinium-GEM neutron detectors, JINST 11 (2016)
To come:
Publication of the gamma simulations
Track simulations and simulated position resolution using the Geant4/Garfield interface (Collaboration with Carsten Sogaard)
Code written, but simulations have to be run and results analysed