## Slide 1: The Bifrost spectrometer
Science case, outline and requirements
Rasmus Toft-Petersen
Technical University of Denmark

## Slide 2: Outline
Motivation
Science case
Operating principle
Technical requirements

## Slide 3: Bifrost motivation
Flux in reactor:
1015 n/s/cm2
Monochromatic flux at sample: 108 n/s/cm2
Typical detector count rate: 0.5-5 cts/s
Current state-of-the-art:
Mono Flux | 107-108 n/s/cm2
Spatial angle | 0.015 steradians
Energy transfer | Single value
Triple-axis spectrometer
Mono Flux | 105-106 n/s/cm2
Spatial angle | 3 steradians
Energy transfer | Continuous
Time-of-flight
spectrometer
In both cases, getting the full picture takes about a week

## Slide 4: Bifrost motivation
Three main reasons for building BIFROST:
Flux optimization for weak signals
Parametric overview studies
Optimization for sample environment
Poly Flux | 109-1010 n/s/cm2
Spatial angle | 0.1 steradians pr. Ef
Energies pr Q-channel | Continuous
SE performance | Great
BIFROST
Bifrost
aims to perform
efficient overview studies with triple-axis flux:
Polychromatic beam,
large detector angular coverage and multiple analyser energies
makes this possible!
Bifrost will have enough flux and probe a large enough (Q, E)-range
to see the unexpected and to sacrifice flux for resolution!

## Slide 5: Bifrost motivation
Three main reasons for building BIFROST:
Flux optimization for weak signals
Parametric overview studies
Optimization for sample environment
Poly Flux | 109-1010 n/s/cm2
Spatial angle | 0.1 steradians pr. Ef
Energies pr Q-channel | Continuous
SE performance | Great
BIFROST
Bifrost
aims to perform
efficient overview studies with triple-axis flux:
Polychromatic beam,
large detector angular coverage and multiple analyser energies
makes this possible!
Bifrost will have enough flux and probe a large enough (Q, E)-range
to see the unexpected and to sacrifice flux for resolution!

## Slide 6
Magnetism in superconductors
J. Chang et al, Physical Review Letters 102 , 177006 (2009)
Gap
Applied magnetism:
Magnetic excitations, the electron-glue in the high-Tc superconductors?
This entire field is limited by lack of neutron flux
A. Boothroyd, et al. Nature 2011

## Slide 7
Quantum magnetism
Fundamental magnetism: as the quantum critical point is reached, the golden ratio
pops out!
R.Coldea, et. al, Science, 327 (2010)

## Slide 8
Crystal growth as the main limitation
Organic superconductors - electrocrystallization
Many ionic conductors are magnets – flux growth
C. Stock, et. Al. PRL (2009) NaMnO2 Powder
A. Boothroyd, et. Al. PRL (2004) 0.25 cm2 sample Na0.75CoO2

## Slide 9
Pressure studies
Pressure changes structure and the exchange path. Detailed parametric studies could allow complicated theories for exchange to be tested more precisely. DFT? Dzyaloshinsky-Moriya?
Phonons under pressure: Structural phase transitions? Lifetimes? Phonons near melting points?
Yu, et al, Scientific Reports, SnSe (2016). Phonons in Iron near TC DFT+measurements

## Slide 10
A new opportunity:
Earth science
New option: Efficient low resolution QENS at high pressures. Can’t be done
With X-rays or backscattering
Earth science: Dynamics of water in earths mantle

## Slide 11
Soft matter
In membranes, collective dynamics are believed to drive transport of molecules, pore opening, membrane fusions and protein-protein interactions
M. C. Rheinstädter, PRL (2004)

## Slide 12: The beamline

## Slide 13: Operating principle: primary spectrometer
Combine a long
instrument with
long-pulsed source.
Flight time: 100 ms

## Slide 14: Operating principle: secondary spectrometer
Pyrolythic graphite is transparent at E < 5 meV
Efficient use of pyrolytic graphite and a long primary flight path is a powerful cocktail in a single scattering plane
We can over 0.5 ster in the scattering plane: A compression of the capabilities of a TOF spectrometer

## Slide 15: The chopper system
A relatively simple chopper setup
1 fast double-disc PSC chopper
3 slow frame overlap choppers
A fast chopper before sample enables order sorting

## Slide 16: Improving the backend resolution
The prismatic analyzer concept (Jonas Okkels Birk): Use broad PG mosaicity and distance collimation.
Resolution
at the Ef = 5 meV
Analyzer -> 70 µeV.
Match the PSC to this analyzer and achieve unprecented flux and resolution at Ei = 15 meV

## Slide 17: Sample environment
BIFROST can keep
elastic sample environment
scattering in the elastic line due to the long flightpath! Direct geometry ToF cannot
4 seasons, JPARC

## Slide 18: Main requirements
1.7 Å bandwidth
Polychromatic flux > 1010 n/s/cm2
PSC: Pulse duration 0.1-3.1 ms
Beam size: 2x2 cm
Divergence < 0.75 degrees
Flexible E-resolution, 30-170 μeV
Angular resolution 0.7 degrees
10 analysers pr Q-channel
Order sorting chopper
120 degree angular coverage
Moveable evacuated tank
Translateable filter+collimator
Temperatures below 50 mK
Magnetic fields above 15 T
Pressures above 2 GPa
Primary spectrometer
Secondary spectrometer
Sample environment

## Slide 19
Schedule considerations
PSI CAMEA → Many of the technical solutions and the prototyping regarding the secondary spectrometer are in place: PG holders, crosstalk shielding, Be-filter.
The Bifrost team is strong, we believe we can be ready for user operation in 2023.
IFE: Shielding
Rodion Kolevatov
Isabel Jansa Llamas
LLB: Detectors, tank design polarization, choppers
Philippe Bourges
Sylvain Rodrigues
PSI: Guide, Vacuum housing Be-filter, prototyping
Jonas Okkels Birk
Christof Niedermayer
Felix Groitl
KU: Guide design and more
Kim Lefmann
Martin Olsen
Sonja Holm
DTU: Management and more
Niels Bech Christensen Rasmus Toft-Petersen Lead engineer
Wigner: Slow choppers
Marton Marko

## Slide 20
Schedule considerations
Focus on settling the guide design – early procurement of monolith insert
2017 will mainly focus on guide design, chopper design and shielding design
Tank and detailed detector design will be settled end of 2017, start 2018
Possible early procurement of guide, choppers and the more complicated shielding parts.

## Slide 22: Thank you for your attention