## Slide 1: BEER – Scopes & Budget
Nuclear Physics Institute CAS
Czech Republic
Přemysl Beran
Jan Šaroun
Petr Lukáš
Petr Šittner
Helmholtz-Zentrum Geesthacht
Germany
Jochen Fenske
Dirk Jan Siemers
Martin Müller
Peter Staron
Rüdiger Kiehn
Gregor Nowak
Mustapha Rouijaa
John Hedde
ESS coordinator
Markus Strobl

## Slide 2
BEER – Budget & Configuration
Cost Category Instrument 11.994.402 €
be competitive or even better than other engineering diffractometers
keep flexibility (resolution/intensity, …)
easy to upgrade
stay in budget
deliver best performance possible within budget
World Class Instrument 17.935.509 €
Full Scope Instrument 27.265.819 €
BEER proposal with revised budget
be competitive or even better than other engineering diffractometers

## Slide 3
BEER Overview
01 Shielding & 02 Neutron Optics
03 Choppers
04 Sample Environment
05 Detectors and Beam Monitors
08 Instrument Specific Technical Equipment
09 Instrument Infrastructure
Others (06 DMSC, 07 MCA, 10 Vacuum, 11 PSS)

## Slide 4: Neutron Optics Monolith Insert
Horizontal guide profile with the monolith insert.
Focusing at the thermal moderator:
beam axis angle: + 0.295 deg
beam axis shift: -30 mm at the entry -10 mm at the shutter
bi-spectral extraction
Si blades, m=4, t=0.5 mm
narrow beam section with choppers
beam axis
y, mm
2.12 m
m=4
m=4
m=0 ?

## Slide 5: Neutron Optics Guide Profile
beam expansion, w= 2 cm -> 4 cm, length=10 m
z, mm
m=2.5
m=4 to 2.5
m=2.5 to 5
The profile results from numerical optimization
and subsequent trade-off between cost and
performance.
Focused at the top moderator ( 3cm).
Vertical divergence at the sample ~ 30 mrad.
horizontal
vertical
DLS closed once inside the bunker,
2nd closure is outside (dashed green lines).
Guide 1:
width = 2 cm
length = 18 m
R = -2 km
Guide 2:
width = 4 cm
length = 105.5 m
R = 25 km

## Slide 6: Neutron Optics Performance
Beam brightness at the sample
dashed curves: beam axis focused near the moderators boundary
Option 2:
yields less thermal neutrons
saves shielding cost

## Slide 7
Shielding
Guide Shielding
Before DLS
hd concrete
After DLS
hd concrete
DLS closed
-1 m

## Slide 8
8
Guide Hall
Laboratories
12 m
10 m
8 m
7 m
Cost Category: reduced size
Cave shielding
(Ø 50 cm hd concrete)
Shielding
Experimental Cave

## Slide 9: Neutron Optics Focusing Guide
sample axis
guide exchanger
wall
Beam shaping optics:
vertically focusing guide with exchangeable end section
2 adjustable divergence slits (S1, S2)
adjustable slit S3 for gauge volume definition, variable distance
S1
S2
S3
absorbing walls
divergence
World Class: only two options
Cost Category: no guide exchanger

## Slide 10: 01 Shielding & 02 Neutron Optics Budget
 | Cost Category | World Class | Full Scope
01 Shielding | 2.749.142 | 3.020.398 | 3.020.398
guide shielding + shutters | 2.308.518 | 2.362.118 | 2.362.118
cave shielding | 440.624 | 658.280 | 658.280
02 Neutron Optics | 2.643.000 | 2.791.000 | 2.891.000
Insert+ BS switch | 194.000 | 194.000 | 194.000
chopper section | 98.000 | 98.000 | 98.000
expansion part | 324.000 | 324.000 | 324.000
narrow bent guide | 297.000 | 297.000 | 297.000
transport guide | 1.470.000 | 1.470.000 | 1.470.000
focusing guide | 230.000 | 303.000 | 403.000
adjustable slits 3x | 30.000 | 30.000 | 30.000
guide exchanger |  | 75.000 | 75.000

## Slide 11
BEER Overview
01 Shielding & 02 Neutron Optics
03 Choppers
04 Sample Environment
05 Detectors and Beam Monitors
08 Instrument Specific Technical Equipment
09 Instrument Infrastructure
Others (06 DMSC, 07 MCA, 10 Vacuum, 11 PSS)

## Slide 12
Chopper System
Housing
Part B
Part A
Crane (Lifting)
Motor position
(spindle)
Lid: to guarantee vacuum
Lid
Chopper
remove of chopper without dismantling of the guide

## Slide 13
Part B
Part A
Chopper
Front
Back
Vacuum, etc.
Cooling
Bearing position
Top
Chopper System
Housing

## Slide 14
Ball bearing
Magnetic bearing
Supplier recommendations:
For FAST choppers (fmax ≥ 168 Hz)
     magnetic bearings
For SLOW choppers (fmax ≤ 70 Hz)
   hybrid ball bearings
        Reliability: almost the same
        Cost: lower costs
For slower choppers (fmax ≤ 42 Hz)
     hybrid ball bearings
        Reliability: even better
Chopper System
Bearing System

## Slide 15
Chopper | Name | Function | Speed [Hz] | Bearing Alternative 1 | Bearing Alternative 2
1 | PSC1 (fast) | Pulse Shaping | 168 | Magnetic | Magnetic
2 | PSC2 (fast) | Pulse Shaping | 168 | Magnetic | Magnetic
3 | PSC3 (fast) | Pulse shaping | 168 | Magnetic | Magnetic
4 | MCa (fast) | Modulation | 42-300 | Magnetic | Magnetic
5 | MCb (fast) | Modulation | 42-300 | Magnetic | Magnetic
6 | MCc (slow) | Modulation | 42-70 | Ball | Magnetic
7 | FC1a (slow) | Framing | 14/7 | Ball | Magnetic
8 | FC1b (slow) | Framing | 63/70 | Ball | Magnetic
9 | FC2a (slow) | Framing | 14 | Ball | Magnetic
10 | FC2b (slow) | Framing | 7 | Ball | Magnetic
Chopper System
Bearing System

## Slide 16
Pulse Shaping Chopper
Modulation Chopper
Frame definition Chopper
Chopper System
Overview

## Slide 17
FC1a
FC1b
PSC1
-Diameter: 700 mm
-Slit opening: 144°
- frequency: 168 Hz
PSC2
-Diameter: 700 mm
-Slit opening: 144°
- frequency: 168 Hz
at ~ 6.5m
optically blind setting provides:
constant Dl/l, independent on wavelength
broad variety of resolution options
Chopper System
Pulse Shaping

## Slide 18
Pulse Shaping Chopper
Modulation Chopper
Frame definition Chopper
Chopper System
Overview

## Slide 19
T = 17%
T = 4.4%
T1 = 17%, T2 = 100%
Diameter: 700 mm
Slit opening: 16 x 4°
Slit distance: 22.5°
Diameter: 700 mm
Slit opening: 4 x 4°
Slit distance: 90°
Diameter: 700 mm
Slit opening: 7 x 4°
(slit distance 22.5°)
+ 1 x 180°
for high symmetric materials
for low symmetric materials
to combine SANS and Diffraction
MCa at ~8.95m
MCb at ~ 9m
MCc at ~ 9.5m
Chopper System
Pulse Modulation

## Slide 20
Pulse Modulation :
Pulse Shaping:
Resolution:
Pulse Modulation:
+ high intensity, high resolution for high symmetric materials
- overlap of reflections for low symmetric materials possible
 avoid overlap with frequency below 42Hz  low resolution
Chopper System
Performance

## Slide 21
Pulse Shaping Chopper
Modulation Chopper
Frame definition Chopper
Chopper System
Overview

## Slide 22
Diameter=700 mm
Slit opening: 180°
frequency: 63 Hz or 70 Hz
Pair of FC1
FC1b at ~ 8.32m
Diameter: 700 mm
Slit opening: 70°
frequency: 14 Hz or 7 Hz
FC1a at ~ 8.28m
FC1:
limits the range of wavelengths and
blocks undesired overlaps
FC1b
FC2b
Diameter: 700mm
Slit opening: 180°
frequency: 14 Hz
Diameter: 700 mm
Slit opening: 90°
frequency: 7 Hz
FC2a at ~ 79.55m
FC2b at ~ 79.59m
Pair of FC2
FC2:
operates with FC1 to set the wavelength frame
Chopper System
Frame Definition

## Slide 23
Pulse suppression
(2 x 1.7Å)
Alternating wavelength frames
Only thermal or cold neutrons reach
the sample successively
Chopper System
Performance

## Slide 24
Adequate setting of FC1a and FC1b
pre-selection of thermal and cold neutrons in successive pulses
pulse n: thermal
pulse n+1: cold
Chopper System
Performance

## Slide 25
Pulse Shaping Chopper
Modulation Chopper
Frame definition Chopper
World Class
Cost Category
+ high flexibility (wide resolution range)
- no combination of diffraction and SANS
+ high intensity for high symmetric materials
- almost limited to high symmetric materials
- no extension of wavelength-band
Chopper System
Overview

## Slide 26: 03 Choppers Budget
 | Cost Category | World Class | Full Scope
03 Choppers | 490.050 | 1.990.900 | 2.207.450
PSC1 |  | 218.500 | 218.500
PSC2 |  | 191.550 | 191.550
PSC3 |  | 191.550 | 191.550
CHIM |  | 150.000 | 150.000
MCa | 233.500 | 206.550 | 206.550
MCb |  | 206.550 | 206.550
MCc |  |  | 176.550
CHIM | 40.000 | 40.000 | 80.000
FC1a |  | 176.550 | 176.550
FC1b |  | 176.550 | 176.550
CHIM |  | 40.000 | 40.000
FC2a |  | 176.550 | 176.550
FC2b | 176.550 | 176.550 | 176.550
CHIM | 40.000 | 40.000 | 40.000

## Slide 27
BEER Overview
01 Shielding & 02 Neutron Optics
03 Choppers
04 Sample Environment
05 Detectors and Beam Monitors
08 Instrument Specific Technical Equipment
09 Instrument Infrastructure
Others (06 DMSC, 07 MCA, 10 Vacuum, 11 PSS)

## Slide 28: Sample Environment Overview
Stress rig:
Dilatometer:
commercial dilatometer (Bähr 805 A/D)
induction heating: – max. heating rate 4000 K/s – max. cooling rate 2500 K/s (hollow samples)
DSC unit
deformation units (compr., tension; 25 kN)
World Class
Cost Category
max. force 60 kN
vacuum chamber
resistive and inductive heating 1100° C
friction stir welding
laser welding
Welding devices:

## Slide 29: 04 Sample Environment Budget
 | Cost Category | World Class | Full Scope
04 Sample Environment | 0 | 330.000 | 1.130.000
Stress-rig + furnace | 0 | 300.000 | 300.000
Coordinate measuring machine | 0 | 30.000 | 30.000
Laser and stir welding | 0 | 0 | 400.000
Dilatometer | 0 | 0 | 400.000
+ pool SE and other collaborations

## Slide 30
BEER Overview
01 Shielding & 02 Neutron Optics
03 Choppers
04 Sample Environment
05 Detectors and Beam Monitors
08 Instrument Specific Technical Equipment
09 Instrument Infrastructure
Others (06 DMSC, 07 MCA, 10 Vacuum, 11 PSS)

## Slide 31
D1 – D4: 1 x 1 m² (res. 2 mm x 5 mm)
arc: 3 x (0.5 x 0.5 m²) (res. 5 mm x 5mm)
SANS: 0.5 x 0.5 m² (res. 5 mm x 5 mm)
D5 (backscattering): 0.5 x 0.5 m²
            (res. 5 mm x 5 mm)
Imaging:  ODIN
η > 60 % ( 2 Å)
countrate < 106 1/s (global)
Requirements:
D1 - D2: 0.5 x 0.5 m² (res. 5 mm x 5 mm)
World Class
Cost Category
10B4C converter blades
MWPC
FPGA readout
Technologies:
Detectors
Overview

## Slide 32
D1 – D4: 1 x 1 m² (res. 2 mm x 5 mm)
arc: 3 x (0.5 x 0.5 m²) (res. 5 mm x 5mm)
SANS: 0.5 x 0.5 m² (res. 5 mm x 5 mm)
D5 (backscattering): 0.5 x 0.5 m²
            (res. 5 mm x 5 mm)
Imaging:  ODIN
η > 60 % ( 2 Å)
countrate < 106 1/s (global)
Requirements:
D1 - D2: 0.5 x 0.5 m² (res. 5 mm x 5 mm)
Instrument (option) | sample-dete. dis. | Detector size [m2] | Detector coverage [sr]
BEER (FS) | 1.2 m - 2 m | 5.25 | 1.63
BEER (WC) | 2 m | 2 | 0.5
BEER (CC) | 2 m | 0.5 | 0.125
TAKUMI | 2 m | 2.46 | 0.62
ENGIN-X | 1.53 m | 2.06 | 0.88
VULCAN | 2 m | 1.75 | 0.44
SMARTS | 1.50 m | 1.30 | 0.58
Detectors
Overview

## Slide 33
d-spacing:
pole figure coverage:
World Class
Cost Category
Detectors
Performance
82° .. 98°

## Slide 34
D1 – D4: 1 x 1 m² (res. 2 mm x 5 mm)
arc: 3 x (0.5 x 0.5 m²) (res. 5 mm x 5mm)
SANS: 1 x 1 m² (res. 5 mm x 5 mm)
D5 (backscattering): 0.5 x 0.5 m²
            (res. 5 mm x 5 mm)
Imaging:  ODIN
η > 60 % ( 2 Å)
countrate < 106 1/s (global)
Requirements:
Cost Category
Detectors
Surrounding

## Slide 35: 05 Detectors Budget
 | Cost Category | World Class | Full Scope
05 Detector and Beam Monitors | 1.663.500 | 2.888.900 | 9.068.750
Beam monitor | 20.000 | 20.000 | 20.000
Beam monitor | 20.000 | 20.000 | 20.000
Am 0.5 x 0.5 (arc detector) |  |  | 
Hardware | 550.000 | 0 | 550.000
Readout electronics | 89.400 | 0 | 89.400
Coating | 38.400 | 0 | 38.400
Radiacollimator | 20.000 | 0 | 80.000
Hardware | 440.000 | 0 | 440.000
Readout electronics | 89.400 | 0 | 89.400
Coating | 38.400 | 0 | 38.400
Radiacollimator | 20.000 | 0 | 80.000
Hardware | 0 | 0 | 440.000
Readout electronics | 0 | 0 | 89.400
Coating | 0 | 0 | 38.400
Radiacollimator | 0 | 0 | 80.000
arc detectorportal | 0 | 0 | 446.500

## Slide 36: 05 Detectors Budget
 | Cost Category | World Class | Full Scope
05 Detector and Beam Monitors | 1.663.500 | 2.888.900 | 9.068.750
Am 1 m x 1m |  |  | 
Hardware | 0 | 1.026.000 | 1.026.000
Readout electronics | 0 | 89.400 | 89.400
Coating | 0 | 153.600 | 153.600
Radiacollimator | 0 | 90.000 | 90.000
Detectorportal | 247.450 | 287.450 | 287.450
Hardware | 0 | 750.000 | 750.000
Readout electronics | 0 | 89.400 | 89.400
Coating | 0 | 153.600 | 153.600
Radiacollimator | 0 | 90.000 | 90.000
Detectorportal | 90.450 | 119.450 | 119.450
Hardware | 0 | 0 | 750.000
Readout electronics | 0 | 0 | 89.400
Coating | 0 | 0 | 153.600
Radiacollimator | 0 | 0 | 90.000
Detectorportal | 0 | 0 | 119.450
Hardware | 0 | 0 | 750.000
Readout electronics | 0 | 0 | 89.400
Coating | 0 | 0 | 153.600
Radiacollimator | 0 | 0 | 90.000
Detectorportal | 0 | 0 | 119.450

## Slide 37: 05 Detectors Budget
 | Cost Category | World Class | Full Scope
05 Detector and Beam Monitors | 1.663.500 | 2.888.900 | 9.068.750
Backscattering |  |  | 
Hardware | 0 | 0 | 440.000
Readout electronics | 0 | 0 | 89.400
Coating | 0 | 0 | 38.400
Radiacollimator | 0 | 0 | 30.000
detectorportal | 0 | 0 | 109.450
SANS |  |  | 
Hardware | 0 | 0 | 440.000
Readout electronics | 0 | 0 | 89.400
Coating | 0 | 0 | 38.400

## Slide 38
BEER Overview
01 Shielding & 02 Neutron Optics
03 Choppers
04 Sample Environment
05 Detectors and Beam Monitors
08 Instrument Specific Technical Equipment
09 Instrument Infrastructure
Others (06 DMSC, 07 MCA, 10 Vacuum, 11 PSS)

## Slide 39: 08 Instrument Specific Technical Equipment Overview
Hexapod:
high load table:
six axis robot:
payload 2 t
x, y: ±200 mm
z: ±250mm
payload 3 t
rotation ±180°
z: ± 500 mm
payload 14 kg
repeatability : ±0.06 mm
Cybaman:
payload 25 kg
linear stages:
payload 300 kg
travel 1000 mm
accuracy ±26.9 µm
World Class
Cost Category
payload 2 t
rotation ±180°
z: ± 500 mm

## Slide 40: 08 Instrument Specific Technical Equipment Budget
 | Cost Category | World Class | Full Scope
08 Instrument Specific Technical Equipment | 2.982.950 | 4.187.050 | 5.366.750
Phase 1 | 471.850 | 471.850 | 471.850
Travel | 125.000 | 300.000 | 300.000
Personnel | 2.156.400 | 2.749.500 | 3.027.000
high load table | 200.000 | 300.000 | 300.000
hexapod 2t | 0 | 200.000 | 200.000
cybaman | 0 | 0 | 71.000
six axis robot | 0 | 36.000 | 36.000
linear stage x | 9.900 | 9.900 | 9.900
linear stage y | 9.900 | 9.900 | 9.900
linear stage z | 9.900 | 9.900 | 9.900
positioning control | 0 | 100.000 | 100.000
SANS scattering tube | 0 | 0 | 831.200

## Slide 41
BEER Overview
01 Shielding & 02 Neutron Optics
03 Choppers
04 Sample Environment
05 Detectors and Beam Monitors
08 Instrument Specific Technical Equipment
09 Instrument Infrastructure
Others (06 DMSC, 07 MCA, 10 Vacuum, 11 PSS)

## Slide 42
Personnel
Access
Control hutch
Equipment
Access
Heavy load
table < 3 t
elevated floor
Guide Hall
Laboratories
Cave shielding
10 m
12 m
Cost Category:reduced size
7 m
8 m
Instrument Infrastructure
Experimental Cave

## Slide 43
Control hutch
Equipment
Access
Lift ~5t
Storage + Lab
Space
Access to
cables, etc.
Guide Hall
Laboratories
Cost Category: reduced size
Instrument Infrastructure
Experimental Cave

## Slide 44: 09 Instrument Infrastructure Budget
 | Cost Category | World Class | Full Scope
09 Instrument Infrastructure | 160.000 | 780.000 | 780.000
Instrument Cave | 100.000 | 500.000 | 500.000
Control hutch | 60.000 | 280.000 | 280.000

## Slide 45
BEER Overview
01 Shielding & 02 Neutron Optics
03 Choppers
04 Sample Environment
05 Detectors and Beam Monitors
08 Instrument Specific Technical Equipment
09 Instrument Infrastructure
Others (06 DMSC, 07 MCA, 10 Vacuum, 11 PSS)

## Slide 46: Others – Budget (06 DMSC, 07 MCA, 10 Vacuum & 11 PSS)
 | Cost Category | World Class | Full Scope
06 Data Acquisition and Analysis | 0 | 0 | 0
07 Motion Control and Automation | 115.360 | 139.760 | 145.760
EPICS integration | 9.800 | 11.200 | 13.200
Network | 12.600 | 14.000 | 15.000
control rack, etc. | 92.960 | 114.560 | 117.560
10 Vacuum | 0 | 0 | 0
11 PSS | 100.000 | 177.000 | 177.000

## Slide 47: Cost Category Instrument Summary
All optical devices (extraction system, no guide exchanger,…)
Only MCa and FC2b
Only ±90° detectors (reduced size)
No SANS option
No Sample Environment (only pool SE)
reduced size of experimental cave
no platform for easy transport of SE and equipment
- fully included
- easy to upgrade
- cost & time intensive upgrade

## Slide 48: Cost Category Instrument Upgrade & Staging
Upgrades to full scope:
Reconstruction of Experimental Cave
Detectors D1 & D2 (full size)
exchange of guide segments
Pulse shaping choppers PSC1 – PSC3
Frame definition choppers FC1a/b, Fc2a
Hexapod
Robot
Arc detectors
backscattering detector
SANS
……
 time + cost intensive

## Slide 49
World Class Instrument
Summary
All optical devices (extraction system, focusing guide, guide exchanger 2 options, …)
all Choppers except MCc
Only ±90° detectors
No SANS option
Stress rig with furnace
full size of experimental cave
platform for easy transport of SE and equipment
- fully included
- easy to upgrade
- cost & time intensive upgrade

## Slide 50
Upgrades to full scope:
Detector D4
Arc detector
Backscattering detector
Detector D3
SANS option
    +
1. biaxial stress rig
2. digital image correlation
3. annealing furnace
4. welding devices
5. Gleeble® simulator
World Class Instrument
Upgrade & Staging

## Slide 51
Full Scope Instrument
Summary
All optical devices (extraction system, focusing guide, guide exchanger, …)
all Choppers
Full detector coverage
SANS option
Stress rig, dilatometer, …
full size of experimental cave
platform for easy transport of SE and equipment
- fully included
- easy to upgrade
- cost & time intensive upgrade

## Slide 52: BEER Instrument Performance Summary
Cost Category:
World Class:
Full Scope:
Instrument (option) | sample-dete. dis. | Detector size [m2] | Detector coverage [sr]
BEER (FS) | 1.2 m - 2 m | 5.25 | 1.63
BEER (WC) | 2 m | 2 | 0.5
BEER (CC) | 2 m | 0.5 | 0.125
TAKUMI | 2 m | 2.46 | 0.62
ENGIN-X | 1.53 m | 2.06 | 0.88
VULCAN | 2 m | 1.75 | 0.44

## Slide 53: BEER Instrument Performance Summary
Cost Category:
World Class:
Full Scope:
Instrument (option) | sample-dete. dis. | Detector size [m2] | Detector coverage [sr]
BEER (FS) | 1.2 m - 2 m | 5.25 | 1.63
BEER (WC) | 2 m | 2 | 0.5
BEER (CC) | 2 m | 0.5 | 0.125
TAKUMI | 2 m | 2.46 | 0.62
ENGIN-X | 1.53 m | 2.06 | 0.88
VULCAN | 2 m | 1.75 | 0.44

## Slide 54: BEER Instrument Scientific Scope
 | Cost Category | World Class | Full Scope
In situ & in operando | (reduced d- range, limited SE, difficult multiphase analysis) | (reduced d-range, not full SE suite) | 
Strain scanning | (limited positioning system capabilities and precision) | (reduced d-range) | 
Texture & texture evolution | (significant reduced pole figure coverage) | (slight pole figure coverage) | 
Long term experiments | (no transport platform) |  | 
 | Not competitive to existing instruments | Competitive to or exceeding existing instruments | Competitive to or exceeding existing instruments

## Slide 55: BEER Instrument System Requirements
 | Cost Category | World Class | Full Scope
#1 nuclear and magnetic structure |  |  | 
#2 in situ & in operando | (limited SE for engineering) | (not full SE suite) | 
#3 residual strain | (limited sample complexity, load and throughput) |  | 
#4 microstructure | (microstructure except microstrain) |  | 
#5 long term experiments | (no transport platform, no lift) |  | 
#6 d-range | (reduced detector size and coverage) | (reduced detector coverage) | 
#7 pole figure coverage | (significant reduced detector coverage) | (reduced detector coverage) | 
#8 texture evolution | (significant reduced detector coverage) | (reduced detector coverage) | 
– fully included – easy to upgrade – time and cost intensive upgrade (reconstruction necessary)

## Slide 56: BEER Instrument System Requirements
 | Cost Category | World Class | Full Scope
#9 two strain components |  |  | 
#10 continuation measurements |  |  | 
#11 sample environment driven |  |  | 
#12 gauge volume | (Only one set of collimators) |  | 
#13 dmin |  |  | 
#14 d- resolution | (only 1 modulation Chopper) |  | 
#15 space for SE |  |  | 
#16 heavy samples | (limited load of heavy table) |  | 
#17 SANS | (no SANS option) | (no SANS option) | 
#18 direct imaging |  |  | 
– fully included – easy to upgrade – time and cost intensive upgrade (reconstruction necessary)

## Slide 57: BEER Instrument Budget Summary
 | Cost Category | World Class | Full Scope
01 Shielding | 2.749.142 | 3.020.398 | 3.020.398
02 Neutron Optics | 2.643.000 | 2.791.000 | 2.891.000
03 Choppers | 490.050 | 1.990.900 | 2.207.450
04 Sample Environment | 0 | 330.000 | 1.130.000
05 Detector | 1.663.500 | 2.888.900 | 9.068.750
06 Data Acquisition and Analysis | 0 | 0 | 0
07 Motion Control and Automation | 115.360 | 139.760 | 145.760
08 Instrument Specific Technical Equipment | 2.982.950 | 4.187.050 | 5.366.750
09 Instrument Infrastructure | 160.000 | 780.000 | 780.000
10 Vacuum | 0 | 0 | 0
11 PSS | 100.000 | 177.000 | 177.000
12 Contingency | 1.090.400 | 1.630.501 | 2.478.711
Total | 11.994.402 | 17.935.509 | 27.265.819
Person years | 19.9 | 25.2 | 27.7

## Slide 58
Thank you for your attention!