## Slide 1
MIRACLES SCOPE (1/2)
Primary Spectrometer & Sample Environment

## Slide 2
PRIMARY SPECTROMETER
  Neutron Guide
  Guide Shielding
  Chopper Cascade
  Slits
SAMPLE ENVIRONMENT
  Configuration 1
  Configuration 2
  Configuration 3
Outline
Fixed for all Configurations
5.7 M€
76.5 k€
611 k€
1031.5 k€

## Slide 3
Superpolished
Copper
Aluminum
Borkron Glass N-BK7
Guide
Substrates
Starts at 2m from the moderator & ends at 162.5 m
9 guide sections, m values: 1.5 to 4
Substrates & coating, 2676 k€
Vacuum system, 704 k€ (no vacuum pumps)
  A 2m long vacuum aluminum system + integrated 3mm B4C shielding = is about 4.4 k€/m for 12 x 12 cm2. Included rubber sleeves and clamps to connect the 2m long vacuum housings.
Steel support structure, 96 k€. (0,6 k€/m)
Installation, alignment and documentation, 192 k€. (1.2 k€/m for guide+support)
Substrates and coatings quotation from Swiss Neutronics
Vacuum housing, support structure and installation quotes from S-DH
1
2
3
4
5
6
7
8
9
Bunker R ≤ 28 m
Guide Hall / E02 R ≤ 154.5 m
Instrument Hall / E01
R ≤175.7 m
Sample
Moderator
Monolith R ≤ 6 m
Primary Spectrometer: Neutron Guide
Total price: 3668 k€
DESCRIPTION
COSTING

## Slide 4
Neutron Guides – Detailed Costing
ID | Length [m] | Dimensions [cm2] | m value | Substrate | Curvature [m] | Total Cost [k€]
Section 1 | 5 | 6 x 7.5 4 x 12 | 3 | Superpolished Copper |  | 144
Section 2 | 0.5 | 4x12, 4.3x12 | 3 | Aluminum |  | 13.9
Section 3 | 9 | 4.3x12, 11x12 | 3 | Aluminum |  | 283.8
Section 4 | 6 | 11x12, 11x12 | 1.5 | Aluminum |  | 130.4
Section 5 | 32.5 | 11x12, 11x12 | 2 | Borkron Glass N-BK7 | 5000 | 542.2
Section 6 | 1.15 | 11x12, 11x12 | 1.5 | Borkron Glass N-BK7 |  | 14.7
Section 7 | 22.5 | 11x12, 11x12 | 2 | Borkron Glass N-BK7 | 5000 | 375.4
Section 8 | 75 | 11x12, 11x12 | 1.5 | Borkron Glass N-BK7 |  | 957.5
Section 9 | 7 | 11x12, 3.2x3.2 | 4 | Borkron Glass N-BK7 |  | 214.2

## Slide 5
Primary Spectrometer: Guide Shielding
Primary layer shielding: Steel, 606.6 k€. 50.55 m3, 404.4 tonnes
(12000 €/m3, 1500 €/tonne)
Secondary layer shielding: Concrete, 203.2 k€.
254 m3 (800 €/m3)
SHIELDING CROSS SECTION
Shielding sections along the beamline:
Methodology according to ESS NOSG Cost Calculation Process
Total: 809.8 k€
(Shielding inside the bunker R<28 m is provided by ESS)
Section | Length (m) | Grounding Zone | Distance from moderator [m] | m value
A | 17 | Instrument Hall 2/D03 | 45 | 2
B | 5 | Instrument Hall 2/D03 | 50 | 2
C | 27.5 | Guide Hall / E02 | >50 | 2
D | 78 | Guide Hall / E02 | >50 | 1,5
E | 7 | Instrument Hall 3/ E01 | >50 | 4

## Slide 6
Chopper Cascade
Total: 1185.5 k€
Source: ESS Neutron Chopper Systems Costing Estimate
Chopper assemblies, 682.6 k€
CHIM, 199 k€
Support System (Vacuum, Cooling), 18 k€
Control System, 201.2 k€
Installation activities, 84.7 k€
5 chopper assemblies: PWD pair,
PS pair
3 WBD/FO chopper assembly.

## Slide 7
Chopper Cascade, Detailed costing
Chopper 5 inside the bunker  +10%
Inside the bunker = +10%
Inside the bunker = +10%
At least one per grounding zone. (Bunker + E02)
1 drive per axis. (-10% if 5 or more units used)
For choppers inside the bunker. 1 per M.rack
+20% per additional axis after the first.
Incl. Flanges, tubes.+15% per assembly after 1st.
For the fast PWD chopper assembly
One per assembly. +30% after the first assembly.
One per assembly. +30% after the first assembly.
One per assembly. +30% after the first assembly.
Labour cost = 84.7 k€
Non labour cost = 1100.75 k€

## Slide 8
Slits
1 Pre-sample slit
Motorized slit has 4 motors
Operation under vacuum 10-3 mbar
Absorbing material B4C in resin on Cd plate
Control cabin control software for Windows system
Both the slit size and beam center axis position can be adjusted over the whole cross section of 5 x 5 cm2
60 k€ with motors
40 k€ without motors
Total: 60 k€
Source: Mirrotron

## Slide 9
Sample environment
  All our quotations of SE have been discussed with Harald Schneider.
  CONFIGURATION 1: minimum contribution to pool (1224 k€ /16 = 76.5 k€).
  CONFIGURATION 2:
    Essential scope for day 1:
      Orange cryofurnace (SAD-TEFI; 2-600 K; plug&play). 50 k€
      Top loading CCR, with customer high temperature option. 80 k€
      High temperature furnace. 75 k€
      Humidity chamber 100 k€
    Scope that can be designed and installed during user operation stage, in close collaboration with SAD:
      Orange cryofurnace (SAD-TEFI; 2-600K; plug&play; with sample changer 10-20 samples). 250 k€
      Gas process handling, special dedicated cells. 200 k€
      High pressure cell. 50 k€
      Electromagnet. 50 k€
      Laser pump probe setup. 200 k€
    6 kV HV supply. 25 k€
    ESS support. 76.5 k€
    Commissioning and first real test. 180 k€ (labour)
Configuration 2
Total: 611 k€
431.5 k€ non labour
Configuration 1
Total: 76.5 k€

## Slide 10
Sample environment
  All our quotations of SE have been discussed with Harald Schneider.
  CONFIGURATION 3 (or Configuration 2 upgrade):
    Basic equipment + humidity chamber. 355 k€
    ESS support. 76.5 k€
    Clamp cells. 50 k€.
    In-situ gas adsorption measurements. 250 k€.
    Commissioning & first test & continuous user operation. 300 k€ (labour).
Configuration 3
Total: 1031.5 k€
731.5 k€ non labour