## Slide 1: BrightnESS Task 5.1 Questions around VMM3 data processing
Troels Blum, Stig Skelboe, Carsten Søaard

## Slide 2: First measurements
[1] D. Pfeiffer et al.: First measurements
with new high-resolution
gadolinium-GEM neutron detectors,
Journal of Instrumentation, May 2016.
APV25 chip
Neutron event, external triggering
Charge trace per strip
Several extremes per strip

## Slide 3: NMX detector
VMM3 chip
Self triggered, peak value, peak time
First charge peak per strip
Latency: 250 ns + peak time
Neutron event segmentation required

## Slide 4: Electron pulses - 1
A single APV25 output pulse (strip 9 [1]) and a deconvolution of the pulse,
approximately 75 ns duration. The impulse respons of the APV25 shaping amplifier is:
h(t)=t exp(-t/𝜏) where 𝜏=50 ns, h(𝜏) is maximum.

## Slide 5: Electron pulses - 2
A double pulse recorded at strip 5 [1] which after deconvolution turns out to be triple,
with a duration of approximately 350 ns

## Slide 6: Neutron event validation
At a given time, the sum of the charges on the x-strips must equal the sum of the
charges on the y-strips. The output from the VMM3 chip limits this test considerably.
Figures from [1]

## Slide 7: Current activities
Simulation of conversion electron traces
  Understand conversion electron trajectory
  Identify multiple events
  Validate detector algorithm
Data analysis
  Rate of multiple extremes in the charge profiles, i.e. C or U shaped neutron events
  Characterization of a typical charge profile
  Generation of VMM3 style data and evaluation of the accuracy of the reconstructed data
  Data for experiments with segmentation: various degrees of overlap

## Slide 8: Future activities
Segmentation, properties of VMM3 output
  Charge amplitude of the first peak of an event
  Corresponding time, time resolution 25 ns (12 MSB of 20 bit time)
  A full neutron event is assumed to last no more than 600 ns
  Reconstruction of the charge profile assumes just one peak
  At a given time, the total charge collected by the x-strips equals the total charge collected by the y-strips (the charge condition)
Experiment simulation
  Evaluate the spatial resolution of the detector.
  Identify spurious detector signals
  Estimate maximum local data rates