## Slide 1: Event Formation Unit: Event Formation Pipeline
Morten Jagd Cristensen
www.europeanspallationsource.se
7 November 2016

## Slide 2: System overview

## Slide 3: System overview
Two data streams per instrument
  Detector Data / EPICS Data
Event Formation processes Detector data
Events are streamed to Aggregator (kafka) for later filewriting to persistent storage

## Slide 4: Event Formation Unit (EFU)
One EFU per detector panel
Direct fiber connection (10G)
EFU is pure multi core software processing (if possible)
Switched Ethernet on the output side

## Slide 5: EFU Pipeline and Stages

## Slide 6: EFU Pipeline and Stages
input
distributor
distribute data to multiple processing cores (load balancing)
validator
detect invalid data (crc errors, etc.)

## Slide 7: EFU Pipeline and Stages
input
distributor
distribute data to multiple processing cores (load balancing)
validator
detect invalid data (crc errors, etc.)
processing
collection
pick up data until enough to process
rejection
reject data (noise, artifacts, simultaneous, ...)
clustering
determine a dataset suitable for event calculation
event calculation
generate <time, detector pixel id> tuple

## Slide 8: EFU Pipeline and Stages
input
distributor
distribute data to multiple processing cores (load balancing)
validator
detect invalid data (crc errors, etc.)
processing
collection
pick up data until enough to process
rejection
reject data (noise, artifacts, simultaneous, ...)
clustering
determine a dataset suitable for event calculation
event calculation
generate <time, detector pixel id> tuple
output
serialization
convert data structures to buffers for transmission
sorting
sort data by time or pixel id
producer
transmit data to Kafka cluster

## Slide 9: Processes, plugins and pipelines
EFU is a single linux process with pthreads
Detectors are loadable (supports test versions)
Contains the input, processing and output functions

## Slide 10: Current status
Software event processing pipeline
  From System Architecture document
  Current is prototype 2
  Implements CSPEC and TREX fully, NMX not so much yet
CSPEC (TREX) data generator
  Transmits over Ethernet
  Single packets or continuous transmission
Kafka producer
  Buffers event data into 1MB and transmits

## Slide 11: Pipeline SW Architecture
input
processing
output
Eth. RingBuffer <9000>
Lockless FIFO <int>
pthread
pthread
pthread
Prototype Pipeline Process v2
UDP
TCP
input thread writes data to buffers by socket receive()
processing thread reads data from RingBuffer, writes (event) data to event RingBuffer
output thread reads (event) data from RingBuffer and appends to Kafka transmit buffer. Sends when full.
No dynamic allocation of memory, no mutexes, small data structures, minimal copying.
Event RingBuffer <12> (
Lockless FIFO <int>

## Slide 12: Summary
Working prototype ready to accept more realistic data than what is currently being generated (by DMSC)
Further Information
Event processing software
  https://bitbucket.org/europeanspallationsource/event-processing-sw-experiments.git
Continuous Integration
  https://jenkins.esss.dk/dm/job/event-processing-sw-experiments/
System Architecture
  https://ess-ics.atlassian.net/wiki/display/DMSC/Event+Formation+Files

## Slide 14: Producer
Producer
0
1
2
3
4
5
6
7
Continuous memory of N buffers of size S
Lock less FIFO of N unsigned ints (index)
1
0
7
6

## Slide 15: Producer
Producer
  idx = getindex() // idx is now 2
0
1
2
3
4
5
6
7
Continuous memory of N buffers of size S
Lock less FIFO of N unsigned ints (index)
1
0
7
6

## Slide 16: Producer
Producer
  idx = getindex() // idx is now 2
  buffer = getbufferdata(idx)
  rx = receive(buffer, getmaxbuffersize())
0
1
3
4
5
6
7
Continuous memory of N buffers of size S
Lock less FIFO of N unsigned ints (index)
1
0
7
6
2

## Slide 17: Producer
Producer
  idx = getindex() // idx is now 2
  buffer = getbufferdata(idx)
  rx = receive(buffer, getmaxbuffersize())
  setdatalength(rx)
  push(index)
0
1
3
4
5
6
7
Continuous memory of N buffers of size S
Lock less FIFO of N unsigned ints (index)
1
0
7
6
2
2

## Slide 18: Producer
Producer
  idx = getindex() // idx is now 2
  buffer = getbufferdata(idx)
  rx = receive(buffer, getmaxbuffersize())
  setdatalength(rx)
  push(index)
  nextbuffer()
0
1
3
4
5
6
7
Continuous memory of N buffers of size S
Lock less FIFO of N unsigned ints (index)
1
0
7
6
2
2

## Slide 19: Producer
0
1
3
4
5
6
7
Continuous memory of N buffers of size S
Lock less FIFO of N unsigned ints (index)
1
0
7
6
2
2
Producer
  idx = getindex() // idx is now 2
  buffer = getbufferdata(idx)
  rx = receive(buffer, getmaxbuffersize())
  setdatalength(rx)
  push(index)
  nextbuffer()
Consumer

## Slide 20: Consumer
Producer
  idx = getindex() // idx is now 2
  buffer = getbufferdata(idx)
  rx = receive(buffer, getmaxbuffersize())
  setdatalength(rx)
  push(index)
  nextbuffer()
Consumer
  idx = fifo.pop() // idx is now 6
  buffer = getbufferdata(idx)
  createevent(buffer)
0
1
3
4
5
6
7
Continuous memory of N buffers of size S
Lock less FIFO of N unsigned ints (index)
1
0
7
2
2