## Slide 1: High-Resolution Gadolinium-GEM Neutron Detectors for the NMX Instrument at ESS
09.11.2016
This work was partially funded by the EU Horizon 2020 framework, BrightnESS project 676548
Dorothea Pfeiffer

## Slide 2: NMX detectors

## Slide 3: Reflections of example crystal
NMX: Macromolecular Diffractometer
Science goal: Protein crystallography with neutrons

## Slide 4: TOF separation of reflections

## Slide 5: Requirements and challenges
200 μm position resolution (beyond state of art for time resolved neutron detectors)
High rate requirements with up to MHz/cm2
High gain stability and count rate stability
Mechanical robustness (detectors mounted on freely movable robotic arms)
Reasonable gamma suppression
Idea: Use GEM detector with Gd converter
GEM foil
Electrical field in holes

## Slide 6: Gd-GEM backwards setup
neutron
conversion electron
Start of track

## Slide 7: 10B4C GEM μTPC Results
Pristine position resolution σ <200 μm reached with Single GEM
Detection efficiency < 5 % at normal incidence of neutron
D. Pfeiffer et al., JINST 10 (2015) 04, P04004

## Slide 8: Gd-GEM μTPC Results
Position resolution σ <300 μm reached with Triple GEM, APV-25
Detection efficiency < 12 % at normal incidence of neutron
D. Pfeiffer et al, 2016 JINST 11 P05011

## Slide 9: Better tracking algorithms needed
Used for 10B4C
VMM-like?
Used for APV-25

## Slide 10: Geant4 Gd simulation problems Getting worse in 10.2.p02
Photon Evaporation 10.1
Photon Evaporation 10.2
Without Photon Evaporation
gamma
gamma
gamma
ce
ce
  Problems with gamma spectra:
  https://zzz.physics.umn.edu/lowrad/_media/meeting8/ychen_gdgammas_aarm2015.pdf

## Slide 11: Task division Geant4/Garfield++
gamma
(Standard and low energy EM physics)
“Kill” gamma when entering gas region in Geant4
TransportPhoton()
Garfield++ simulation according to needs
Charged particle
PAI/PAIPhot Model
In gas region
“Kill” secondary e- produced in gas region in Geant4
TransportDeltaElectron()
Charged particle
(Standard and low energy EM physics)
“Kill” primary when entering gas region in Geant4
SetParticle()
NewTrack()
Primary particle entering gas
Physics model in Geant4
Point of transfer of
Control between
Geant4/Garfield++
TrackHeed Method
in Heed/Garfield++
1b
2
1a
Geant4
Garfield++

## Slide 12: Degrad Simulations
DEGRAD simulation of 70 keV electron in Ar/CO2 70/30
DEGRAD by Steve Biagi: http://magboltz.web.cern.ch/magboltz/
3D
xz
yz
Only Monte Carlo program that incorporates all relevant physics processes for electrons in gas
Simulations with Geant4/Garfield interface have to be benchmarked against Degrad
Check of primary ionization distribution in Geant4/Garfield++

## Slide 13: Detection efficiency gammas based on threshold
Threshold where 10% of ce are lost
Threshold where 25% of ce are lost
Brightness Report on Natural and enriched Gadolinium converters design
Simulations of converter and gamma sensitivity will be published soon

## Slide 14: Arrival position neutron on converter

## Slide 15: Arrival time neutron on converter

## Slide 16: Arrival position ce in drift

## Slide 17: Arrival position Compton e- in drift

## Slide 18: Arrival position gamma in drift

## Slide 19: Number of conduction electrons in drift

## Slide 20: Number of CE electrons in drift

## Slide 21: Limits of reconstructed position of CE (relative to arrival position in drift)
Compare to DEGRAD!

## Slide 22: Tasks discussed at CERN meeting (July 2016) and per email
Implemented (Michael, Patrik, Doro)
  Fast conversion of DATE APV-25 rawdata to root file
  Study of VMM-2 data format (now understood)
  Fast conversion of DATE VMM-2 rawdata to root file
  Extensive measurements with APV-25 to compare with simulations and decide detector geometry (converter, drift, readout)
  First measurements with VMM-2 with gamma sources
  First measurements with VMM-2 with neutrons
  Extensive detector simulations
Implemented (Martin)
      Software to convert root file
      Software to display events and generate metric

## Slide 23: Tasks discussed at CERN meeting (July 2016)
Implemented
  NMX Data storage (Carsten, DMSC)
In progress
  Search for better metric for position resolution using real data (Martin, Carsten, Doro)
  Integrating Geant4/Garfield interface into ESS simulation framework (Carsten)
  Understanding of implications of VMM-2 data format for achievable rates etc (Morten)
  Modification of VMM-2 slow control to facilitate the work with several chips (Michael)
Open or unknown:
  Use of GPU to do tracking (Troels)
  Use of DSP board for tracking (Hans, Doro)

## Slide 24: TO DO
  Complete analysis of the 2016 measurements
  2016 measurements needed to finalize detector design

## Slide 25: SRS Data Format for VMM-2

## Slide 26
00000000
Frame counter
564d32
Data marker
0e
VMM-ID
0000
Trigger counter
0000
Trigger timestamp
801ec506
Data 1
fc000000
Data 2
Repeated n times (for each strip hit)
fafafafa
End marker
Incremented with each trigger
One VMM

## Slide 27
00000000
Frame counter
564d32
Data marker
0e
VMM-ID
0000
Trigger counter
0000
Trigger timestamp
c038d60a
Data 1
fc000000
Data 2
Repeated n times (for each strip hit)
fafafafa
End marker
00000001
Frame counter
564d32
Data marker
0f
VMM-ID
0000
Trigger counter
0000
Trigger timestamp
c0345e07
Data 1
fc000000
Data 2
Incremented with each trigger
Incremented with each trigger
Two VMMs
First VMM
Second VMM
Repeated n times (for each strip hit)

## Slide 28
801ec506
Data 1
1000 0000 0001 1110 1100 0101 0000 0110
4 Bytes
32 Bits
0110 0000 1010 0011 0111 1000 0000 0001
32 Bits reversed
ADC (10 Bits)
Bit 0
Bit 31
Bit 0
Bit 31
0110 0000
Bit 0 - 7
11
Bit 14 - 15
0x360 = 864
10 1000
Bit 8 - 13
00
Bit 22 - 23
0x28= 40
01 1110
Bit 16 - 21
0000 01
Bit 26 - 31
0x5e = 94
TDC (8 Bits)
BCID (12 Bits)

## Slide 29
fc000000
Data 2
1111 1100 0000 0000 0000 0000 0000 0000
4 Bytes
32 Bits
0000 0000 0000 0000 0000 0000 0011 1111
32 Bits reversed
Flag (1 Bits)
Bit 0
Bit 31
Bit 0
Bit 31
1
Bit 31
1
Bit 30
00 0000 0000 0000 0000 0000 0000 1111
Bit 0 - 29
0xF = 15
Over threshold flag (1 Bits)
Channel No (12 Bits)