## Slide 1: Neutron Beam Extraction System Design status for IAC
Jarich Koning
www.europeanspallationsource.se
4th Oct 2016

## Slide 2: NBEX overview
NBEX breakdown
Neutron Beam Port Insert
Neutron Beam Window
Light Shutter System
RH Tooling
In this presentation
Light Shutter System
NBEX alignment
Optic envelope
NBW
RH Tooling

## Slide 3: Light Shutter System
Gamma-Beam-Shutter (GBS) on top of Bridge-Beam-Guide (BBG).
  Not configurable, but some customization is ok
Each ‘Shutter’ has ballscrew-style actuator
  Brake is ‘normally open’  no power means GBS closes by gravity descent
  Actuator pushes BBG up to mount against NBW
During maintenance, GBS will stay in front of beam port on dedicated hooks
Floor-to-vessel shielded as much as possible
All handling from basement, except:
  NBPI exchange from bunker
  Rescue scenarios from Bunker
BBG
NBPI
Floor filler block
Rigid chain actuator
Bunker roof support
Floor fill shielding
Handling tooling
NBW
GBS
Shutter actuator
GBS hooks
Target level floor
Block locking system

## Slide 4: Alignment strategy
Port blocks measured at installation (expected <±2mm)  TNBA
Machine internal mounting pads to correct to within <±0.05mm
Replicate port block situation on test-bench
  Align NBPI + BBG (=shutter) internal guides there (±50µm / <200µrad guide-to-guide)
BBG provides fiducials to help bunker-mounted equipment
NBPI-to-BBG kinematic mount delivers good repeatability
  Blind-folded mounting of NBPI and BBG should each deliver some ±150µm / <<200µrad absolute
  Before operation many chances to correct: check NBPI without NBW in place, check NBPI+BBG with optically open NBW
Notes:   TNBA, Theoretical Neutron Beam Axis

## Slide 5: Alignment – one time
Port blocks (±2mm overall)
NBPI
NBW
BBG
Bunker beam line
Target building
Bunker floor
(±25mm on edge)
Monolith concrete
Experiment Hall
floor
Target building base slab
Pillar/walls
Mounts
Mounts
Mounts
Mounts
Baseplate (±0.1mm flat and level)
Z
X
Custom machined mount blocks comprising full kinematic mount allow NBPI at < ±100μm, thus effectively the beamguides are at < ±150 μm vs TNBA
Dowels + good manufacturing allow Y, Z and rX with < ±100μm on interface
Good manufacturing allows < ±200μm on interface
Needs ±25mm seismic clearance
No mechanical interface, use fiducials on BBG as reference
Theoretical Neutron Beam Axis
Beam guides in NBPI aligned at test-stand to < ±50μm

## Slide 6: Repeatability
Port blocks
NBPI
NBW
BBG
Bunker beam line
Target building
Bunker floor
Monolith concrete
Experiment Hall
floor
Pillar/walls
Mounts
Mounts
Mounts
Mounts
Baseplate
Z
X
Whenever NBPI extracted  new NBPI  see prev. slide
Full kinematic mount allows < ±50μm
If Target building stable: BBG kinematic mount leads here to
< ±50 μm, too
Post-installation alignment opportunity in Basement
Experiment Hall
floor
Target building base slab

## Slide 7: Optic envelope up to R6m
NBPI horizontal cross-section
  ~130mm @ ~R1.68m, 170mm @ R2m, 200mm @ R2.35m, 270mm @ R3.75m
NBW max width could be 270mm
Light shutter space is 390mm (from R5.5m to R6.0m)
Max focal point opening is 2.86° constrained by NBW
Max pinhole opening is 6.00° constrained by NBPI front and NBW
  Moderator visibility depends on exact port
Max 300W nuclear heating  H2O cooling (35°±5°C, ΔTmax=3°C)
  Thermal conditioning of beam guides is up to instrument
  Conditioning need depends on selected atmosphere (HV or He@Atm)

## Slide 8: NBW: one-piece Al6061T6
Vacuum seals milled into NBW
NBW max surface:
  H 562 x W 270mm
AA12 case possibly resulting in several thickness NBW variants
Z, Y and rX dowels integrated
Other DoFs known from as-built metrology
RH features integrated
NBPI engaging force integrated
Water connectors integrated
One-piece, single use
NBW area
Dowel-in-hole and dowel-in-oblong hole constrain Y, Z and rX
Vacuum sealing edge
Vessel-side water flange

## Slide 9: BBG to NBW mount
Mount:
Sphere (3DoFs)
Cylinder (2DoFs)
Top pad touches (1DoF)
NBW provides kinematic mount to BBG
NBW connects Cooling water flow to NBPI
NBW pushes NBPI (on its integrated disc spring stacks) forward on its kinematic mount to port blocks
NBW area
Cooling
Tilting axis
Notes: Extra slides follow

## Slide 10: Beamlines in NBW & BBG
Freia (pink)
Heimdal (red&blue)
Loki (purple)
NMX (green/grey)
ESTIA (yellow)
SKADI (grey)
Pictures:
Left: Insert back flange@5.5m
Mid: NBW@5.5m
Right: BBG@R6m

## Slide 11: Window thicknesses
Monolith NBW
  Considering safety case of chopper failure creating projectile
  Different chopper and projectile cases considered
  Impacting projectile directly drives NBW thickness
  NBW height x width irrelevant for projectile impact
  Ongoing investigations are in the order of 10mm
In NBPI: when Instruments requires He atmophere: 2 x 1mm
  Preliminary investigation shows only 15C ΔT on Si benders
In light shutter to enclose air: 2 x 0.5mm
Further beamline: up to instruments

## Slide 12: NBEX Handling Strategy
Shutter blocks handling
  Remove shutter actuator
  Remove blocks one by one in basement using
    Rigid chain actuator from basement
    Block locking system in basement ceiling
  Radiating blocks
    Shall use shielded vault in basement
    Shall use shutter cask
NBPI handling
  Leave GBS in vault, in target floor
  Clear beamline and adjacent beamlines’ choppers
  Install and use NBPI exchange tool
NBW handling
  Use several tools from basement
  Move in vertical vault
Lower shielding cart
Lower shielding
Support table
Shutter cask on cart
NBPI Exchange
Floor Unit
NBW handling tool

## Slide 13: NBEX Handling Tasks
Operational
Operational ‘on-off’:
  Open beamlines
  Closed beamlines
  Bi-spectral switch = extra positions defined by ballscrew positioning
Shutdown
NBEX block removal
Operational ‘on-off’:
  Open beamlines
  Closed beamlines
  Bi-spectral switch = extra positions defined by ballscrew positioning
For all maintenance:
  Remove ballscrew actuator, install shield, tools in basement
  Use rigid-chain actuator with locking system bringing blocks down
  BBG block can be brought to ACF for scrapping
  Normally GBS remains on locking hooks – with a mechanical override this can be removed as well
NBEX maintenance carts
Operational ‘on-off’:
  Open beamlines
  Closed beamlines
  Bi-spectral switch = extra positions defined by ballscrew positioning
For all maintenance:
  Remove ballscrew actuator, install shield, tools in basement
  Use rigid-chain actuator with locking system bringing blocks down
  BBG block can be brought to ACF for scrapping
  Normally GBS remains on locking hooks – with a mechanical override this can be removed as well
Then:
NBPI maintenance (replacement)
  Use NBPI exchange tool (next slide)
NBW maintenance (replacement)
  Use several tools from vertical vault (2 slides further)
Sealing surface refurbishment
  Use tool from vertical vault (after NBW removal)

## Slide 14: Insert exchange
NBPI extraction tool
Handling carriage forward
Hoist floor unit in
Hoist tool in
Lower door
Push tool FW
Bring carriage FW
Pick up NBPI
(and bring to ACF)

## Slide 15: Handling the NBW
Uses rigid chain actuator from Basement
Unbolts/collects/moves NBW into shutter cask
Polishes/refurbishes vacuum sealing surface
Helium leak testing carriage
Bolting
Handling
Polishing / Inspection
He leak testing

## Slide 16: Further development
No cooling/conditioning for the BBG
  Humid air to Nitric Acid (under intense gamma)requires confinement of air in beam guides
No trespassing from bunker into shutter space nor contact
  Instrument that pushes forward like ESTIA: work out safety implications, check with PSS.
Upcoming tailoring:
  Bi-spectral switch in BBG
  ESTIA ‘retractable’ beamline
  NBW variants

## Slide 17: Neutron Beam Extraction System
Model reference: ESS-0065135
Notes: Extra slides follow

## Slide 18: Thermal results
ESS-0058384, rev 2
Cooling not optimized
Si-wafers-to-BGs in vacuum assumed
BGs passively cooled
BGs with spring-and-screws, ΔTmax=15°C
Wafers in guides with radiative heat transfer, ΔTmax=10°C
Cooled NBPI deformation, smax=49μm (cooling is not optimized)

## Slide 19: ESTIA retractable beamline
Uses two vacuum ‘actuators’. Unlocked by BBG+GBS moving downwards
BBG+GBS motion then pushes back the grey vessel
Passive motion

## Slide 20: BBG tilting engagement
Tilting axis
Actuator force
Notes: Extra slides follow

## Slide 21: NBEX  interface  Instrument
Highlighted: Common NBEX fixed features
Vertical relocation of wheels only after discussion with NBEX
Sizing of wheels yet to be confirmed
Rest of volume is up to Instrument
BBG Side view
TCS
TCS

## Slide 22: NBEX  interface  Instrument
Highlighted: Common NBEX fixed features
Rest of volume is up to Instrument
NBPI back
view