## Slide 1: Tunnel – ISRC1 & LEBT2 (with focus on installation)
Øystein Midttun
WP33 – ion source guy (in-kind)
1ISRC = ion source
2LEBT = low energy beam transport
3WP3 = normal conducting front end = first 50 m of the accelerator
www.europeanspallationsource.se
24 November, 2016

## Slide 2: For an accelerator physicist an ion source is something far far away, …
CERN is an extreme case

## Slide 3: For an accelerator physicist an ion source is something far far away, …
ESS is a little easier

## Slide 4: ... sometimes referred to as a black box, ...
Ions

## Slide 5: ... and should ideally have three buttons.
Ions
On/off
Particle
type
Intensity

## Slide 6: (in the ESS case: two buttons)
Protons
On/off
Intensity

## Slide 7: An ion source generally consists of a plasma generator and an extraction system
Plasma
(ion + electrons)
Material input
Power to heat
the plasma
E
Ions
Plasma chamber
Hole to let ions out
Extraction electrode

## Slide 8: The ESS proton source uses microwaves to heat the hydrogen plasma
Waveguide
Solenoid magnets
Plasma chamber
Gas injection
High voltage insulator
Extraction eletrodes
Pumping ports
50 cm

## Slide 9: The magnetron injects the microwaves, and the high voltage platform provides the electric extraction field
High voltage isolators
Magnetron
Plasma chamber
Power -> microwave oven
High voltage -> Tesla coil

## Slide 10: The low energy beam transport (LEBT) matches the beam to the RFQ input
Proton source
– creates the beam
Iris
– controls the current
Chopper and collimator
– controls the pulse length
Solenoid
– focuses the beam

## Slide 11: With computer models, we can simulate and “look at” the beam in the LEBT
H+
H2+

## Slide 12: The ion source and LEBT are the first elements of the accelerator
Proton source
LEBT

## Slide 13: Logically they are installed (and commissioned) first
Installation
Commissioning
3 weeks
for installation, and
9 weeks
for commissioning
is (very) short

## Slide 14: Installing the ion source is a collection of small tasks (not exhaustive list)
Cooling water
Fiber optics
HV power
Controls power
HV platform
HV cage
Ground connections
LEBT
Proton source
Control system
H2 gas delivery
Diagnostics

## Slide 15: The final installation will be something similar to the Linac4 installation at CERN
Ion source
LEBT
H- ion source and LEBT at Linac4, CERN

## Slide 16: I hope that you will not consider the ion source as a black box (it can also be white or grey …)
I hope that you will not consider the ion source as a black box
Proton source for ESS – Catania, Italy