## Slide 1: Target ‘Ready for Beam’ Signal Definition
Linda R. Coney, Jens Harborn, Kristoffer Sjögreen
European Spallation Source (ESS)
www.europeanspallationsource.se

## Slide 2: Outline
Defining ‘Ready for Beam’
State Machines
System classification & loads
Ready for Beam

## Slide 3: RBOT vs Ready for Beam
RBOT – planning milestone
  All Target systems are designed, manufactured, delivered, installed and tested without beam
  System function has been verified to meet requirements set out during design for operations & interfaces
  Not necessarily when beam actually arrives on target
BOT – later milestone when beam arrives
  Licensing permission to take beam from SSM approved
  Practice with remote handling of monolith systems done
  Instruments ready
  Requires target systems signal ‘Ready for beam’

## Slide 4: Defining Ready for Beam parameters
Quick answer
  Everything is running as designed to meet system performance and interface requirements as verified during previous testing
Of course… it is more complex..
  Systems defined as ok – what folds into that definition?
    Does it depend on the beam conditions – power, (un)rastered, rep rate?
    Does it depend on the state of other systems?
    Does it change during commissioning?
  How are the safety systems related to beam-to-Target?
    PSS, TSS, WES (Worker Evacuation System), ACF-mode control
    Fire, ODH

## Slide 5: Different answers depending on the system during ESS startup
System | Depend on beam parameters? | On other systems? | Change with commissioning? | Is it a required safety system?
Primary water systems | No | Yes (connected cooling systems) | No | No
HVAC | No | Unlikely | No | No
He cooling system | Probably (flow) | Yes (1046) | Possibly | No (not the cooling function)
Wheel | Yes (limited p+ beam power is allowed on not rotating wheel.. otherwise NO) | Yes | Possibly | No
LH2 system | Maybe? | Maybe? | Maybe? | No
MP (Target) | Yes | Yes | Possibly | No

## Slide 6: Different answers depending on the system during ESS startup – I&C systems
System | Depend on beam parameters? | On other systems? | Change with commissioning? | Is it a required safety system?
TSS | No | No | No | Yes
PSS | Yes (ON/OFF) | Maybe | Maybe | Yes
WES | No | No | No | Yes
MP (Target) | Yes | Yes | Possibly | No
ACF mode control | No | No | No | Decoupled/No

## Slide 7: Defining Ready for Beam parameters
Need a systematic method for identifying when each system is ok for beam
Define state machines for each system from overall ESS down to subsystems
  All state machines have 6 basic modes in common
  Running, Starting, Stopping, Standby, Fault, Off
  Each of the five main ESS system groups is represented by its own state machine
Depending on system functionality, sub modes are added to one of the basic modes
  Ex. Target wheel has sub-mode ‘Parked’ under ‘OFF’

## Slide 8: State Machines
  Five main ESS system groups defined
  ESS
  Accelerator
  Target Station
  Neutron Scattering Instruments
  PSS
Each is represented by its own state machine
Top level state machine has the five basic modes with additional sub-modes within RUNNING and OFF

## Slide 9: State Machines – Signal Exchange
State machines for the main system groups exchange signals
Start requests propagate within the main systems and down to lower levels – Chain principle
Conceptual example based on early Startup discussions

## Slide 10: State Machines – Chain Principle
Start request propagates from Target Station down to lowest sub-systems
Confirm operational propagates back up to Target Station
Only systems with direct dependencies perform synchronized information exchange

## Slide 11: Define Modes for Each System
What is ‘Running’ for the different systems?
What are ‘Fault’ conditions for the different systems?
What are limits for process values?
  MP limits, TSS limits where applicable
Identify role in radiation safety case as defined by the accident analyses
  g Determines classification of system and quality class
Identify operational and accidental loads
  gDetermine load cases for which the systems must be qualified
  Example for mechanical system – wheel

## Slide 12: Classification of systems
ESS rule for identification & classification of safety important components (ESS-0016468)
  g safety or safety-related (Category 1-5)
ESS rule for quality regulation – mechanical equipment (ESS-0047989)
  g Quality class & corresponding RCC-MRx code class
Wheel – Category 4 (MQC4) g but we apply RCC MRx Section III Subsection C because it is exposed to radiation (formal EN-13445 according to PED)
RCC MRx defines 4 Operating Conditions with criteria levels
  Component replaced if reach Level D stress, exposed to Level C < 10 times
Operating Conditions | Occurrence | Criteria Level
SF1 | Normal operation | Level A criteria
SF2 | Normal operating incidents | Level A criteria
SF3 | Emergency conditions | Level A or Level C criteria
SF4 | Highly improbable | Level A, C or D criteria

## Slide 13: Design basis (KFM) – System 1000 (wheel, shaft, drive)
System description, classification, level of exposure to radiation
Load cases – Derived from legislation, similar operational experience, accident analysis reports
  Includes connections/interfaces with Safety SSCs
Normal operations loads
  Design conditions (ex. Pressure, temperature, mass)
  Operating conditions (ex. steady beam, beam trips,
Transient loads
  Operating conditions (ex. beam trips with helium cooling operational, unsynchronized rotation)
  Accidents – Stopped wheel (AA1), non-rastered & focused beam (AA2), loss of cooling (AA3, AA4, AA7, AA8), local blockage (AA5), EQ (AA14)
Identify loads applied to each part of the system and bin into RCC-MRx categories: SF1 – SF4

## Slide 14: Summary of loads – System 1000
Identify loads mitigated by MP or TSS
  Determines which criteria can be used to define limits
  MP – level A
  TSS – level A, C or D
SF2 – normal operating incidents
SF1 loads are normal operating conditions
Wheel
Shaft
Drive

## Slide 15: Summary of loads – System 1000
SF3 – emergency operating conditions
SF4 – highly improbable operating conditions

## Slide 16: Required for ‘Ready for Beam’ – Safety Systems
PSS – in mode ‘Running’
  All enclosures searched and secured
TSS – in mode ‘Running’ and sub-mode ‘Beam to Target’
  Helium temperature below TSS trip level
  Helium flow above TSS trip level
  Helium pressure above TSS trip level
  Wheel rotation above TSS trip level
  Monolith pressure below TSS trip level
WES (Worker Evacuation System) – in mode ‘Running’ & ok
Fire detection/alarm system

## Slide 17: Required for ‘Ready for Beam’ – Systems
Machine protection – in mode ‘Running’ and ok
  All parameters monitored by MP are within the MP trip levels
Target station systems in mode ‘Running’ and within normal operating parameters as defined by the load cases
  Wheel drive – synchronized rotation
  Helium cooling system
  Primary water systems, intermediate water systems
  Cold moderator cryo system
  Monolith vessel atmosphere system, shutters
  Target building HVAC
  Target monitoring plug systems

## Slide 18: Conclusions
Development of the process is underway
Need to further define operating parameters and limits for all of the systems in order to arrive at quantitative parameter values
Further investigation of the relationship between target station systems and beam configurations (current, power, rep rate, etc) needed

## Slide 19: Conceptual Sample Start Sequence
User activates Start Request
  Propagates to Target Station (TS) and is read by many systems within TS
    ex. TSS, target wheel, MR-system
  Propagates to Accelerator (ACC) with all sub-systems and to Target Machine Protection
TS response:
  The target wheel enters READY FOR BEAM when the cooling is RUNNING and synchrinized run.
  TSS reads a set of target station process values, ex. Helium cooling flow and target wheel rotation and enters mode BEAM TO TARGET and indicates ‘ready for beam’. TSS continuously reads the process values while in mode BEAM TO TARGET.
Acc reads:
  ‘Ready for beam’ from TSS and
  ‘Ok’ from all PSS signals, and
  Maximum allowed proton power from NSS and
  Enters start sequence for beam to target.
ACC main State Machine indicates different modes
  ex. ION SOURCE ON to STARTUP RAMPING and finally to PRODUCTION
ESS main state machine
  Reads modes from TS, ACC, and NSS and indicates current overall mode