## Slide 1: Neutron Beam Extraction System Design status for TAC-15
Jarich Koning
Sara Ghatnekar, Naja de la Cour, Bengt Jönsson
www.europeanspallationsource.se
6th April 2017

## Slide 2: NBEX overview
Breakdown
Neutron Beam Port Insert
Neutron Beam Window
Light Shutter System
Handling & Installation Tooling
Test stands

## Slide 3: Light Shutter System
Gamma-Beam-Shutter (GBS) on top of Bridge-Beam-Guide (BBG).
  “Light shutter” comprises GBS+BBG
  BBG internals are up to instrument
Each ‘Shutter’ has ballscrew-style actuator
  Brake is ‘normally open’  no power means GBS closes by gravity descent
  Actuator pushes BBG up to mount against NBW
During maintenance, GBS will stay in front of beam port on dedicated hooks
Bunker-floor-to-Vessel gap shielded as much as possible
All handling from basement, except:
  NBPI exchange: from Bunker
  Rescue scenarios: from Bunker
BBG
NBPI
Floor filler block
Rigid chain actuator
Bunker roof support
Floor fill shielding
Handling tooling
NBW
GBS
Shutter actuator
GBS hooks
Bunker floor

## Slide 4: Optic envelope up to R6m
Horizontal cross-section
  NBPI: ~130mm @ ~R1.68m, 170mm @ R2m, 200mm @ R2.35m, 270mm @ R3.75m
  NBW max width could be 270mm
  Light shutter width available is 390mm max (from R5.5m to R6.0m)
Max opening: from focal point 2.86°, a pinhole in NBPI yields 6.00°

## Slide 5: Beamlines in BBG and NBW
FREIA (pink)
HEIMDAL (red&blue)
LOKI (purple)
NMX (green)
ESTIA (yellow)
SKADI (light brown)
MAGIC (cyan)
BIFROST (dark green)
T-REX (light pink)
TEST (brown)
ODIN (white)
DREAM (dark cyan)
BEER (orange)
C-SPEC (dark red)
VESPA (black)
This status is 12-2016, much has changed!
Beamline geometries up to R6m are frozen per 31-03-2017
Instrument models (G. László)
NBEX baseline geometries (J.F. Koning)
Instrument NBOA (I. Sutton)

## Slide 6: Installation
Experiment Hall
floor
Monolith concrete
Filling
Port blocks
Ports for NBPI: ±1mm, budgeted at ±0.5mm for shape, and ±0.5mm for alignment
Target building
Bunker floor
NBW
NBW w.r.t. port
±0.3mm (bolts)
Pillar/walls
Bunker beam line
Mounts
Mounts
Mounts
Mounts
BBG
FFB
GBS
Light shutter structure ±0.5mm
Light shutter blocks on rails and vertical ballscrew with servo repeat to ±0.05mm
Supports Bi-spectral switch in BBG
Feedback to correct absolute position needs to come from instrument
Z
X
BPCS
TNBA = Theoretical Neutron Beam Axis
Target building base slab
Baseplate
Flat and level on topside within ± 0.2 after alignment. Grouting fill keeps shape under loading.
TCS Z value derived from central ‘vessel support (not shown)
Values w.r.t. TCS (absolute) if not otherwise noted
NBPI
NBOA
NBPI shape ±1mm
NBOA aligned w.r.t. NBPI mounts ±0.05mm
NBPI mounts aligned per direction with ± 0.05mm
After all ports are done, TCS X&Y are defined
Notes: TNBA=Theoretical Neutron Beamline Axis
BPCS = Beam Port Coordinate System. Definition: X=downstream, Z=up. Location: 5500mm from TCS at the respective port angle looking at the respective focal point

## Slide 7: Alignment system for NBPI
Alignment
Y (side)
Z (one foot)
Alignment
Z, two feet
Alignment
Y (side)
X (end-stop)
NBPI
CoG
Guide rails
(no alignment)
All Final Alignment units (blue) to be adjusted and assembled after Port Block installed in Monolith.
Y
X
BPCS
Y
X
BPCS
Z
Full kinematic mount

## Slide 8: NBW: one-piece Al6061T6
NBW area
Vacuum sealing edge
Max NBW area
Helium leak-testing line
Cooling connections
Vacuum seals milled into NBW
One piece of Al6061T6
NBW Surface (link):
  Max: H 562 x W 270mm
  Variant 1: H 380 x W 240mm Vertically TCS -183mm to +197mm
RH features integrated
NBPI engaging force integrated
Water connectors integrated
Helium leak-testing integrated
Test for multiple use
Proto to be delivered 10-04-2017

## Slide 9: Window thicknesses
Monolith NBW
  Hazard of projectile impacting NBW, then MR, drives thickness (ESS-0064402), based on projectile definition (ESS-0061754)
  NBW Height x Width irrelevant for projectile impact: 4.0mm Al necessary
  Common 380x240 area captures known instruments
  For 1bar Δp 4.0mm thickness (ESS-0064402) needed, results 1.8mm deflection max.
In BBG (light shutter) to enclose air:
  2 x ‘foil’, e.g. 0.5mm
  Up to instruments
NBPI windows
  Unknown yet, as thin as possible for area of specific instrument
  Common sealing edge to NBPI if possible
  Can further constrain optical envelopes

## Slide 10: NBPI Windows
From Target perspective the NBPI does not need windows
Not needed for ‘looking holes’ (TEST, MAGIC)
Off normal monolith atmosphere: still risk on nitric acid → NBPI windows
Windows have to survive pressure vessel testing 175kPa and/or 1bar Δp
Integrate Helium loop -> under review
NBPI window (upstream)
NBPI body
NBPI lid
NBOAs
Monolith
NBW
NBPI window (downstream)

## Slide 11: NBEX Handling Strategy
Light Shutter blocks handling
  Remove shutter actuator
  Remove blocks one by one in basement using
    Rigid chain actuator from basement
    Block locking system in lower shielding assembly
  Radiating blocks
    Shall use lower shielding vault in basement
    Shall use shutter cask
NBPI handling
  Clear light shutter blocks and NBW
  Clear beamline (possibly adjacent beamlines’ equip.)
  Install and use NBPI exchange tool
NBW handling
  Use several tools from basement like the shutter blocks
  Move in vertical vault only, except for rescue: bunker access needed
Lower shielding cart
Lower shielding
Support table
Shutter cask on cart
NBPI Exchange
Floor Unit
One of the NBW handling tools

## Slide 12: NBEX Handling Tasks
NBEX maintenance carts
Operational ‘on-off’:
  Open beamlines
  Closed beamlines
  Bi-spectral switch = extra positions defined by ballscrew positioning
For all maintenance:
  Remove ballscrew actuator, install shield, tools in basement
  Use rigid-chain actuator with locking system bringing blocks down
  BBG block can be brought to ACF for scrapping
  Normally GBS remains on locking hooks – with a mechanical override this can be removed as well
Then:
NBPI maintenance (replacement)
  Use NBPI exchange tool (next slide)
NBW maintenance (replacement)
  Use several tools from vertical vault (2 slides further)
Sealing surface refurbishment
  Use tool from vertical vault (after NBW removal)
Operational
Operational ‘on-off’:
  Open beamlines
  Closed beamlines
  Bi-spectral switch = extra positions defined by ballscrew positioning
NBEX block removal
Operational ‘on-off’:
  Open beamlines
  Closed beamlines
  Bi-spectral switch = extra positions defined by ballscrew positioning
For all maintenance:
  Remove ballscrew actuator, install shield, tools in basement
  Use rigid-chain actuator with locking system bringing blocks down
  BBG block can be brought to ACF for scrapping
  Normally GBS remains on locking hooks – with a mechanical override this can be removed as well
Shutdown

## Slide 13: Insert exchange
NBPI extraction tool
Handling carriage forward
Extra shielding installed
Hoist floor unit in
Hoist tool in
Lower door
Push tool FW
Bring carriage FW
Pick up NBPI
(and bring to ACF)

## Slide 14: Handling the NBW
Uses rigid chain actuator from Basement
Unbolts/collects/moves NBW into shutter cask
Polishes/refurbishes vacuum sealing surface
Bolting
Handling
Polishing / Inspection

## Slide 15: NBEX schedule
  30-04-2017: NBEX-NSS interface closed
  30-04-2017: NBW vacuum test completed
  15-05-2017: NBEX internal requirements
  31-05-2017: Other NBEX interfaces closed
NBEX CDR coupled to Bunker CDR (Sept 2017)
  01-01-2018: NBW handling test stand
  01-12-2018: in-monolith optics on site
  01-03-2018: NBEX horizontal test stand, location in target building?
  01-10-2018: NBEX vertical test stand, location needs high floor load, 7m high, target building?
21-01-2019: Start of assembly of bunker R6 structure
  R6 pillar flanges w.r.t. port blocks - ports in port blocks have to be ready & aligned
01-03-2019: 1st instrumented NBPIs ready for installation
  Start of LSS installation, too
  09-2019: SATs on NBEX installated systems: NBPIs, LSS (water, shutter motion etc)
  10-2019: Handover bunker area to NSS
  15-11-2019: Bunker installation starts, NBEX finished

## Slide 16: NBEX schedule
Open issues for NBEX CDR
  No radiation fields information yet
  Interfaces not finalized
  Manufacturing method of large components not yet adjusted to supplier possibilities
  Delivery lead time
Suggesting CDR scope to be tailored
  RH Casks are deferred so defer nuclear aspects of NBEX shielded tools
  Outsource all NBEX tools as functional spec instead of manufacturing drawings
  Get NBW, horizontal and vertical test stands timely to enable tool SATs
Notes:     Blocking detailing handling scenarios and tooling design
    BBG activation is potential risk to Bunker
    Important for on-time delivery and cost
    Manufacturers need to be able to advise without disqualifying themselves from quotation
    Develop NBPI extraction tool as installation tool only, rebuild 1 tool as cask after installation
    Develop lower shielding as installation tool
    Defer shutter cask but develop design with lower shielding assembly
    Exclude test stands from this CDR scope, align with outsourced tools Oct 2018

## Slide 17: Neutron Beam Extraction System
Model reference: ESS-0065135
Notes: Extra slides follow