## Slide 1: Responses to TAC-14 Recommendations
Rikard Linander
www.europeanspallationsource.se
April 5, 2017

## Slide 2: Target ready for beam
Recommendation:
Decide which instrumentation will be used to confirm that the target is ‘ready for beam’ (What is meant by target failure?).
Response:
See talk by L. Coney.

## Slide 3: TSS safety functions
Recommendation:
Define which parameters are in TSS and which are in MPS (current logic is good).
Response:
TSS functions are defined as required by the Accident Analyses when there is a need for a monitoring/interlock Safety SSC to prevent or mitigate an event
  As identified in AA1, AA2 and AA3, the TSS will monitor: He inlet temp, He outlet flow, He pressure, Monolith pressure, and slowing of the target wheel rotation
  TSS actuation prevents the beam from reaching the target
  These functions are assigned to L3 in the DiD analysis
MP functions which are necessary to protect the equipment and facility availability are identified according to HAZOP analyses for the target station systems.
  MP will monitor significantly more parameters than TSS and is not necessarily restricted to beam shutdown.
  In the context of the DiD analysis for radiation safety, some L2 monitoring/interlock functions have been identified which prevent or mitigate the accidents earlier in the event development. These are safety-related, and it has been determined that MP can fulfill these functions. These functions are listed in each AA.

## Slide 4: Operation instructions
Recommendation:
Define what action would be taken if a critical parameter moves ‘out of range’ (eliminate the need for personnel judgement as far as possible).
Response:
Operation instruction TBD

## Slide 5: Off-normal events for the target wheel
Recommendation:
Continue the simulation calculations and analyses to establish the effects of off-normal events and their consequences for safe operation of the target. This work is to mitigate the inability to measure target temperatures directly.
Response:
A number of off-normal events are analyzed. Stop rotation of the target wheel, proton beam outside normal operation, loss of cooling, target vessel rupture, partial loss of cooling and water leakage from intermediate cooling system into the helium cooling system.
The TSS will measure inlet and outlet temp. , outlet flow and wheel rotation and trip the AC if some of these measurements are outside normal operation.

## Slide 6: Gamma imaging system
Recommendation:
Continue the work on the gamma camera, laser distance and vibration measurements, and temperature measurements from outside the wheel.
Response:
TIK 4.1 ready se above.
Tests on going to use gamma from tungsten bricks to verify structural integrity of the spallation material geometry.

## Slide 7: Accelerator – Target interface
Recommendation:
Continue to mature the decision, seek concurrence of the Accelerator Division & the project, and present details at TAC15, including a differentially pumped monolith design and the backup PBW design.
Response:
See presentation by L. Emås.

## Slide 8: Monolith vessel drain
Recommendation:
A sloping catch basin for water removal is lacking but would insure maximum liquid removal from the monolith in an off-normal scenario.
Response:
This is under discussion with ESS-Bilbao. It is in the design, but the location of the slope is not finally set.

## Slide 9: Monolith atmosphere
Recommendation:
A full helium system should remain in the baseline.
Response:
This is the case. See presentation by L. Emås.

## Slide 10: NBPI cooling
Recommendation:
Monolith inserts should be designed to be cooled independent of the monolith environment to preserve or consider a vacuum option.
Response:
The inserts are designed to be individually cooled. Sufficient cooling of optics equipment can, if requested and required, rely on thermal conduction through remaining gas pressure at rough vacuum levels (10 Pa - 100 Pa).

## Slide 11: Tungsten samples testing
Recommendation:
Repeat the second stage of the selection process with new samples with refined specifications (especially for the temperature window and the thickness reduction during hot rolling) if this has not already been done.
Response: (See also R. Linander talk)
The evaluation of tungsten samples was presented to the CDR team. No additional requirements was identified during this review.

## Slide 12: Tungsten release factors
Recommendation:
Experiments on W release factors should be carried out as soon as possible.
Response:
Two tungsten bricks has been irradiated at ISOLDE (CERN). The irradiated tungsten has been transported to DTU (Denmark) and the analysis of the block has started in December 2016. It is expected that the work will be concluded by the end of April 2017.

## Slide 13: ETHEL
Recommendation:
Perform an extended ETHEL test and consider oxidation.
Response:
With ETHEL(1) we confirmed that Tungsten does not erode in the helium flow. Tungsten can however be oxidized at high temperatures with oxygen access, which has been studied in detail by LTH Materials Engineering. That is however not a topic for ETHEL, as it does not require the flow.
The setup has now been modified ETHEL(2), to confirm pressure losses and cooling in the block configuration. The laser measurements were troublesome, but LTH Energy Sciences have some data now.
However, new experiments (TOAST = Tungsten Oxidation AeroSol Transport) are planned at LTH Energy Sciences to confirm that aerosol releases, obtained from experiments and analyses of accidents in other facilities, are also specifically applicable to accidents postulated in ESS.

## Slide 14: CMS sapphire window/blind flange
Recommendation:
Plan to exchange the sapphire window with a blind flange in case of failure to be able to continue operation of the loop.
Response: (See also Y. Beßler talk)
Blind flanges already are an option in the original design. We foresee that the Sapphire viewports will be delivered:
  a) From a vendor, certified for our use, mounted in a CF flange of our choice, or
  b) Developed by our in-kind partner/ESS and verified for our use, mounted in a CF flange.
In any case a blind flange will/can be mounted for a safe operation. We also have considered the consequences in case of glass rupture so that the hydrogen will be evacuated in a safe way. Detailed description in the CMS Solution document ESS-0092146.
A replacement of the flange will always lead to a system shutdown.

## Slide 15: Risk of increased particle deposition in helium cooling loop
Recommendation:
The system should be flexible enough to run with higher particle deposition than planned (e.g., space for additional shielding, consider where the filters are placed, etc.). Be careful of the risk.
Response:
Filter design and filter shielding ongoing. Change of filters during maintenance is under evaluation.
Radiation detection instruments on pipes and filters.

## Slide 16: Installation management
Recommendation:
Identify Installation Managers as soon as possible and start them working together as soon as possible.
Response:
A Deputy Installation Coordinator is being recruited and plans are in place to hire additional installation support staff as needed.

## Slide 17: Temporary services for installation
Recommendation:
Utilize temporary services, target in-kind partners, and/or contracted industry for as much installation work as possible. System engineers and future operations staff should be involved as much as possible.
Response:
The current situation is in short the following. For installation works during 2017 the current plan is to use temporary services provided by Skanska as far as possible. Installation for some work elements is already included in the scope that in-kind partners have taken on, such as the Active Cells, and we are pursuing the same strategy for other elements. The plan is still to build up a central Target installation team, consisting of 6-8 people, for overall coordination and execution of the installation. With regards to involvement of future operations staff the plan is to start recruitment of these teams by early 2019, which will give them the opportunity to get involved in the second half of the installation phase, and more importantly in the systems commissioning.