## Slide 1: Optics review of C-SPEC
Damian Martin Rodriguez
Neutron Optics and Shielding Group
www.europeanspallationsource.se
3 March, 2017

## Slide 2: Overview of the review
Main concerns from the optics design are:
No comparison with alternative design as in ESS-0059811 (NOSG checklist). CSPEC team requested an alternative guide design (results available in ESS-0094282)
Analysis of the substrate lifetime does not take into account full beam exposure of the substrate on misalignments (see ESS-0097645)

## Slide 3: Assessment of alternative guide design
Constraints and criteria to take into account:
Moderator geometry, building (piling corridor) and beam requirements impose certain constraints, which discourages the vertical bending for long cold instruments.
High speed choppers also put constraints in the beam size to be transported.
The low dimensionality of moderators gives an unprecedented opportunity of using elliptic geometry without its disadvantages.
We are using as many straight parts as possible in order to reduce risks during installation (breaking of guides during storage, …)

## Slide 4: Assessment of alternative guide design
Bunker wall
P chopper
(55 x 100 mm2)
100 m
M chopper
(16 x 38 mm2)
150 m
9.5 m
m= 3-5
m= 2
m= 2
m= 2
m= 2
m= 2
m= 2.5
m= 2
m= 2
m= 3-5
m= 6
m= 3-5 (small)
m= 2 (big)
See ESS-0094282 for further details

## Slide 5: Assessment of alternative guide design
The table in the ConOps is unclear and we have no updated model for simulation. Not the most accurate comparison.
The performance of the design provided by NOSG with the pancake moderator is better than the baseline performance shown in the documentation.
(simulations made with pancake moderator at 5 MW)
Limit on fig. 6 of CSPEC ConOps

## Slide 6: Assessment of alternative guide design
 | NOSG Design
Performance (signal) | ̴ 2 x CSPEC
Cost | ̴ 0.7 - 0.8 x CSPEC coating surface, lower shielding costs (low m)
Other | Low complexity, many straight and exchangeable parts
High energy background (from Target) | ?????
Is vertical bending reduce the high energy background in a higher degree than horizontal?
How much in order to outweigh the benefits of the NOSG design?

## Slide 7: Substrate lifetime calculations
The use of borofloat has the advantage of lower fabrication costs and helps the early procurement strategy the team wants to follow
However, the risk of using borofloat may have very important consequences (substitution of long sections of guide if lifetime estimations are too optimistic)
There will be a report to define lifetime requirements and failure modes before summertime (ESS-TUM)

## Slide 8: Conclusions
We present a guide design that has advantages of higher flux delivered, lower cost (direct and associated) and lower complexity. The difference on fast neutron suppression with the guide have to be quantified in order to make a decision.
The use of borofloat has construction cost savings and an important strategic advantage (fabrication of optics in-house), but it may carry a risk that has important consequences, and should be added in the risk registry of the project.