CFWG: Moderators, Beam Extraction & Shielding
General Update on Neutron Optics Group
12th February 2013 – Neutron Optics TAP #3 Meeting
Phil Bentley

---
New Thinking Required
Sub-sonic
Supersonic
Warp drive(!)
Space
Fission (<20 MeV)
EM Showers Only
(<GeV)
Hadronic Showers
(>~GeV)
Probing Standard Model
(Tev)

---
Beam spacing - preliminary conclusions
A 10 degree slot width is the minimum to avoid staggering choppers.
A 15 degree slot width is the minimum required to ensure instruments independence and install some lateral shielding
INSTRUMENT 01
<-------------- 15 degree ------------- >
INSTRUMENT 03
< 5 degree >
INSTRUMENT 02
TARGET MONOLITH
[Speaker Notes: 5 degree sector drawn Does not fit ! With 10 degree its tight 12 > 15 would permit independent positioning of equipment and some cross talk shielding]

---
The real thing @ SNS  7.5 degree separation – Staggered Chopper installation
The real thing @ SNS
7.5 degree separation
Staggered Chopper installation

---
Angular Separation
- Short instruments minimum 10, ideal 15
- Medium instrument sector (60-80 m) 10 degrees
- Long instrument sector (around 150m) 5 degrees is not yet clear, somewhere between 5 and 7.5 seems feasible.
- Expect a change request in around 6 weeks time

---
Primary Shutter Stakeholder Consultation
- All stakeholders democratically created evaluation criteria, evaluation scores, and weighting factors to choose most important factors
- Stakeholders included neutron instrument scientists, target division, neutron optics group, instrument engineering, conventional facilities.
- Options were:
  - Primary shutter inside monolith
  - Primary shutter outside monolith
  - Service shutter (current baseline)
  - No shutter

---
Primary Shutter Stakeholder Consultation
- Two evaluation matrices, one for operational aspects (top), the other for project aspects (bottom)
- Most important factor was ease of beam port activation
- Next most important items were normal operations with proton beam on, and complexity of the monolith

---
Operational Factors
Clearly, primary shutter inside monolith is the favoured option from an operational perspective
"Badness" Scores for Each Option
Operational Aspects Lower scores are better
Badness

---
Project Factors
Clearly, no shutter is the favoured option from a project perspective
"Badness" Scores for Each Option
Project Aspects Lower scores are better
Badness

---
So What's Next?
- An ad-hoc advisory panel will be convened to review the proposed changes to the monolith design

---
High Energy Background / Prompt Pulse
Now have collaboration between ESS, SNS & PSI

---
HYSPEC data summed over all detectors
HYSPEC data summed over all detectors
Elastic scattering
from Vanadium
Inelastic feature from
Vanadium
Spallation
Event every
16.7 ms
(1/60 Hz)
Background tail ends about 3.5 ms beyond spallation event

---
High Energy Background / Prompt Pulse
- Measurements are required – large survey of PSI and SNS are planned
- SNS were able to do much with heavy shutters, we are examining this option for ESS
- We still require x100 more effective shielding, shielding design and layout work to meet our objectives
- Note that this does not mean spending x100 more money or having something x100 thicker!

---
Angular Separation
- Short instruments minimum 10, ideal 15
- Medium instrument sector (60-80 m) 10 degrees
- Long instrument sector (around 150m) 5 degrees is not yet clear, somewhere between 5 and 7.5 seems feasible.
- Expect a change request in around 6 weeks time

---
New Types of Background Shielding
- Reliable models on different materials at high energy
- New concept based on multiple materials (the data below is already old, we are much better)
1 neutron in ->
10 neutrons in ->
Steel Shielding
Steel Shielding
1 neutron in ->
10 neutrons in ->
New Shielding
New Shielding

---
New Types of Background Shielding
- Reliable models on different materials at high energy
- Setting up collaboration with SNS, PSI right now (hence Phil Bentley absence)
Maximum from spallation in shielding
10,000 neutrons in
Shielding efficiency for other
Particles is the same
Neutrons passing through
old shielding concept based on Steel
New concept 100x better at
stopping high energy neutrons

---
In Summary
- Some changes will probably be required for the beam extraction compared to the baseline design
- We will probably request changes to shutter specifications and installation method, to be reviewed by the TAP and a specialist ad-hoc committee
- Timescale for changes: March/April