CFWG: Moderators, Beam Extraction & Shielding
Introduction to High Energy Background Problem
Or probably a recap...!
2. 12th February 2013 – Neutron Optics TAP #3 Meeting
  Phil Bentley

---
Root Cause of Prompt Pulse
- One hadron (proton, neutron or pion) interacts with another hadron
- At 100s MeV and above, this causes particle showers / spallation (our source!) but this happens not just in the source but everywhere that you get an interaction
- Subsequent particles of sufficient energy also create their own particle showers
10 neutrons in ->
1 m thick Steel Shielding

---
ISIS - TS2 - LET
The problem with the prompt pulse
LET Prompt pulse from TS1- 100 m away - frequency corresponds!
1 order of magnitude greater than background
(vanadium standard 7% scatterer)
4 orders of magnitude lower than Elastic line
Currently they are not too concerned about it.
See no prompt pulse from TS2

---
J-Parc:Amateras:
Spin wave excitations in a S=3/2 Heisenberg AF with Ei=4.7meV.
A Q-independent signal (prompt pulse) E=3.5meV. E over dQ=1.1-1.9AA-1.
The prompt pulse is ~ 1/100 of the elastic line.
You can easily calculate where the prompt pulse appears in an excitation spectrum.
Ei=4.7meV, the prompt pulse emitted 40msec (1/25Hz) after t=0 appears at E=3.5meV.
Shielding mainly of concrete and iron.
4Seasons sees nothing but only measures in 1st time frame AND has a T0 chopper

---
HYSPEC data summed over all detectors
Elastic scattering
from Vanadium
Inelastic feature from
Vanadium
Spallation
Event every
16.7 ms
(1/60 Hz)
Background tail ends about 3.5 ms beyond spallation event

---
HYSPEC
Former source
Of 70% background
feature
Region above end of
Proton beam is beacon
Of fast neutrons
Proton beam dump off collection ring
Was found innocent
HYSPEC