## Slide 1
DMSC-Detector Group Interface
DMSC-DG Meeting
9th May 2017
Steven Alcock (DG)

## Slide 2: Agenda
Target Architecture Overview
Basic Networking (and the role of the FPGA)
Proposed Stack Implementation
The Merits of a Switch

## Slide 3: Target Architecture
FPGA Master 1
FPGA Master 2
Switch
DMSC Server 1
DMSC Server 2
FPGA Master:
  Aggregates data from upstream detector hardware,
  Packetises data,
  Forwards to NIC in DMSC server.
Assume more than one Master, and more than one NIC.
Switch is optional!
Diagnostic Server
Notes: Powerful FPGA Master concentrates all data from upstream detector hardware, and sends to a NIC in a server, possibly via a switch.
May use a single switch for multiple instruments, and may service multiple NICs.

## Slide 4: Protocol Stack - Overview
Physical Layer (Copper/Fibre)
Link Layer (Ethernet)
Network Layer (IP)
Transport Layer (TCP/UDP)
Application Layer (Instrument Data)
Notes: TCP/IP is the standard for Internet communications, and is a de-facto standard for similar networks.
Stack provides a useful service-based abstraction model for describing networks. Some or all layers may be different depending on application.
In the case of TCP/IP, the technology is widely understood and available.

## Slide 5: Protocol Stack – Physical Layer
Responsible for moving bits from source to destination.
Expect to use commercial fibre/copper cables
FPGA achieves mechanical connectivity via standard QSFP+ cages.
Common to have “hardened” silicon to handle remaining PHY functionality (such as scrambling, coding, clock recovery and deskew).
Multi-Gigabit Transceivers deserialise signals and clock them into FPGA user-logic.
RJ45 (1000 BaseT)
QSFP+ (100 GbE)

## Slide 6: Protocol Stack – Data Link Layer
Responsible for moving frames between devices on a common LAN.
MAC sublayer typically implemented in FPGA logic, BUT this is non-trivial for high data rates (> 1 Gbps).
Standard practice to buy a “logic core”.
Latest VCU118 FPGA avoids this by including, for free, a hardened PHY/MAC core for 100 G applications.
Future-proofs design.
Chart: 
| 1 | 10 | 25 | 40 | 56 | 100
Standard Ethernet Rates (Gb/s) | 1 | 10 | 25 | 40 | 56 | 100
Notes: 100 G is cheaper (in terms of money) than eg 10 or 40 G, because the PHY/MAC functionality is included in the FPGA.

## Slide 7: Protocol Stack – Network Layer
Responsible for moving packets across a network of separate LANs – implies routing.
Full implementation not well suited to FPGAs:
  Trivial to implement basic header functionality
  More difficult to implement associated functionality such as ARP, DHCP.
All our nodes are on the same LAN – no need for the IP layer?

## Slide 8: Protocol Stack – Transport Layer
Responsible for reliably moving packets across a network of separate LANs.
TCP is not well suited to FPGAs:
  Stateful retransmission of packets requires potentially extensive buffering and control logic.
  For low rates, common practice to instantiate a hard or soft microprocessor, although commercial logic cores do exist.
Generally, UDP is used instead.
  Lightweight protocol that doesn’t gain us much?
Source Port | Destination Port | Length | Checksum

## Slide 9: Protocol Stack - Conclusion
Physical Layer (Fibre)
Application Layer (Custom Protocol)
Link Layer (100 G Ethernet)
Run our own custom protocol over raw Ethernet at 100 G.

## Slide 10: Frame Size
Frame Type | L1 Overhead | L2 Overhead | MTU | Total | Efficiency
Standard | 20 | 18 | 1500 | 1538 | 97.5%
Jumbo | 20 | 18 | 9000 | 9038 | 99.6%
Lower protocol overhead and lots of spare bandwidth:
  Jumbo frames not essential for throughput.
Standard frames (marginally) reduce buffering requirements on FPGA:
  RAMs instantiated in 4500- or 2250-byte blocks
The figures below do NOT account for Instrument Protocol overhead, as this is to be finalised. The actual efficiency, in terms of digitised samples, will be lower.
Notes: L1 Overhead: preamble (8 bytes), inter-packet gap (12 bytes)
L2 Overhead: 6-byte destination MAC address, 6-byte source MAC address, 2-byte EtherType, 4-byte CRC

## Slide 11: Optional Switch – MSN2100
Rate Conversion:
  100 G to 56/40/25/10 G
“Load Balancing”:
  Redistribute single input port across multiple output ports
Diagnostics:
  Duplicate input port on multiple output ports
Low Cost:
  About 5000 USD
Notes: Good relationship with Mellanox due to prior projects at RAL and close proximity to Daresbury.
Testing is under way.

## Slide 12: Questions
What EtherType should we use in the frame header?
Are there any compelling reasons to use IP/UDP?
Anything else?