## Slide 1: Data Acquisition and Monitoring for Detector Development
Morten Jagd Christensen
www.europeanspallationsource.se
9 May 2017

## Slide 2: Architecture

## Slide 3: System overview
Two data streams per instrument
  Detector Data / EPICS Data
Event Formation processes Detector data
Events are streamed to Aggregator (kafka) for later filewriting to persistent storage

## Slide 4: System overview

## Slide 5: Event Formation Unit (EFU)
One EFU per detector panel
Direct fiber connection (10G)
EFU is pure multi core software processing (if possible)
Switched Ethernet on the output side

## Slide 6: EFU Pipeline and Stages

## Slide 7: EFU Pipeline and Stages
input
distributor
distribute data to multiple processing cores (load balancing)
validator
detect invalid data (crc errors, etc.)

## Slide 8: EFU Pipeline and Stages
input
distributor
distribute data to multiple processing cores (load balancing)
validator
detect invalid data (crc errors, etc.)
processing
collection
pick up data until enough to process
rejection
reject data (noise, artifacts, simultaneous, ...)
clustering
determine a dataset suitable for event calculation
event calculation
generate <time, detector pixel id> tuple

## Slide 9: EFU Pipeline and Stages
input
distributor
distribute data to multiple processing cores (load balancing)
validator
detect invalid data (crc errors, etc.)
processing
collection
pick up data until enough to process
rejection
reject data (noise, artifacts, simultaneous, ...)
clustering
determine a dataset suitable for event calculation
event calculation
generate <time, detector pixel id> tuple
output
serialization
convert data structures to buffers for transmission
sorting
sort data by time or pixel id
producer
transmit data to Kafka cluster

## Slide 10: Pipeline SW Architecture
input
processing
output
Ethernet RingBuffer <9000> (length)
Lockless FIFO <unsigned int, length>
pthread
pthread
pthread
Prototype Pipeline Process v2
UDP
TCP
input thread writes data to buffers by socket receive()
processing thread reads data from RingBuffer, writes (event) data to event RingBuffer
output thread reads (event) data from RingBuffer and appends to Kafka transmit buffer. Sends when full.
No dynamic allocation of memory, no mutexes, small data structures, minimal copying.
Event RingBuffer <12> (length)
Lockless FIFO <unsigned int, length>

## Slide 11: Application Interfaces

## Slide 12: Processes, plugins and pipelines
EFU is a single Linux/Mac process with pthreads
Detectors are loadable modules
Contains the input, processing and output functions

## Slide 13: EFU Connectivity
efu server
processing
input
output
Graphite
db
Command
Client
Kafka
Broker
Detector
Data
UDP
TCP
graphite_ip:2003
broker_ip:9092
config .json
calibration
data
file system
efu_ip:8888
TCP
TCP
efu_ip:9000
Greylog
greylog_ip:12201
TCP
Grafana
grafana_ip:3000
Live
Metrics
servers
user interaction

## Slide 14: Gd-GEM VMM SRS Readout

## Slide 15: Gd-GEM VMM SRS Readout
Gd-GEM Detector
FE Hybr.
FEC
Analog/Electric
Domain
Digital HW Domain
Network Data Domain
Input
Decoded data dump
Output
Proc.
Events
Particle tracks (x,y)
Histograms (x,y)
File System Domain
Data Aggregation Domain
EFU

## Slide 16: Live Data Monitoring
Detector
Live Monitor
Application Monitoring
Detector and readout
Event formation
Aggregation
Gd-GEM
RD-51 SRS

## Slide 17: Delayed ‘Live’ Data Monitoring
Detector
Live Monitor
NFS Storage
Raw data streamer
Multi Grid
~210.000 raw files
~500M Events
Application Monitoring
Detector and readout
Event formation
Aggregation
Gd-GEM
HDF5 files

## Slide 18: Packet sizes and data rates
78 M Evts/s
@ 128 bit

## Slide 19: Wish list

## Slide 20
Packet sizes
  Jumbo frames, pref. 9KB
No implicit data interpretation
  VMM id, FEC#, etc. should be in the packets
Data integrity
  sequence numbers
Efficient encoding
  (VMM2 horror story)
In-band control and config. protocol
  Time units for tdc values
  geometry remappings
  thresholds
  occational counters
Addressing flexibility
  Unicast, multicast
  sequential sender addresses (or ports) (within a range)

## Slide 21: Summary

## Slide 22: The End