## Slide 1: New Simulation Tools and Reproduction of CNCS results using Geant4
E. Dian, K. Kanaki, X. X. Cai, R. Hall-Wilton, A. Khaplanov, T. Kittelmann
dian.eszter@energia.mta.hu
HAS Centre for Energy Research
European Spallation Source ESS ERIC
28 March 2017, ICANS XXII, Oxford
676548

## Slide 2: Outline
The ESS detector challenge
  All instruments in different design phases
  Diverse set of requirements
  Challenge: new detectors with several different designs
Powerful simulation tools
Application in detector design:
  Background study for MultiGrid detector
I’m an end-user!
Notes: ESS
  Instruments in different design phases
  Challenge: new detectors
  Challenging environment around instruments
  Prototyping and existing tech was enough so far -> strong and appropriate sim. Tool needed
General description of coding framework (Before unavailable extensions to unify all packages of this field -> see jamboree. Nice plot from TK!
Openly available , well documented and USEFUL tools, continuous development, use it, it’s not only for dets!)
  NXSG4 - MG
  Ncrystal - ?? Ask XX
  (MCPL?) –LOKI?/SKADI
Application in detector development, detector background (Motivation from det/inst design point of view, example given from bg pov
  Gamma bg, NA -> ref to MCNP paper
  Scat. n bg -> MG@CNCS (+ MG@IN6 ?)
    Detector effect vs instrument effect

## Slide 3: The ESS detector challenge
Various detectors for various instruments at ESS
All with different designs, all have to be optimised for respective instrument requirements
Good measurement =>high signal-to-background
ESS: increased flux
Low level background => need to understand
Effective and universal simulation tool
SANS
BandGEM (Milan/CNR/INFN/CERN/ESS)
Molecular crystallography
Notes: ESS
  Several detectors for various instruments, different phases of development (get nice plot from IKON12!)
  Conclusion:
    We cannot manage without very effective tools
  Core of all measurement is the SBR. ESS increases flux, so increases Signal. Now we have to build detectors with low Bg.
    (keep in mind: @CF it’s easy and fast to build up and modify geometries,
    analyse and plot data, move from one code to the other safe, handles well the big amount of data)

## Slide 4: The ESS detector challenge
Various detectors for various instruments at ESS
All with different designs, all have to be optimised for respective instrument requirements
Good measurement =>high signal-to-background
ESS: increased flux
Low level background => need to understand
Effective and universal simulation tool
Background suppression
e.g. MultiGrid for inelastic instrument
Using scientific quantities for optimisation
Notes: ESS
  Several detectors for various instruments, different phases of development (get nice plot from IKON12!)
  Conclusion:
    We cannot manage without very effective tools
  Core of all measurement is the SBR. ESS increases flux, so increases Signal. Now we have to build detectors with low Bg.
    (keep in mind: @CF it’s easy and fast to build up and modify geometries,
    analyse and plot data, move from one code to the other safe, handles well the big amount of data)

## Slide 5: The detector simulation challenge
Several already existing simulation codes
New or improved features needed:
  Physics
    Coherent scattering
    Inelastic scattering
    Single- and polycrystals…
  And more
    Communication
    Visualisation
    Ready-to use…
inspiration
Notes: Point out: What is geant4?

## Slide 6: NXSG4 extension [Thomas Kittelmann, Mirko Boin]
nxs library
  Low-energy neutron scattering
  Polycrystalline materials
    Coherent and
    Incoherent neutron scattering
http://cern.ch/nxsg4/
  examples, license details
  instructions for installation and usage
  usage of the code (including nxs and SgInfo) is free for non-commercial purposes
doi:10.1016/j.cpc.2014.11.009
NXSG4 makes nxs library available as Geant4 extension
Notes: Point out: What is geant4?

## Slide 7: NXSG4 extension [Thomas Kittelmann, Mirko Boin]
Free-gas model Geant4 aluminum
NXSG4 aluminum
n
n
Geant4 simulation

## Slide 8: NCrystal [Xiao Xiao Cai, Thomas Kittelmann]
NCrystal
  Neutron scattering on single- and polycrystalline materials
  detailed Bragg diffraction
  first principle inelastic model
C++
open source
full-instrument simulation
monochromators, analysers, filters, powder samples
Standalone NCrystal tool coming soon
See Xiao Xiao Cai’s talk
Friday 09:55 (Neutronics 2)
Notes: Coming soon as a standalone tool (right now it’s only available @ CF)
Consistent treatment of low energy neutrons and other particles within one code
  Coherent scattering
    Bragg diffraction
    Inelastic scattering (it was future plan in Sept, ask XX)
  Scattering on single- and poly-crystals

## Slide 9: NCrystal [Xiao Xiao Cai, Thomas Kittelmann]
Powder Diffractometer PUS at IFE, Norway
Standalone NCrystal tool coming soon
Geant4 simulation
Notes: Coming soon as a standalone tool (right now it’s only available @ CF)
Consistent treatment of low energy neutrons and other particles within one code
  Coherent scattering
    Bragg diffraction
    Inelastic scattering (it was future plan in Sept, ask XX)
  Scattering on single- and poly-crystals

## Slide 10: MCPL-Monte Carlo Particle List [Thomas Kittelmann, Esben Klinkby, Erik B. Knudsen, Peter Willendrup]
Monte Carlo Particle List
  https://mctools.github.io/mcpl/
  Interchange particles with all their properties between MC packages
  flexible yet efficient storage of particle-state information
http://sine2020.eu/news-and-media/mcpl-a-new-format-that-simplifies-data-interchange-between-applications.html
Best code for best application
arxiv:1609.02792
Contact:
mcpl-developers@cern.ch

## Slide 11: ESS Coding Framework [Thomas Kittelmann, Xiao Xiao Cai, Kalliopi Kanaki]
Geant4 simulation framework
  Developed by ESS Detector Group
  Used by other groups in ESS e.g. Accelerator Group, Shielding and Optics Group
Contains all afore mentioned tools:
  Integrated
  Transparent for end-user
  Out-of-the-box usage
And more:
  Effective build system
  Python interface
  Easy-to-handle histograms for analysis
  3D visualisation
  Griff: an effective binary format for results
  Powerful parameter scan without recompilation
  Intuitive
  User friendly
Contact:
Thomas Kittelmann: thomas.kittelmann@esss.se
Xiao Xiao Cai: xcai@dtu.dk
Kalliopi Kanaki: kalliopi.kanaki@esss.se
  Fast to develop new simulations
Available, just send a mail 
I’m a happy end-user!
Notes: Contains all above mentioned tools are integrated, transparent for end-user in ready-to-use (out-of-the-box ?) form and more
G4!
  Build system
  Python interface
  Histograms
  3Dviewer
  Griff
  scalable
  Fast, safe and user friendly
  Used by other groups in ESS e.g. Accelerator Group, Shielding and Optics Group

## Slide 12: ESS Coding Framework [Thomas Kittelmann, Xiao Xiao Cai, Kalliopi Kanaki]
Geant4 simulation framework
  Developed by ESS Detector Group
  Used by other groups in ESS e.g. Accelerator Group, Shielding and Optics Group
Contains all afore mentioned tools:
  Integrated
  Transparent for end-user
  Out-of-the-box usage
And more:
  Effective build system
  Python interface
  Easy-to-handle histograms for analysis
  3D visualisation
  Griff: an effective binary format for results
  Powerful parameter scan without recompilation
  Intuitive
  User friendly
Contact:
Thomas Kittelmann: thomas.kittelmann@esss.se
Xiao Xiao Cai: xcai@dtu.dk
Kalliopi Kanaki: kalliopi.kanaki@esss.se
  Fast to develop new simulations
Available, just send a mail 
I’m a happy end-user!
Now let’s use it!
Notes: Contains all above mentioned tools are integrated, transparent for end-user in ready-to-use (out-of-the-box ?) form and more
G4!
  Build system
  Python interface
  Histograms
  3Dviewer
  Griff
  scalable
  Fast, safe and user friendly
  Used by other groups in ESS e.g. Accelerator Group, Shielding and Optics Group

## Slide 13: Detector background study with Monte Carlo codes
Sources of neutron detector background
  Neutron induced gamma background (MCNP6)
    Prompt gamma radiation from neutron capture
    Decay gammas from neutron activation
  Scattered neutrons (Geant4)
    Elastic, inelastic
    Coherent, incoherent
Great impact of Coding Framework!
41Ar activity saturates at 128 mBq/cm3 low
Negligible signal from self-activation
General neutron activation study prepared with MCNP6 for ESS operation conditions - Ar/CO2 counting gas - Aluminum-frame
E. Dian et al. arXiv:1701.08117
submitted to ARI
Notes:     General neutron activation study already prepared for B4C-based neutron detectors -> ref arXiv:1701.08117
    If it weren’t negligible, we could use it as an input to G4 
    Run until sample, MCPL-> uniq tool to optimise det with realistic (meas or sim) data

## Slide 14: Detector background study with Monte Carlo codes
Sources of neutron detector background
  Neutron induced gamma background (MCNP6)
    Prompt gamma radiation from neutron capture
    Decay gammas from neutron activation
  Scattered neutrons (Geant4)
    Elastic, inelastic
    Coherent, incoherent
Great impact of Coding Framework!
General neutron activation study prepared with MCNP6 for ESS operation conditions - Ar/CO2 counting gas - Aluminum-frame
E. Dian et al. arXiv:1701.08117
submitted to ARI
41Ar activity saturates at 128 mBq/cm3 low
Negligible signal from self-activation
Notes:     General neutron activation study already prepared for B4C-based neutron detectors -> ref arXiv:1701.08117
    If it weren’t negligible, we could use it as an input to G4 
    Run until sample, MCPL-> uniq tool to optimise det with realistic (meas or sim) data

## Slide 15: Detector background study with Monte Carlo codes
Sources of neutron detector background
  Neutron induced gamma background (MCNP6)
    Prompt gamma radiation from neutron capture
    Decay gammas from neutron activation
  Scattered neutrons (Geant4)
    Elastic, inelastic
    Coherent, incoherent
Great impact of Coding Framework!
General neutron activation study prepared with MCNP6 for ESS operation conditions - Ar/CO2 counting gas - Aluminum-frame
E. Dian et al. arXiv:1701.08117
submitted to ARI
41Ar activity saturates at 128 mBq/cm3 low
Negligible signal from self-activation
Notes:     General neutron activation study already prepared for B4C-based neutron detectors -> ref arXiv:1701.08117
    If it weren’t negligible, we could use it as an input to G4 
    Run until sample, MCPL-> uniq tool to optimise det with realistic (meas or sim) data

## Slide 16: Detector background study with Monte Carlo codes
Sources of neutron detector background
  Neutron induced gamma background (MCNP6)
    Prompt gamma radiation from neutron capture
    Decay gammas from neutron activation
  Scattered neutrons (Geant4)
    Elastic, inelastic
    Coherent, incoherent
Great impact of Coding Framework!
General neutron activation study prepared with MCNP6 for ESS operation conditions - Ar/CO2 counting gas - Aluminum-frame
E. Dian et al. arXiv:1701.08117
submitted to ARI
41Ar activity saturates at 128 mBq/cm3 low
Negligible signal from self-activation
Notes:     General neutron activation study already prepared for B4C-based neutron detectors -> ref arXiv:1701.08117
    If it weren’t negligible, we could use it as an input to G4 
    Run until sample, MCPL-> uniq tool to optimise det with realistic (meas or sim) data

## Slide 17: Scattered neutron background – power of simulation
Detector
Sample environment
Scattered neutron
Real and measurable neutron energy at conversion point
Scattered neutron
Follow the history of neutrons
Study and distinguish background effects
Guidelines for detector design
Realistic simulation
Geant4 simulation

## Slide 18: Large area detector for chopper spectroscopy - MultiGrid
Bla
Large area MultiGrid detector chosen as example
Chopper spectroscopy:
  Low background is essential
A. Khaplanov et al.
http://dx.doi.org/10.1016/j.nima.2012.12.021
Geant4 simulation
Notes: Point out: Visualisation!

## Slide 19: MultiGrid detector test at ILL
In-beam test of the Boron-10 Multi-Grid neutron detector at the IN6 time-of-flight spectrometer at the ILL
A. Khaplanov et al.
http://iopscience.iop.org/article/10.1088/1742-6596/528/1/012040/pdf
Validation
No shielding on the rear wall of grids

## Slide 20: MultiGrid detector test at ILL Measured data (ToF, depth of detection)
Validation

## Slide 21: MultiGrid detector test at ILL Measured and simulated ToF-depth of detection
ToF
Depth in detector [cells]
Backscatter from the unshielded rear wall of the detector at 4.6 Å
Depth in detector [cells]
Validation
Measured ToF-depth characteristic and backscatter phenomena reproduced with simulation at 4.1 and 4.6 Å
measured
simulated
Geant4 simulation

## Slide 22: MultiGrid detector test at ILL Measured and simulated ToF spectra
Validation
Measured ToF-spectrum reproduced with simulation at 4.1 and 4.6 Å
Estimated flat alpha-background added (red), unique for this prototype
Geant4 simulation

## Slide 23: MultiGrid detector test at CNCS, SNS
Detector
Sample environment
3.3 m
Isotropic scattering particles simulated from sample
Geant4 simulation
Notes: Origin of particles…

## Slide 24: MultiGrid detector test at CNCS, SNS [Anton Khaplanov]
Chopper spectroscopy
Measured quantities:
  ToF
  detection-coordinates
Energy transfer: Etrf = Einitial – Efinal
Etrf = Einitial - Efinal
Derived energy transfer at 3.678 meV from measurement
Counts
See Anton Khaplanov’s talk Today 12:10 (Detectors 1)
Anton Khaplanov et al.: Multi-Grid Detector for Neutron Spectroscopy: Results Obtained on Time-of-Flight Spectrometer CNCS
Submitted to JINST arXiv:1703.03626

## Slide 25: MultiGrid detector test at CNCS, SNS
Etrf = Einitial - Efinal
Elastic peak
Scattered neutron background from detector
Geant4 simulation

## Slide 26: MultiGrid detector test at CNCS, SNS
Etrf = Einitial - Efinal
Elastic peak
Scattered neutron background from detector
Geant4 simulation
Scattered neutron background from sample environment

## Slide 27: MultiGrid detector test at CNCS, SNS
Etrf = Einitial - Efinal
Elastic peak
Scattered neutron background from detector
Geant4 simulation
Scattered neutron background from sample environment

## Slide 28: MultiGrid detector test at CNCS, SNS
Etrf = Einitial - Efinal
Elastic peak
Scattered neutron background from detector
Scattered neutron background from sample environment
Geant4 simulation

## Slide 29: MultiGrid detector test at CNCS, SNS
Etrf = Einitial - Efinal
Elastic peak
Scattered neutron background from detector
Scattered neutron background from sample environment
Distinguish different sources of background
Detailed analysis and quantification of background effects
Energy transfer reproduced with simulation at 3.678 meV
Validation

## Slide 30: Summary
Great progress in neutron scattering simulation
  Improved modeling for neutron scattering on crystalline material (NXSG4, NCrystal)
  Effective particle interchange (MCPL)
    Easy to combine MC codes
  ESS Coding Framework, where all tools are combined
  Full-scale instrument simulation can be done with a single application
Realistic MultiGrid model built
  reproduced measured results from IN6 and CNCS experiments
Ready to use for optimisation
A powerful neutron simulation toolkit developed
Instruments with better signal-to-background ratio by design

## Slide 31: Summary
Great progress in neutron scattering simulation
  Improved modeling for neutron scattering on crystalline material (NXSG4, NCrystal)
  Effective particle interchange (MCPL)
    Easy to combine MC codes
  ESS Coding Framework, where all tools are combined
  Full-scale instrument simulation can be done with a single application
Realistic MultiGrid model built
  reproduced measured results from IN6 and CNCS experiments
Ready to use for optimisation
A powerful neutron simulation toolkit developed
Use the Force, Luke!
Instruments with better signal-to-background ratio by design

## Slide 32
28 March 2017, ICANS XXII, Oxford
676548
Thank you for your attention!
Thanks to the collaborators for all the prepared tools and materials, and for making my life easier!

## Slide 33: MultiGrid detector test at CNCS [Anton Khaplanov]
Chopper spectroscopy
Measured quantities:
  ToF
  detection-coordinates
Energy transfer: Etrf = Einitial – Efinal
Etrf = Einitial - Efinal
Derived energy transfer at 3.807 meV from measurement
Counts
See Anton Khaplanov’s talk Today 12:10 (Detectors 1)
Anton Khaplanov et al.: Multi-Grid Detector for Neutron Spectroscopy: Results Obtained on Time-of-Flight Spectrometer CNCS
Submitted to JINST arXiv:1703.03626

## Slide 34: MultiGrid detector test at CNCS
Etrf = Einitial - Efinal
Elastic peak
Scattered neutron background from detector

## Slide 35: MultiGrid detector test at CNCS
Etrf = Einitial - Efinal
Elastic peak
Scattered neutron background from detector
Scattered neutron background from sample environment

## Slide 36: MultiGrid detector test at CNCS
Etrf = Einitial - Efinal
Elastic peak
Scattered neutron background from detector
Scattered neutron background from sample environment

## Slide 37: MultiGrid detector test at CNCS
Elastic peak
Scattered neutron background from detector
Scattered neutron background from sample environment
Etrf = Einitial - Efinal

## Slide 38: MultiGrid detector test at CNCS
Etrf = Einitial - Efinal
Elastic peak
Scattered neutron background from detector
Scattered neutron background from sample environment
Distinguish different sources of background
Detailed analysis and quantification of background effects
Energy transfer reproduced with simulation at 3.807 meV
Validation