## Slide 1: ESS elliptical cryomodule
ESS CRYOMODULE FOR ELLIPTICAL CAVITIES
CRITICAL DESIGN REVIEW
SACLAY April 3th, 2017
Unité mixte de recherche CNRS-IN2P3
Université Paris-Sud 11
91406 Orsay cedex
Tél. : +33 1 69 15 73 40
Fax : +33 1 69 15 64 70
http://ipnweb.in2p3.fr

## Slide 2: ESS elliptical cryomodule
SUMMARY
Overview
Medium & High beta
Bellows & transitions
Cavity string supporting system
Coupler bell
Spaceframe
Thermal screen
Vacuum vessel
Transportation
Heat balance
Jumper connections
Instrumentation

## Slide 3: ESS elliptical cryomodule

## Slide 4: ESS elliptical cryomodule

## Slide 5: Main characteristics
GROUND
1156,3
506,3
4300
6587,6 (valve flange to valve flange)
1500
1500
1500
2969,5
2745
1500
1245
Ø1216
For more information, see interface drawings:
24G9914 Tunnel version
24G9916 Test stand version
24G9919 Transportation version
Weight: 6 tons

## Slide 6: High and medium beta standardization
High beta (0,86):
5 cells
Length 1316,91mm
Medium beta (0,67):
6 cells
Length 1259,40mm
57,5 mm

## Slide 7: High and medium beta standardization
Identical sub-assemblies:
Vacuum vessel
Spaceframe
Thermal shield
Cryogenics circuits
Position of the nozzle
Ø418
20
188
900
120,3 (HB)
115,3 (MB)
180
908
Blocks for half ring fasteners
Position of the nozzle
1316,91 (HB) / 1259,4 (MB)
Main identical dimensions
Main differences
Same mechanical interfaces in the tunnel
250
794
Specific components:
Inter cavities bellows
Cold/warm transitions
1500 between couplers

## Slide 8: Inter-cavities bellows
Manufacturer WITZENMANN/HYDRA
Internal diameter 135mm
External diameter 174mm
Corrugation length 13mm
Thickness 2x0.3mm
Axial stroke per corrugation +/- 3mm max.
Axial stiffness per corrugation 210N/mm
Radial stroke per corrugation +/-0.08mm max.
Radial stiffness per corrugation 44500N/mm
HIGH BETA
Number of corrugations: 6
Overall length 183mm (at rest)
Axial stroke for 6 corrugations +/-18mm
Axial stiffness for 6 corrugations 35N/mm
Radial stroke for 6 corrugations +/-0.48mm
Radial stiffness for 6 corrugations 7417N/mm
MEDIUM BETA
Number of corrugations: 10
Overall length 240,5mm
Axial stroke for 10 corrugations +/- 30mm
Axial stiffness for 10 corrugations 21N/mm
Radial stroke for 10 corrugations +/-0.80mm
Radial stiffness for 10 corrugations 4450N/mm
Hexagonal aluminium seals for bellows and transitions
(XFEL Type)

## Slide 9: Cold / warm transitions
Weight: 5.8 Kg without the flat cover and the vacuum valve
25.5 Kg with the flat cover and without the vacuum valve
49 Kg with the flat cover and the vacuum valve
BELLOWS
Metal: stainless steel
Type: corrugated bellows
Internal diameter: 105mm
External diameter: 132mm
Thickness: 0.3mm
Corrugation length: 6.3mm
Number of corrugations: 5
Axial spring rate per corrugation: 240N/mm
Axial spring rate for 5 corrugations: 48N/mm
Located at each extremity of the cryomodules
Specific supporting tools
External vacuum valve
Air
2 identical transitions for high beta
2 different for medium beta

## Slide 10: Cold / warm transitions
Heat transfer on the 2K circuit: 0.91W
Heat transfer on the 50K circuit: 1.40W
NEITHER ICING
NOR CONDENSATION OUTSIDE
THERMAL BEHAVIOUR
External radiation replaced by heat flux
For more information, see technical note:
"HB Cryomodule – Cold/warm transition"
(IPN/EDMS-I032756)

## Slide 11: Cavity string supporting system
Rods
Magnetic
shield
Half rings linked to the tank (under the magnetic shield)
Helium tank
Half ring
(titanium)
Clevis pin
(rotating joint)
Supporting rod
(TA6V, Diam. 6mm)
Hanging of the cross rods
on 2 titanium half rings fastened (on their middle only) to the helium tank on one side
On the spaceframe on the other side
Spaceframe ring
Fastening of the thermal shield
(& thermalization)
The rods are composed of 2 sections. The first is assembled on the cavity string alone, the second after insertion in the spaceframe while the hanging of the thermal shield

## Slide 12: Cavity string supporting system
- Heavy load spring D16x32 H38mm, stiffness 518N/mm
- Stroke under 3000N pre-stress: 5,8mm
- Locking of the rods after pre-stress
- Rod length 490mm, diameter 6mm, material TA6V
LOCKING DEVICE ON THE SPACEFRAME
M6 thread
M16 thread
Spring
Blocking nut
Rod
Pre-stress nut
Intermediate screw blocked in rotation
Spaceframe ring

## Slide 13: Cavity string supporting system
MECHANICAL STRESS FIGURES
Stress in the rod core (M6 thread, Ø4.77mm, 17.9mm2) due to the 3000N pre stress: 168MPa
Stress in the upper rod core due to the weight (900N per rod): 51MPa
Stress in the rod core due to the thermal shrinkage: 250MPa (equiv. force 4443N)
Total stress in the rod core: 469MPa (Tensile yield strength 825MPa to 1040MPa)
Maximum force in one upper rod: 8343N
Maximum vertical acceleration during transportation: 5g (given to inter-cavity bellows maximum transverse displacement)
Characteristics | TA6V
Density | 4.43
Young modulus (GPa) | 110 (293K)
Poisson’s ratio | 0.33
Yield strength (MPa) | 825 (290K)
Heat conductivity 4-50K (W/m.K) | 0.233-2.411
Heat conductivity 50-300K (W/m.K) | 2.411-7.555
Thermal shrinkage 4-293K | 0.0017
Traction test performed at more than 1 ton
For more information, see technical note:
"Cavity string supporting system"
(IPN/EDMS-I036271)

## Slide 14: Cavity string supporting system
Titanium half rings
3000N pre-stress
After cool down
Locked point on the spaceframe
SIMPLIFIED
MODEL
Rod displacement
Titanium tank alone
Spaceframe
Rods
Half rings
Helium tank
Displacement
Stress
Max 31MPa

## Slide 15: Cavity string supporting system
Material | G10 (Normal dir.) |  | Nitronic 50 (SS304) |  | TA6V |  |  | 
Diameter (mm) | 6 | 7 | 6 | 7 | 3 | 4 | 5 | 6
Section (mm2) | 28.27 | 38.48 | 28.27 | 38.48 | 7.07 | 12.57 | 19.63 | 28.27
Loss 4-50K (260mm) (W) | 0.00078 | 0.0011 | 0.01354 | 0.01846 | 0.0016 | 0.0028 | 0.004 | 0.00629
Loss for 32 rods (W) | 0.025 | 0.034 | 0.433 | 0.591 | 0.050 | 0.089 | 0.139 | 0.201
Loss 50-293K (140mm) (W) | 0.01423 | 0.0194 | 0.39596 | 0.5385 | 0.0453 | 0.0805 | 0.1257 | 0.18086
Loss for 32 rods (W) | 0.455 | 0.619 | 12.671 | 17.232 | 1.450 | 2.576 | 4.022 | 5.788
HEAT LOSSES
SOLUTION ADOPTED
Calculation by Ansys®
Length 490mm
50K thermalization at 300mm

## Slide 16: Axial positioning
No permanent axial rods
Adjustment at 290K of the axial position of the cavities by rods fixed at different spaceframe rings(removed after jamming of the couplers on the vacuum vessel)
The rods are located between the tank and the magnetic shield
Locking by threaded rod
Jamming on the coupler flange (see next slide)
All the tooling is temporary and is removed for operation after axial jamming of the cavity string (see following slide)
This tooling is carried out again for transportation (g-load compensation)
Transverse bar

## Slide 17: Axial blocking
Coupler
Atmospheric pressure compensation
(see relevant slides)
"Bell" for vessel/coupler connection
Bellows
Coupler flange
Thin plate
(thickness 0,75mm)

## Slide 18: Atmospheric pressure compensation
The aim of the device is to limit the load on the cavity flange while pumping and cooling (1 ton if nothing done)
Vacuum effect
9985N
Spring effect
9177N
Doorknob weight 550N
Flange locked to the vessel
Thermal shrinkage
258N
Effort on the flange (N) | 0 (stop rod) | 808 (Push) | 0
A pre-stress is performed by means of 3 heavy load springs (3 x 172N/mm). A stop rod device (x3) avoids any force on the coupler flange during this operation.
The vacuum pressure is applied to the bellows flange (Dext 360mm)
Due to the cooling, the thermal shrinkage of the coupler (0,5mm) induces both the lifting of the lower parts of the RF line (coaxial line and door-knob) and a compression of the springs
Stop rods
Bellows
Springs
Flange
Coupler

## Slide 19: Atmospheric pressure compensation
Test equipment to validate the atmospheric pressure compensation device (CEA)

## Slide 20: Atmospheric pressure compensation
PRE-STRESS OPERATION
The stress value is applied with accuracy by means of a hydraulic jack. Each spring remains in position between 2 flanges and is released after assembly .

## Slide 21: spaceframe
Closing parts
(stainless steel)
8 Pipes D40x60
(Alu. 6060T6)
Rings (Alu.6082 T651)
(thickness 30mm)
Positioning & resting blocks
Rollers
(1st level)
Rollers
(2nd level)
Hanging of the cavities
Hanging of the thermal shield
Positioned inside the vacuum vessel
Remains at ambient temperature
Rolling inside the vacuum vessel on 2 rails
For more information, see technical note:
"ESS Cryomodule - Spaceframe"
(IPN/EDMS-I046559)

## Slide 22: Spaceframe locking
Axial locking at the trap doors levels (2x2)
The spaceframe is directly fastened to the vacuum vessel by a set of brackets
Transverse blocking:
3 jacks at 120°
On 3 sections
Positioning:
3 vertical jacks

## Slide 23: Spaceframe mechanical behaviour
During insertion in the vacuum vessel (on rollers)
Stress max. 38MPa
Rollers
Total Displ. (mm) | Structure Displ. (mm) | Blocks Displ. (cavity string fastening) (mm) | Max stress (Mpa)
2,06 | 1,99 (Z:-1,96 to +0,42) | 0,07 à 1,76 (Z: -1,67 to +0,17) | 38
Supports
During the positioning
& in operation (on supports)
Stress max. 38MPa
Calculations performed with full load:
Weight, pre-stress & cooling down (rods).
Minimum yield strength Rp0,2 for aluminium 6060T6 or 6082T6: 240MPa

## Slide 24: Thermal shield
Made of aluminium
Thickness 2mm
Several plates
2 closing plates at each extremity
Cooling circuit
Extruded aluminium pipe
stainless Steel/alu. transition at each extremity
Weld seams
Cooling circuit connections: weld or VCR

## Slide 25: Thermal shield hanging & thermalization
Elastic boxes
Thermal shield
Supporting rods
The boxes are blocked only at the fixed point at mid of the thermal shield
Locking screws
& thermalization
FOLDED BOXES ENSURE THE AXIAL MOVING AND THE THERMALIZATION OF THE THERMAL SHIELD.
THEY PERMIT ONLY LOW DISPLACEMENTS ON OTHER DIRECTIONS
3 prototypes have been made (thickness 0,5 , 1 et 1,5mm)
Maximum thermal shrinkage to be compensated: 12,9mm

## Slide 26: Thermal shield thermal aspects
In operation
Cooling down
Thermal shrinkage
Fixed point
Constant temperature gradient along 4 sections
Temperature map
Temperature map

## Slide 27: Thermal shield thermal aspects - stress
In operation
Cooling down
Aluminium 6082T6:
Yield strength 260MPa at ambient temperature
Yielding is limited at very local surfaces
For more information, see technical note:
"ESS Cryomodule – Thermal shield"
(IPN/EDMS-I04659)
As the shield length is divided in several sections for manufacturing constraints (4 for M-ECCTD), the stress is relieved with regard to the calculations

## Slide 28: Spaceframe & thermal shield
M-ECCTD first assembly

## Slide 29: Vacuum vessel
Spaceframe jacks adjustment
Optical alignment
Length: 6285mm
Internal diameter: 1200mm
Thickness: 8 mm
Weight: 3,8 tons
2 supports
Supports
2 flat covers at each extremity
Rail for spaceframe guiding
Stiffeners
Trap doors for CTS access (motor removing)
For more information, see technical note:
"Vacuum vessel – EN13445 Compliance"
(IPN/ATRIUM-46561)

## Slide 30: Vacuum sealing

## Slide 31: Pumping & connecting ports
Feedtroughs
LEMO Type HGP (vacuumtight)

## Slide 32: Transportation additional links
Fastening of the thermal shield
(2x4 positions)
Fastening of each cavity
(see previous slide)
Fastening of the spaceframe on the vacuum vessel
(see previous slide)
Fastening of the jumper cryogenic pipes
To be removed:
Door knobs
Actuators
Others
Specified accelerations during
transportation (CEA) :
Axial (X): 2,5g
Transverse (Y): 2,5g
Vertical (Z): 2,5g
A transportation test Saclay/Lund is foreseen in 2017 for the M-ECCTD

## Slide 33: transportation
Main modes | Frequency (Hz) | % load X | % Load Y | % Load Z
7 | 19,5 |  | 21,5 | 
10 | 21,4 |  | 42 | 
25 | 37,3 |  |  | 24,4
29 | 41,2 |  |  | 5,8
36 | 45 | 11,8 |  | 
Modal analysis
These values are high enough to avoid any activation during transportation
(>16Hz)
For more information, see technical note:
"Cryomodule ESS – Analyse mécanique"

## Slide 34: transportation
"Static" acceleration
Accelerations :
Axial (X): 5g
Transverse (Y): 1,5g
Vertical (Z): 3g
 | X (axial) (Mpa) | Y (trans) (Mpa) | X (vert) (Mpa) | Rp02 at 300K (Mpa)
Vacuum vessel | 44,9 | 41,3 | 45,7 | 210 (SS)
Thermal shield | 43,6 | 12,3 | 30,2 | 240 (Alu)
Space-frame | 35,8 | 24,9 | 48,6 | 240 (Alu)
Cryo. lines | 33,3 | 6,8 | 20,8 | 210 (SS)
Support. rods | 138 | 157 | 238 | 825 (TA6V)
Von-Mises stress

## Slide 35: Heat balance
For more information,
see technical note:
"ESS Cryomodule –
Global heat balance"
(IPN/EDMS-I036405)

## Slide 36: Diphasic pipe & jumper connection
JUMPER CONNECTION
Displacement
Stress
Avoid any additional constraint other than the weight at the jumper VLP line connection in order to limit:
The stress at the connection between the diphasic pipe and the helium tank
The displacement of the first cavity
Additional flexible hoses in the jumper (vertical section on the valve box side)???
To be defined

## Slide 37: M-ecctd instrumentation
Instrumentation | Brand / Reference | Series. Comments & issues
Temperature gauge <10K | Cernox / CX-1050 | Concerns about resin radiation behaviour
Temp. gauge Pt100 >40K | Pyro-Controle | 
Pressure transmitters | MKS / 722B | Remote sensor (radiations)?
Level gauges | Cryomagnetics (L 623mm) | 
Rupture disk | Witzenmann / DN100 | 
Safety valve 0,64bar (SV90) | Herose / 6850 | To be welded. Difficulties do find on the market
Controlled valve 0,5bar (CV91) | To be defined | 
Regulated valve (CV01, CV02) | Weka | 
Flexible heaters | Omega / KHLV | 
Heaters (cartridge, EH11/21/31/41) | Vulcanic / Vulstar 1004 | 
Connectors | LEMO / HGP | 
Beam vacuum valves (CV80/81) | VAT / 48240 (DN100) | 
Insulation vacuum valve (CV71) | VAT / 10844 (DN160) | 
He purge valve (HV90) | VAT / 28424 DN16 + adapt. | 
Vacuum Pirani gauge | Pfeiffer / TPR018 | 
Vacuum Penning gauge | Pfeiffer / IKR-070 | 

## Slide 38: ESS elliptical cryomodule
Fruitful collaboration between IPNO and CEA
Design performed in continuous collaboration
Cooperation to carry on for M-ECCTD assembly, H-ECCTD and series (Technical support and mechanical files follow-up)
As a whole, the supply of M-ECCTD components and sub-assemblies has gone well.
Some remaining design topics still to fix:
Helium collecting line
Jumper connection
Instrumentation

## Slide 39: ESS elliptical cryomodule
Thank you for your attention