## Slide 1: The MYRRHA LEBT Commissioning & Space Charge Compensation Experiments
SLHiPP - 7 Thursday, June 8, 2017
Orsay, France
F. Bouly, D. Bondoux (LPSC\IN2P3\CNRS)
Jorik Belmans, Dirk Vandeplassche (SCKCEN)
Nicolas Chauvin, Frédéric Gérardin (CEA)

## Slide 2: MYRRHA Linac
Courtesy of J.- L. Biarrotte
Courtesy of H. Podlech

## Slide 3: LEBT Functions
 The Low Energy Beam Transfer line (LEBT) is the first 3 meters of the MYRRHA accelerator
Ensure the ‘safe’ beam transport from the source to the RFQ :
 Minimise the beam losses  Increased Reliability
 Condition the beam for the RFQ
 Required parameters at the RFQ entrance : εRMS.norm.proton ≤ 0.2 π.mm.mrad
β =0.04 mm/π.mrad & α = 0.88
‘Clean’ the proton beam from other species (H2+,H3+)
 The Ion source produces protons but also H2+,H3+ (ionisation of H2 gas)
 Give/Create the temporal beam time structure (‘holes’ / pseudo-pulsed beam / power mitigation)
Proposed MYRRHA beam time structure for operation: -> long blue pulses are sent to the reactor (mean power is adjusting with pulse length) -> short red ones are sent to ISOL experiment
40 ms
38 ms

## Slide 4: MYRRHA LEBT Design and Construction
● Design, Construction & Commissioning funded by EU projects (MAX - FP7, MARISA - FP7, MYRTE) and SCK-CEN
● Collaboration :
 LPSC (CNRS) : solenoid design, collimation , vacuum chamber, experimental area, part of the control system,…  SCK-CEN : Chopper + collimation cone, …  Cosylab (+ADEX) : Specific control system developments
 Compact design : ~ 3 meters long with two solenoids
 No ‘clean’ ions separation to ensure a direct proton current monitoring
 A minimum of elements/magnet to tune (Reliability )
 Simple design (Reliability)
 Minimise the number of electrostatic elements (Reliability)
 Shorter Space Charge Compensation transients than in a longer version

## Slide 5: Beam dynamics : Space Charge & Compensation
● Defocusing effect : Coulomb repulsion of charged particles inside the beam
● 2 contributions (Lorentz):  Electrostatic : repelling Force
   Magnetic : attractive Force (charged particles in movement )
Radial force seen by one particle of a continuous (DC) cylindrical and homogenous beam
βL : reduced speed
: vacuum permittivity
q : charge
: beam current
● Complex phenomena, difficult to model, depends on many parameters : influence of the vacuum chamber walls, beam transverse and longitudinal distribution, different species/ions, residual gas interaction, etc.
● A solution to compensate the beam diverging effect in the LEBT :
→ Use the Ionisation of the residual gas in the vacuum chamber.
Courtesy of N. Chauvin

## Slide 6: The LEBT installed at LPSC Grenoble
ECR ion source
Solenoid 1
+ Steerers
Solenoid 2
+ Steerers
Faraday Cup
Faraday Cup
Allison Scanners
Chopper
Collimation system
Collimation cone
+ ACCT
ECR Source M-1000
Collimators & Allison scanner
Chopper

## Slide 7: LEBT tuning
● Goal : tune the solenoids & steerers settings to optimise the transmission through the LEBT and to match the beam into the RFQ
● Solenoid scan on the beam transmission
Isource set at 9 mA, difficult to control below this value (dropout in an other plasma mode)
 Beam current & Twiss parameters measured 26.2 cm after the hole of the collimation cone (FC + Allisson scanner)
 Estimation of the beam parameters to be expected at the Emittance-meter location with TraceWin (SCC comp. : ~ 85% , εRMS.norm.proton = 0.1 mm.mrad)
Requirement at RFQ input
-> β =0.04 mm/mrad & α = 0.88
Estimation : 262.5 mm after the RFQ injection hole
-> β ~ 2.9 mm/π.mrad & α ~ -12.5
RFQ injection
(LEBT output)
Measurement
Allison-Scanner
262.5 mm

## Slide 8: First Transmission map
● Isource = 9 mA
● No collimation in the middle of the LEBT
● No steerer tuning
● P = 1.1 10-5 mbar
● Beam current transmitted through the LEBT as function of the solenoid focusing (current in the coils)
Need to adjust the central position of the beam with the steerers
Need collimation to adjust beam current
Design goal

## Slide 9: Transmission map : Tuned LEBT
● Collimator aperture : 48 mm
● Steerers settings inside solenoid 2 :
 IsteererH = 0.5 A
 IsteererV = -2 A
● Isource = 9 mA
● P = 7 10-6 mbar
No collimation
With collimation

## Slide 10: Transmission map : Tuned LEBT + Kr injection
● Collimator aperture : 48 mm
● Steerers settings inside solenoid 2 :
 IsteererH = 0.5 A
 IsteererV = -2 A
● Isource = 9 mA
● P = 2.4 10-5 mbar (Kr injection)
Gas injection (pressure, type) has an effect on the transmission in steady state and therefore on the space charge neutralisation
Already observed on several experiements :
_ R. Hollinger et. al. , “High current proton beam investigation at the SILHI-LEBT at CEA Saclay ”, TU3001, Proceedings of LINAC2006 , Knoxville, Tennessee, USA,2006
_ D. Winklehner, D. Leitner, "A space charge compensation model for positive DC ion beams." Journal of Instrumentation 10.10 (2015): T10006.
_ R. Ferdinand et al. , “Space-charge neutralization measurement of a 75 keV, 130 mA hydrogen-ion beam”, Proceedings of PAC’97, Vancouver, B.C., Canada,1997

## Slide 11: Space charge compensation
● Evolution of the Emittance in the middle of the LEBT as function of the gas pressure
 the focusing strength of the solenoid is kept constant (Isol=69A)
 Argon or Krypton gas injected
 The beam current is kept constant at the emittance measurement location : Iproton ≈ 8.5 mA
● In steady state we observed that the emittance decreases while residual gas pressure is increased
~1.5 m from the source extraction hole
Chart: Pressure (mbar)
| 8.9399999999999991E-6 | 1.0739999999999999E-5 | 1.2259999999999998E-5 | 1.382E-5 | 2.2220000000000001E-5 | 3.782E-5 | 5.3820000000000003E-5 | 6.9820000000000006E-5 | 8.5820000000000015E-5 | 1.7382000000000004E-4 | 3.2582000000000005E-4
 | 0.15028 | 0.14874 | 0.1498 | 0.1499 | 0.14433 | 0.11354 | 0.10798 | 0.1082 | 0.10677 | 0.1031 | 0.11357
 | 0.143 | 0.1249 | 0.12065 | 0.11285 | 0.11435 | 0.1071 | 0.1957
Ar injection - Horiz. Plane
Kr injection - Vert. Plane

## Slide 12: Space charge compensation
Chart: Pressure (mbar)
| 8.9399999999999991E-6 | 1.0739999999999999E-5 | 1.2259999999999998E-5 | 1.382E-5 | 2.2220000000000001E-5 | 3.782E-5 | 5.3820000000000003E-5 | 6.9820000000000006E-5 | 8.5820000000000015E-5 | 1.7382000000000004E-4 | 3.2582000000000005E-4
 | -1.4254 | -0.96131 | -0.90163 | -0.83513 | -0.49695 | 0.10684 | 0.44053 | 0.67507 | 0.79619 | 1.8617 | 2.6257
 | -1.0238 | -0.1777 | 0.0574 | 0.4038 | 0.7452 | 1.1573 | -1.8207
● For a given focusing strength of the solenoid :
→ the beam divergence is changing with the gas pressure
P =5.4 10-5 mbar
Ar injection - Horiz. Plane
Kr injection - Vert. Plane
P = 9.2 10-6 mbar

## Slide 13: Space charge compensation degree
● Measurement of the space charge neutralisation degree with Kr injection:
Chart: Pressure (mbar)
| 1.2849999999999999E-5 | 1.9074999999999999E-5 | 2.9575000000000001E-5 | 4.4325E-5 | 5.9324999999999999E-5 | 7.3574999999999999E-5 | 8.1000000000000004E-6
 | 85.2239 | 91.2854 | 92.24 | 93.3839 | 94.1144 | 94.4088 | 77.1692
● Careful – several assumptions :
 4-grid analyser (low and noisy signal)
 Beam distribution assumed Gaussian
 Beam radius calculated from emittance measurements

## Slide 14: Chopper & SCC Transients
Chart: Pressure (mbar)
| 1.096E-5 | 1.906E-5 | 2.9559999999999998E-5 | 4.1059999999999997E-5 | 5.0060000000000005E-5 | 6.3560000000000008E-5 | 6.8559999999999994E-5 | 8.106E-5 | 1.3560000000000001E-5 | 1.256E-5 | 2.4559999999999999E-5
Mesure ACCT | 128.5 | 37.2 | 10.4 | 11.6 | 7.4 | 3.8 | 5.4 | 2.5 | 68.9 | 88.4 | 26.1
● Space charge compensation time measured as function of the pressure (Kr injection)
Beam current measured with the ACCT in the final collimation cone
τ95% : time to reach 95 % of the maximum value
Chopper rise time : ~400 ns
95%
500 µs macro-pulse

## Slide 15: LEBT final tuning
● Collimator aperture : 37 mm
 Iout = 4.5 mA
● Steerers settings inside solenoid 2 :
 IsteererH = 0.5 A
 IsteererV = -2 A
● Isource = 9 mA
● P = 2.4 10-5 mbar (Kr injection)
εYY’ rms. norm.proton = 0.08 π.mm.mrad

## Slide 16: CONCLUSIONS & Future work
● The MYRRHA LEBT is fully commissioned
 Effect of gas on space charge compensation experimentally measured
 Tuned to provide the right beam parameters (Twiss, emittance) at RFQ input
● Analysis of experimental data for SCC studies in progress
 Model development With WARP for a better understanding of the Physical process of SCC in the LEBT
- As studied for example on LINAC4 C. A. Valerio-Lizarraga et al., Phy.Rev. ST Accelerator & beams, 2015
- Assess the effect of Emittance-meter on measurement accuracy
- Phd thesis of Frédéric Gérardin at CEA Saclay
 To anticipate on the future re-tuning & operation
● Next step : LEBT will be moved to Louvain-la-Neuve for RFQ and injector commissioning (2018)
Courtesy of F. Gérardin
Courtesy of A. Bechtold

## Slide 17
Thank you to
Julien ANGOT, Dominique BONDOUX , Maud BAYLAC, Jorik BELMANS , Jean-Luc BIARROTTE , Thierry CABANEL, Mohammed CHALA, Nicolas CHAUVIN, Victor AMOR DURAN, Wouter DE COCK, Jean-Marie DE CONTO, Pierre DE LAMBERTERIE, Rémi FAURE, Dominique FOMBARON, Christian FOUREL, Emmanuel FROIDEFOND, Frédéric GERARDIN, Julien GIRAUD, Miguel DE LA IGLESIA, Calogero GERACI, Yólanda GÓMEZ-MARTÍNEZ, Étienne LABUSSIERE, Jean-Claude MALACOUR , Jan MALEC, Isaías MARTÍN-HOYO, Luis MEDEIROS ROMÃO, Myriam MIGLIORE, Robert MODIC, Luc PERROT, Solenne REY, Sébastien ROUDIER, Roberto SALEMME, Thomas THUILLIER, Didier URIOT, Aljaz VRH, Dirk VANDEPLASSCHE, Olivier ZIMMERMANN
Thank You for your Attention