## Slide 1: RF detector
Interface between coupler and interlock

## Slide 2: Layout/schematic

## Slide 3: Board definition
Two channels have been mounted up to the buffer.
One with the ADL5513
The other one with the LTC 5530
The target is to compare the performances of both then cascade the ADC to choose the correct one for the final board.

## Slide 4: ADL5513
Vout vs Pin
Linear
Constant slope
55dB range
Chart: Pin (dBm)
| 4 | 3 | 2 | 1 | 0 | -1 | -4 | -5 | -10 | -15 | -20 | -25 | -30 | -35 | -40 | -45 | -50 | -55 | -57 | -59 | -60 | -61
 | 3.95 | 3.95 | 3.93 | 3.82 | 3.7 | 3.55 | 3.13 | 3 | 2.31 | 1.6 | 0.94 | 0.32 | -0.48 | -1.18 | -1.85 | -2.49 | -3.12 | -3.63 | -3.79 | -3.91 | -3.92 | -3.92

## Slide 5: LTC 5530
Vout vs Pin
Not linear
30dB dynamic

## Slide 6: Rise time
ADL5513
LTC5530

## Slide 7: Noise
Measured pp voltage in 5us sweepon the scope
ADL5513
LTC5530

## Slide 8: Minute
Main driver for the noise is the detector
The ADC steps are small
The worth case for the interlock level / max level is the fwd output level with Toshiba where we have 1.5MW vs 1.5MW (i.e. 0.13dB)
Actions:
  Rafael: measure the detectors with the ADC
  Chiara ask again to toshiba for an interlock level @ 1.66MW