## Slide 1: RF distribution system
Anders Sunesson RF group leader
Design work done by Rutambhara Yogi
www.europeanspallationsource.se
RF cell review, May 11, 2017

## Slide 2: RF distribution system
Transport RF to cavity:
Waveguides
Circulator (protect amp)
Load (reflected power)
Couplers for measurements
Arc detectors for protection

## Slide 3: RF distribution system
Layout in gallery, stub, tunnel very critical
Coexist with shielding and cables in stubs
Coexist with cooling piping, cable trays, RF equipment in gallery
Coexist with cable trays, cavities, cryo lines, piping in tunnel
Interfaces with RF amplifiers, cavities, interlock, LLRF, cooling systems, controls

## Slide 4: Parts of distribution system
Waveguides/coaxes – standard design
Directional couplers – used by LLRF and interlocks
Flexible section – standard design
Circulator – power handling, stability, losses
Load – as high absorption as possible required, temperature handling (hot cooling water, >50 deg C)
Arc detectors – two basic designs to choose from, depends on environment and timing response

## Slide 5: Parts continued
In the gallery, the stubs, and the tunnel, support systems are required
These must carry load of waveguide, circulators, loads, etc (very heavy), at a height of 4 to 5 m

## Slide 6
Failed in visual inspection
ESS needs several kilometers of waveguide and thousands of elbows
Prototypes for 704 MHz circulators and loads
  Circulators: AFT, FMT and MEGA
  Loads: AFT, Thales and MEGA
Supplied in-kind
ESS Bilbao for NC linac
Huddersfield University for SC linac
H-Elbow
Coax-waveguide
Adapters
S11 > 30 dB
S21 < 0.05 dB
Courtesy of R Yogi
Distribution: Waveguide, coax, circulators and RF loads

## Slide 7: Prototypes circulators / loads
Three circulator prototypes were ordered from AFT, MEGA, and FMT
Delivered 2016
FAT results available
Three load prototypes were ordered from AFT, MEGA, Thales
Delivered 2016
FAT results available
No power tests made yet

## Slide 8: Example FAT result circulator

## Slide 9: Example FAT result load

## Slide 10: Arc detectors
Either AFT or Micro-step design
AFT can be used for cavity coupler arc detectors
AFT faster time response
Micro-step cost-effective
Both systems used extensively in existing accelerators

## Slide 11: RF distribution system delivery
NC linac, In-Kind contribution from ESS Bilbao
  All designs are done
  Layouts ready (still some question marks stubs)
  Circulator/load ready for tender (waits for approval)
  Support structures are being designed

## Slide 12: RF distribution system delivery II
SC linac, in-kind contribution from UK
  All designs ready
  Waveguides ordered
  Couplers, flexible sections ordered
  Circulators/loads awarded
  Arc detectors ongoing
  Support structures ready to tender
  Very tricky to get waveguides into the stubs

## Slide 13: Whole gallery

## Slide 14: Layout NC gallery, top

## Slide 15: NC gallery, side view

## Slide 16: NC layout stubs and tunnel

## Slide 17: RFQ/MEBT/DTL 1-2 stub

## Slide 18: RFQ/MEBT/DTL 1-2 stub

## Slide 19: DTL 3-5 stub

## Slide 20: DTL 3-5 stub

## Slide 21: Spoke gallery layout, top view

## Slide 22: Spoke gallery, side view

## Slide 23: Spoke stub and tunnel

## Slide 24: Spoke stub

## Slide 25: Medium/high beta gallery

## Slide 26: Medium/high beta stub and tunnel

## Slide 27: Medium/high beta stub

## Slide 28: Next Steps RF distribution system
Mockup stub installation to ensure waveguides will go in
Prepare for installation in stubs (Q3/4 2017)
Finalise and tender support structures (HU and ESS Bilbao)
Place tenders circulators/loads 352 (ESS Bilbao)
Tender arc detectors
Tender shutter switches

## Slide 29
Thank you