 EPICS integration & IOC
Hinko Kocevar
Software Engineer
www.europeanspallationsource.se
12 June 2017

---
Outline
Status at PDR
Work after PDR
Status at CDR
Work after CDR
[Speaker Notes: Walk through: workflow from acceptances tests to commionning]

---
Crew and tasks
Hardware Hooman Hassanzadegan
Firmware Klemen Erjavec and Dušan Slavinec (Cosylab)
Software Hinko Kocevar
Cabling Hooman Hassanzadegan
Testing / debugging / data evaluation Hooman Hassanzadegan
Coordination made through JIRA issues
Small ICS involvement due to lack of resources

---
Status at PDR
Demo EPICS support and IOC developed by Cosylab in 2014
Demonstrated that chosen hardware is adequate for BCM application
Limited functionality and reduced set of features
Based on obsoleted SIS8300 digitizer board

---
Work after PDR
Work on final BCM EPICS support started 3Q 2016
First task was to develop generic Struck SIS8300 digitizer support
Previously based on NDS
Now based on areaDetector (asynNDArrayDriver C++ class)
Allows control and status reporting of the digitizer and RTM
Delivers 10 channels of digitized analog input data as waveform PVs to clients
Integration with MTCA based EVR and mrfioc2

---
Work after PDR
Once generic SIS8300 support was in place, BCM application development was started
BCM EPICS support derives C++ class of generic SIS8300
Along the way generic support was modularized and improved
Fairly straight forward since BCM is derived from generic
All aspects of control and data transfer were completed in 2 months
Also with CSS OPI

---
Work after PDR
Ten instances of BCM are supported
User controls:
Clock source, trigger source, DSP parameters, alarms, select to monitor desired BCM channels, amount of samples to request, monitoring of BCM core status, setup EVR for trigger generation
Data streams
10 raw digitized data streams, 10 BCM specific data streams, debugging streams
AD plugins utilization (ROI, stats, proc, HDF5, ..)

---
CSS OPI
Top level CSS OPI
General info
Acquisition control
Access to other OPI
RTM selection
BCM instance OPI access
AFE control and monitoring (not seen here)

---
CSS OPI general info
Some generic SIS8300-x digitizer information

---
CSS OPI acquisition control
Selectable data type
Desired number of raw samples
Number of arrays (pulses) collected so far
Force parameter update
FPGA parameters are latched and automatically applied between the pulses

---
CSS OPI analog channels
Channel enable/disable
Software scaling and offset control
No attenuation control

---
CSS OPI acquisition control
Selectable clock source
backplane, RTM, front panel, internal
Clock divider
integer divisor
Trigger repeat
how many pulses to acquire
Trigger source & line
want to use external (EVR),
any available backplane line

---
CSS OPI RTM controls
One type of RTM
At least for BCM
No RTM temperature sensors readout
RTM has them but accessible only over IPMIO

---
CSS OPI BCM control
Ten instances of BCM DSP on single AMC
Instances are pretty much independent, but..
Some controls are common for both instances
Trigger source, clock source, decimation, pulse detection conditions, pulse parameters for alarms,..

---
CSS OPI common BCM
Collection of common BCM controls and statuses
These apply to all BCM instances
Snag: how to name them in control room?

---
CSS OPI BCM DSP configuration
BCM DSP core configuration parameters
Latched after the pulse

---
CSS OPI BCM DSP status
DSP provides core status access status
Refreshed per pulse

---
CSS OPI BCM pulse measurements
BCM DSP measures several pulse parameters including ADC sampling clock frequency
Can raise alarm if not in bounds as configured

---
CSS OPI common BCM alarm controls
BCM DSP can be configured to raise alarm on several conditions
Alarm status is available for monitoring purposes as well as for MPS interfacing

---
CSS OPI common BCM alarm monitors
Individual alarm status is delivered per pulse
Can be cleared on demand by the user

---
CSS OPI BCM probes
With probes we can tap into certain point along the DSP processing chain
Configurable per channel
Up to 64 tap sources available per channel
Used for debugging

---
CSS OPI channel BCM alarm controls
Individual BCM channel can be configured to raise an alarm on several conditions
Alarm status is available for monitoring purposes as well as for MPS interfacing

---
CSS OPI channel BCM alarm monitors
Individual alarm status is delivered per pulse
Can be cleared on demand by the user

---
CSS OPI channel BCM configuration
Droop compensation
Baseline correction
Filtering
Location along the linac

---
CSS OPI channel BCM monitoring
DSP delivers measurements of several parameters per pulse

---
CSS OPI AD plugins
AreaDetector provides plugins
Chain data stream/array
Source can vary, so can destination
Many provided out of the box
Statistics, processing, time series, ROI, saving to file,..
Can develop own plugins
Already done for other systems

---
CSS OPI AD plugin setup
Generic for all AD plugins
Define data source
Monitor array arrival to the plugin
Inspect array properties
Control publishing resulting array to other plugins

---
CSS OPI time series plugin control
Control acquisition
Averaging
Mode
Circular buffer or one shot
Number of points in the buffer
Publishing rate
Access to individual plots

---
CSS OPI time series plot
Plot of BCM8 analog input
Holds 1 pulse

---
Status at CDR
Firmware debugged and tested at Cosylab
Firmware & software debugged and tested also at ESS with EPICS & IOC
Updated EPICS support with latest firmware features
Works with final BCM RTM
Works with SIS8300-L2 AMC (final?)
Several over-the-weekend run tests passed

---
Work after CDR
Handover the EPICS support for SIS8300 and BCM to ICS
Perform integration with multiple SIS8300 AMCs in the same crate
Long term and stability tests (IPMI IOC)
Python scripts for automated tests and reports
Determine minimum set of PVs and amount of data to be delivered (as per BP requirements)

---
Work after CDR
Add recently added FPGA parameters
Solve some outstanding firmware issues (ADC stuck)
Asses performance of the CPU with multiple AMCs / BPMs
Test, test, test..

---
Questions ?