## Slide 1: Event Formation Overview
Tobias Richter
DMSC
European Spallation Source ERIC, Lund, Sweden

## Slide 2
GEM
What is Event Formation?
Convert digitized raw detector signals to pixel ID & timestamp per event in a detector type specific way
technical scope traditionally covered by detector electronics
done in software running on commodity hardware
provides flexibility and extensibility of a software package
shared responsibility of DMSC and Detector Group
performance and correctness challenging task to get right
enables expected ESS count rates and detector capabilities

## Slide 3
BrightnESS is funded by the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 676548
Instrument Readout Architecture
DMSC Hardware
Instrument Hardware
Motion
Chopper
Detector Backend
Detector Backend
Event Formation Unit
Event Formation Unit
EPICS Bridge
Data Aggregation (Kafka)
NeXus File Writing
Live Feedback
MRF
MRF
EPICS
100 GB/s fibre

## Slide 4: Detector Backend = Standard Interface
for event recording
common physical interface and network stack
generic interface and protocol for transmitting diverse information
  detector specific raw signals from the front-end
  global absolute timing
What sits on your end?

## Slide 5
What sits on your end?
--------------
see
Scott Kolya’s presentation
X

## Slide 6
BrightnESS is funded by the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 676548
What does this offer?
readout and streaming of all data
timing in sync with metadata at all rates
clustering and coincidence building
abstraction of logical coordinates and geometry
algorithms and raw data can be inspected “live”
commissioning tools

## Slide 7
Integrating Absolute Timing
choppers (wavelength frame multiplication)
pulse to pulse beam variations
stroboscopic experiments
Crucial at ESS

## Slide 8
wires X
substrate
neutrons
θ
strips Y
10B4C
q = 5 degrees
Event Formation Status
Pre-amp
x32
Wires/
strips/
grids
Shaper
x32
ADC
x32
Digital
cassette
32 wires
32 strips
Cluster: 1 wire 3 strips
Cluster: 1 wire 2 strips
Cluster: 1 wire 1 strip
Cluster: 2 wires 3 strips
No Cluster: 2 wires 0 strip
Graphics courtesy of Francesco Piscitelli

## Slide 9: Gd-GEM Example Traces
Data for X and Y with time and spatial dimension
To be reduced to two numbers
Converter layer (neutron entry point) at the top
APV test data with 25ns time resolution
Final timing will be on a high precision absolute clock
Reduced VMM data (red) simulated

## Slide 10: 2D Detector Image
How do we pick the right locating algorithm and rejection filters?
Success can be quantified.

## Slide 11
Optimization of Processing Parameters

## Slide 12
Optimization of Processing Parameters

## Slide 13
The scientific record of ESS experiments depends on software to function correctly, reliably, in real time
Testing can be automated for generic infrastructure and detector specific processing
BrightnESS is funded by the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 676548
Software Testing

## Slide 14: GEM/VMM DAQ & Monitoring
Installation live in CERN detector lab
Gives faster feedback than legacy DAQ system
Live View
Application Monitoring
Detector and readout
Event formation
Aggregation
Gd-GEM
RD-51 SRS
Added Bonus Outcome!

## Slide 15
Please talk to us.
More importantly talk to the detector group about your readout integration.
Decide with them what the right integration path is. See upcoming presentations.
Then we can identify the best strategy for processing the data and see what support we can provide for commissioning.
Discussions about slow control will follow.
Next Steps
Disclaimer: Different story for cameras.

## Slide 16: Thank you
Data Management Group, DMSC