## Slide 1: Event formation visualization and prototypes
Martin Shetty & Dorothea Pfeiffer
www.europeanspallationsource.se
17-09-28

## Slide 2: Tools to help detector development

## Slide 3: DAQUIRI Features
Live monitoring of EFU
Histograms and visualizes event data
Review detector-specific raw data
Useful in detector development, commissioning & diagnostics
Receives event data from EFUs (via Kafka)
Uses global timing information
Not a data reduction tool

## Slide 4
Generic features

## Slide 5: Grafana

## Slide 6: Features
Data stream format from EFU:
Pulse time
List of Events
Event = (time, pixelid)

## Slide 7: Logical detector geometry
Pixel-id ↔ (x, y, …) mappings

## Slide 8: Projections of volume detectors

## Slide 9: Time of Flight
Plug & play
TOF

## Slide 10: TOF vs. Value

## Slide 11
Detector-specific features

## Slide 12: NMX - Gd-GEM setup
neutron
conversion electron
Start of track

## Slide 13: NMX – Event formation

## Slide 14: NMX – Event formation
Per one detected neutron (efficiency 15%-35% depending on Gd isotope) on the detector
On average 20 strips/channels hit (in x and y)
Per hit: VMM-ID (physical position and coordinate x or y), channel, pulse height and time
Must first cluster the events, then determine x and y entry positions

## Slide 15: NMX – Logical geometry
Readout partitioned into 4 quarters to reduce capacitance and multiplicity of hits
5 VMM3 hybrids in x and y each per module
40 VMM3 in total
One VMM3 covers 5.12 cm of readout
VMM3 chip-ID matched to physical position
Schematic drawing (Old design):
Now 5 VMM3 instead of 6 per coordinate per module
No water cooling

## Slide 16: Raw strip data
Thresholds, voltages, dead strips, gain settings, efficiency

## Slide 17: Pulse height spectrum

## Slide 18: Raw clusters
Cluster data per dimension (x,y) in time and space
Per cluster: physical position in x or y, time
Second clustering step matches x and y
Per cluster: (x,y), time

## Slide 19: Putting it all together at CERN

## Slide 20: DAQUIRI - Current features
detector images
projections of 3d voxel detectors
instantaneous and cumulative histograms
time-of-flight spectra
rate vs. time
coordinate vs. time
custom values received by or generated in EFU:
  spectra of deposited charge
  raw strip & wire data
  Clusters
  ...
  diagnostics only, low count rates

## Slide 21: Summary
Detector development made fun
Commissioning made easy
Diagnostics made meaningful
Confirmation of EFU processing steps:
What do you want?
If you want feature-complete data reduction, use Mantid