## Slide 1
Readout Electronics Back End
IKON13
28th September 2017
Steven Alcock (DG)

## Slide 2: Simplified Readout Electronics Architecture
Steven Alcock, Detector Group, 6th September 2017
FPGA Master 1
FPGA Master 2
Switch
DMSC Server 1
DMSC Server 2
Diagnostic Server
Front End
Front End
Front End
Front End

## Slide 3: 100 G Detector Readout Demonstrator
Steven Alcock, Detector Group, 6th September 2017
Provides the DMSC with high-rate packets in a format representative of the final system.
Allows data packing format to be agreed.
Proves key interfaces.

## Slide 4: Key Features
Four packet engines are independently configurable at run-time.
Aggregate output data rate is configurable at run-time.
Aggregate number of packets is configurable at run-time.
Mellanox Switch can output data as 10/25/40/56/100 G. This means, for example, the full 100 G input could be split across 10 x 10 G outputs.
Steven Alcock, Detector Group, 6th September 2017

## Slide 5: FPGA Architecture
Steven Alcock, Detector Group, 6th September 2017
Packet Config Parameters
RAM Write FSM
RAM Read FSM
512-bit Packet RAM
Packet Config Parameters
RAM Write FSM
RAM Read FSM
512-bit Packet RAM
Packet Config Parameters
RAM Write FSM
RAM Read FSM
512-bit Packet RAM
Packet Config Parameters
Packet Mux
CMAC
RAM Write FSM
RAM Read FSM
512-bit Packet RAM
Data Sink
Config Source

## Slide 6: Variable Packet Rate Design
Tx
Tx
Steven Alcock, Detector Group, 6th September 2017
Ti
Data rate is ratio of time spent transmitting at 100 G (Tx) to time spend idle (Ti).
Tx = {Packet Length in bits} / {100 G Transmission Rate} = L/100e9
Ti = {Number of Idle Clock Cycles} / {Processing Clock Speed} = G/322.265625e6
Therefore the new time taken to transmit one packet becomes {Tx + Ti}
The new rate becomes R = {L/(Tx + Ti)} = {L/(L/100e9 + G/322.265625e6)}
Rearranging gives G = {322.265625*(L/Re5)*(100-R)} where G is in Gbps
Ti

## Slide 7: Packing Format Example 1
Steven Alcock, Detector Group, 6th September 2017
Data
Header
Readout
Header
UDP
Header
IP
Header
Ethernet Header
Data
Payload

## Slide 8: Packing Format Example 2
Steven Alcock, Detector Group, 6th September 2017
Data
Header
Readout
Header
UDP
Header
IP
Header
Ethernet Header
Data
Payload

## Slide 9: Packing Format Example 3
Steven Alcock, Detector Group, 6th September 2017
Data
Header 0
Readout
Header
UDP
Header
IP
Header
Ethernet Header
Data
Payload 0
Data
Header 1
Data
Payload 1
Data
Header 2
Data
Payload 2
Data
Header 3
Data
Payload 3

## Slide 10: To Do List
Support the DMSC!
Physical layer link integrity stress testing with representative cable lengths.
Steven Alcock, Detector Group, 6th September 2017