## Slide 1
SKADI
Progress Update
26. September 2017 | S. Jaksch

## Slide 2
Current Instrument overview
Dogleg Neutron Extraction Update
Sample Area
Scheduling
SoNDe Detector
Overview

## Slide 3
Choppers
Sample Area
Detectortube
SKADI layout
Polarizer, Spin Flipper
Neutron
Extraction
Collimation
Bunker
Heavy shutter
Shutter inside bunker (Gabor‘s design)
All choppers outside bunker

## Slide 4
Sample Area
Plenty of available space
Custom sample environments
Fast change of sample environment
Crane/forklift accessibility
Data
Gas
Electronics
Standardized Interfaces

## Slide 5
Media readily accessible below false floor
Door minimum 2,0x2,0 m2
Door and roof panel motorized
Door also allows access to detector tube
Hollow floor on wheels in order to be readily removable
hollow floor removable
Sample area

## Slide 6
Sample Area

## Slide 7
Goals:
High flux of usable neutrons at sample position
Low background
Go easy on budget
Requirements:
Twice out of line of sight within the bunker
Metal substrates in bunker
Manageable m-values (m <= 4)
Change request for design update submitted.
Dogleg Neutron Extraction

## Slide 8
Properties:
m=4 everywhere
Al substrate
Only straight guides
Inclinations
  -0.9°
  -1.97°
  -0.9
Offset 235 mm at bunker wall
Dogleg Neutron Extraction

## Slide 9
Dogleg Neutron Extraction
109
108
107
106
105
104
intensity / cm2
0
5
10
15
20
25
wavelength / Å
1.0
0.8
0.6
0.4
0.2
0.0
0
5
10
15
20
25
wavelength / Å
Flux improvement over all wavelengths
Still reasonable suppression of low wavelengths
No distortion of phase space
Approximately 60 % transmission plateau
In 3-8 Å band gain factor 4.4

## Slide 10
Option 1: TG5 01/2023
Option 2: TG5 10/2021
Ongoing Discussions
Urgent partial TG3 for single components end 2017/ early 2018 necessary
Unified approach for all FZJ / LLB instruments
Scheduling

## Slide 11
Feasibility tests successfully completed
Model now commercially available
See talk Codin Gheorghe, Thursday 14:00
SoNDe Detector

## Slide 12: Thanks to ...
Sylvain Désert
Jacques Jestin
Henrich Frielinghaus
Romuald Hanslik, FZJ
Achim Gussen, FZJ
Herbert Feilbach
LLB+ JCNS Technical Groups
... and you, for your attention!