## Slide 1: Neutron Beam Extraction System Design status for IKON-13
Jarich Koning
www.europeanspallationsource.se
26th September 2017

## Slide 2: NBEX Light Shutter System
You are encouraged to interact – sheets come from interim review June 2017

## Slide 3: NBEX locations and volume claims
Permanent (red)
Transport (yellow)
  IET
  LSC
Beamline
NBEX nominal volume
Basement, LVL91, Utility rooms
R5.5
R2.7
R5.3
R6
R8
IET transport
Vertical handling test stand
Horizontal handling test stand
ACF docking
LSC transport

## Slide 4: Light shutter function
Open  Closed
Optics switch function: BEER 75mm 2x, ODIN 150mm 2x, T-REX 2x100mm 3x, MAGIC 75mm 2x
No actuator at plugged ports

## Slide 5: Light Shutter System
GBS on top of BBG
  “Light shutter” comprises GBS+BBG
  BBG internals are up to instrument but not repairable
Ballscrew-style vertical actuator
  Brake ‘normally open’  power loss: GBS closes by gravity descent
  Actuator positions BBG then engages brake to hold  no micro-motion possible
@maintenance, GBS will rest at beam port on hooks
Bunker-floor-to-Monolith gap shielded with FFB
400mm surplus at LSS top
LSS Frame mounted to port-block-flange
Bridge Beam Guide
NBPI
Shock absorbers
NBW
Gamma Beam Shutter
Vertical actuator
GBS hooks
Floor Filler Block
Media lines
Water valve panel
Switches beam
Light Shutter Frame
Vertical rails
Port block (excerpt)

## Slide 6: Light Shutter single port configuration
Default configuration contains
  Floor Filler Block
  Bridge Beam Guide
  Gamma Beam Shutter
  LSS frame
  Neutron Beam Port Insert
  Neutron Beam Window
  Media lines and panel
Variants
  BBG specific to instrument, can be optics switch
  FFB variants per type of port and BBG height
  Switch profile length / switch location

## Slide 7: Neutron Beam Extraction System
Model reference: ESS-0065135
Notes: Extra slides follow