## Slide 1: IM-Optics Supplier forum NBOA Concept Design report
ESS
I.Sutton

## Slide 2: What is this all about
Context
Instrument requirements
Generic design
Architecture
Materials
Alignment
Cooling
Coatings

## Slide 3: NBOA Generic One for all … all for one !
Objective
Develop high performance, robust, cost effective design as the template for all inserts.
Conduct its integration, validation and certification
From the template develop custom designs for all instruments inserts as the basis for procurement

## Slide 4
NSS Bunker (Z.Lazic)
NSS Instruments (G. Lazlo)
NSS Neutron optics (P. Bently)
NSS Hall / Logistics
(G. Lazlo / I.Sutton)
Target NBEX Systems (S.Gh)
Target Monolith Systems (S. Ghatnekar)
CF D02
(L. Arthursson)
NBOA organisational context – a complex interface

## Slide 5: “NBOA” – all instruments
IN-MONOLITH (NBOA)
Line of sight YES
Length 3.5m
Substrate Metallic
Atmosphere Vac / He
QC regime Nuclear
R2 R5.5 R6.0 R11.5 (24.5) R15 (28)
IN-MONOLITH (BPSO)
Line of sight YES
Length 0.5m
Substrate Metallic
Atmosphere Vac / He
QC regime Safety
5
NOT this window
‘Neutron beam window’

## Slide 6: Monolith Vessel & Neutron beam ports
Moderator
Neutron beam inserts (gray)
Light shutters (green)

## Slide 7: Neutron Beam Extraction System
Model reference: ESS-0065135
Notes: Extra slides follow

## Slide 8: NBEX
Key stats
Length 3.5m
Mass 4700kg
Material: stainless steel 316L
Principal functions
Bulk shielding
For NBOA
Physical support
Cooling
Alignment w.r.t Moderator
Environment
NBPI A water cooled shielding block on wheels

## Slide 9: Neutron beam optical assembly (NBOA)
R2 R5.5
Neutron Beam Extraction (NBEX)
Resp: Target Division
Neutron Beam Port Insert (NBPI)
Resp: Target division
Role: Shielding & alignment
Neutron Beam optical assembly (NBOA) Resp: NSS / Instrument
Role : Beam extraction

## Slide 10: Requirement collection
3 Pronged approach
Information diffusion
  Full Project meetings IKON
  Monthly news letter
Discussion (grouped)
  Monthly skype meeting
Discussion (individual)
  Confluence
  One on one meetings
Avoid email !

## Slide 11: Iterative engineering process
Description of Surfaces
Architecture
Embodiment
Integration
Surfaces
coatings
Sectioned surfaces
Features
Realistic volumes
Full Features
Integrated volumes
validation
Instrument team
Experts
Internal stakeholders
Instrument team
Experts
Suppliers
Instrument team

## Slide 12: Requirement maturity

## Slide 13: Understanding Commonalities
NBOA
Bi-spectral
Bender
Elliptical
Multiple
DREAM
HEIMDAL
MAGIC
ODIN
LOKI
SKADI
BEER
BIFROST
DREAM
ESTIA
FRIEA
HEIMDAL
ODIN
T-REX
FREIA
HEIMDAL

## Slide 14: Features Bi-spectral extraction (switch)
Engineering issues
Wide opening
High heat load
‘Switch’
Multichannel design
Issues resolved* with move of Switch to outside of monolith.
*One instrument remaining

## Slide 15: Features Multi channel bender
FREIA* R 130 000mm
LOKI* R 61 250mm
SKADI* R 84 000mm
Engineering issues
Multichannel design (3 & 5 channels)
Heat transport from wafers*
Alignment precision requirements.
Integration issues due to high curvature geometry
Issues resolved* with He atmosphere.

## Slide 16: Features Elliptical surfaces
BEER (Top & Bottom)
BIFROST (ALL)
DREAM (Top & Bottom)
ESTIA (Top, Bottom & Right)
FREIA (Top & Bottom)
HEIMDAL-THERMAL (ALL)
ODIN (ALL)
T-REX (Top & Bottom)
Engineering issues
Integration issues due to high curvature geometry
Manufacture due to high curvature geometry*
Issues resolved* with reduced substrate thickness.

## Slide 17: Features special cases
ESTIA
  Collimator section
  Uncoated left side
HEIMDAL
  Dual guide
MAGIC
  No super coated mirrors
ODIN
  Right side open first 300 mm.

## Slide 18: Design philosophy
“True performance can only be judged over the long term ….”
Critical systems shall be;
Robust
Performant
Cost effective
…..in a word simple !

## Slide 19: Recommendations & Decisions
Validation of designs key points
Architecture
Cooling
Materials
Coatings
Alignment

## Slide 20: Architecture Overview
Construction in 3 sections
Small gaps between sections enable independent alignment and compensate for thermal expansion
Justification
Ease of manufacture
Ease in installation
Ease of alignment
Cooling

## Slide 21: Architecture Schematic
ALIGNMENT & RETENTION FEATURES
ALIGNMENT
ALIGNMENT
ALIGNMENT
ALIGNMENT
ALIGNMENT
ALIGNMENT
ALIGNMENT
ALIGNMENT
ALIGNMENT
ALIGNMENT
ALIGNMENT
ALIGNMENT
SECTION 01
SECTION 02
SECTION 03
N

## Slide 22: Architecture Chicanes
2mm (nominal) gap between NBOA and NBEX pocket
2 chicanes along the streaming path
  Step >13mm
Shielding steps are >500mm long & separated by at least 1000mm.
Jackets shall be gap less with respect to substrate.
.
A
B
C

## Slide 23: Construction Materials
Optical substrates
Copper (Pure O2 free)
Benefits
Radiation resistance
Shielding properties
Thermal conduction
Compatibility with coatings
.

## Slide 24: Activation
NBOA = 100 - 300kg of copper
Copper substrates will become activated
With respect to human safety
In this application the activation of the coppers is considered a significant issue because
After 15d Copper 1/1000 activity of Steel
NBOA is shielded within Steel
Removal of NBEX is an RH activity
With respect to Waste disposal
Considered integrally with NBEX
Compatibility of Design & Materials with waste handling stream confirmed

## Slide 25: NBOA Replacement
Potentially 10 -16 additional beam ports will be activation within the first 10 years of operation
Initial suite
Late arrivals ?
Instruments 17-22
Instruments 23 - 28
End of life Replacement

## Slide 26: Alignment
Requirements
Movement +/- 1mm
Resolution 0.01mm
Long term Stability
Key features
Positioning alone ‘long side’
Solid screws opposed by strip springs
Vertical jacks
Support on balls
Retaining pins
Spring side
Solid side

## Slide 27: Retention
Constraints from hazard analysis
Retain components during H3 seismic event
Constraints from Decommissioning
.. All components shall remain within NBEX during transport to disposal facility ….
    Solution: windows on NBPI
….sectioned components shall be retained during handling ….
    Solution: Retaining pins on all guides sections
Design requirement
resist acceleration 2g in all planes
sectioned component

## Slide 28: Alignment details
Side
Fine pitch screw
Lock screw
Spherical ball contact
Screw in pocket acts as retaining pin
Below
Screw + ramp
Ball + cup contact

## Slide 29: Thermal management - Context
Water cooled shielding
Source
‘Air cooled’ shielding
Instruments
Target monolith
R1.0
R2.5
R5.5
R2.0

## Slide 30: Thermal management - heat load
Heat load due to gamma heating
NBEX up to from 150 - 350w
beam port dependent
Initial study NBEX operates within vacuum
Minimal conduction path point contact
Heat dissipation by irradiation to neighboring blocks (cooled – uncooled)
Without cooling temperature peak ~125c
To maintain a stable and acceptable operating temperature NBPI is water cooled to 35 - 40c
Source: Alan Takibayev 4-2017
Source: Anders Olsson 5-2017

## Slide 31: Thermal management - heat load (NBOA)
Heat load due to gamma heating
NBOA 50 - 100w (beam port dependent)
  (30% more in copper than in steel, less in silicon )
Deposition profile is geometry dependent
  Straight
  Curved
  Converging
Initial studies with a cooled NBPI
  Straight geometry
  In vacuum
  Conduction via point contact
  Heat dissipation by irradiation
Without cooling temperature peak ~100c
Recommended operating temperature is 60c
Source: Anders Olsson 5-2017
Source: Anders Olsson 5-2017

## Slide 32: Thermal management - heat load (NBOA)
Need to improve heat conduction
within NBOA to reduce ‘hot spots’
Need to improve heat dissipation from NBOA > NBPI
Following recommendation, decision taken to close NBPI volume and adopt Helium atmosphere.
Study with helium, worst case geometry, worst case heat load
Peak temperature ~55c
Source: Anders Olsson 5-2017

## Slide 33: Thermal management - atmosphere
Volume : 10 - 60ltr
Pressure : 200 - 500mbar (TBD)
Operating temperature 40c +/- 5
Media : Pure Helium
Flow : None
The volume is expected to remain closed during operation and topped up ‘annually’
The pressure may change during operation between the limits indicated

## Slide 34: Thermal management - sealing
Seals
Front window – NBPI body
  Knife edge
Rear window - NBPI body
  Knife edge
NBPI Lid - NBPI Body
  Energized crushable metallic
Ports – NBPI body (~20)
  Energized metallic
Alternative sealing type under study
Crushable wire
Lip weld
1
2
3
4

## Slide 35: Coatings
ESS Decision
Cap coatings of in-monolith optics in a general case to < M = 4.0
Use of coatings above this value is exceptional with the express consent of ESS
Prohibited in-monolith

## Slide 36: Coatings Cap at 4 ? Who is affected ?
Instrument | Top | Bottom | Left | Right
BEER | 4 | 4 | 2.5 | 2.5
BIFROST | 3.5 | 3.5 | 3.5 | 3.5
C-SPEC | 3 | 3 | 4 | 3.5
DREAM | 4 | 4 | ? | 3.5
ESTIA | 4 | 4 | - | 4
FREIA | 1 | 1 | 4.4 | 2.5
HEIMDAL- THERMAL | ? | ? | ? | ?
HEIMDAL- COLD | ? | ? | ? | ?
LOKI | 3 | 3 | 3 | 3
MAGIC | - | - | - | -
MIRACLES | 3 | 3 | 3 | 3
NMX | 2 | 2 | 2 | 2
ODIN | 4 | 4 | 5 | 5
SKADI | 3 | 3 | 3 | 3
T-REX | 5 | 5 | 1.5 | 1.5
VESPA | 6 | 6 | 6 | 6
4 instruments are effected
Study of changes is underway

## Slide 37: Outstanding technical issues
No major technical issues outstanding
Minor issues
NBOA
Coating changes – 3 instruments
NBOA – NBEX
Beam window thickness optimisation
Operating temperature
  Requirement to be confirmed
  Technical solution requires

## Slide 38: Thanks for joining us Questions are welcome !
NBOA – NBEX Team

## Slide 39: Activation of Steel Components
decay time: 2000 hours
Max dose rate: 50 – 80 mSv/h
T1/2 = 5.27 a
Distance to source: 1.5 - 2.1 m