## Slide 1: Neutron beam optics assembly Engineering implementation
E.Nilsson
Neutron Instrument Technologies
On behalf of NBOA – (NBEX) engineering team
www.europeanspallationsource.se
14 June, 2017

## Slide 2: NBOA Generic One for all … all for one !
Objective
Develop high performance, robust, cost effective design as the template for all inserts.
Conduct its integration, validation and certification
From the template develop custom designs for all instruments inserts as the basis for procurement

## Slide 3: Design philosophy
“True performance can only be judged over the long term ….”
Critical systems shall be;
Robust
Performant
Cost effective
…..in a word simple !

## Slide 4: Diversity
NBOA
Tall
Wide
Small
Unique
HEIMDAL
No-optics
MAGIC
Intermediate
BEER
BIFROST
C-SPEC
DREAM
ESTIA
FREIA
LOKI
SKADI
MIRACLES
NMX
ODIN
T-REX
VESPA
Tall = Height >2x width
Wide = Width >2x height
Small = Smaller than 30x30
Intermediate = Other geometries

## Slide 5: Diversity
NBOA
Bi-spectral
Bender
Elliptical
Multiple
DREAM
HEIMDAL
MAGIC
ODIN
LOKI
SKADI
BEER
BIFROST
DREAM
ESTIA
FRIEA
HEIMDAL
ODIN
T-REX
FREIA
HEIMDAL

## Slide 6: Beam Profiles
Instrument | IN (H*W) | OUT (H*W)
BEER | 35x85 | 60x30
BIFROST | 34,6x68,7 | 48,8x51
C-SPEC | 55x70 | 55x70
DREAM | 23,9x44/23,9x32,3 | 37,6x29,5
ESTIA | 134x67 | 191,9x96
FREIA | 120x40 | 242x40
HEIMDAL- THERMAL |  | 
HEIMDAL- COLD | 20x20 | 20x20
LOKI | 25x30 | 25x30
MAGIC | 30x124 | 30x42
MIRACLES | 49x60,5 | 71x46,6
NMX | 28x30 | 45x30
ODIN | 33x43,8 | 52,6x37
SKADI | 30x30 | 30x30
T-REX | 30x90 | 44,4x63,8
VESPA | 35x35 | 40x40

## Slide 7: TALL Issues
Parameters
Height up to 250mm tall (+substrate)
Weight up to 200kg
Specific challenges related to this group
NBPI Integration,
  Vertical space (clashes)
  Complex shapes
Alignment
  Vertical axis
  Highest weight on alignment features
Largest sets of windows
Highest heat load on optics
Outstanding issues
Increased vertical view of moderator ?
NBOA
Tall
ESTIA
FREIA

## Slide 8: TALL Solutions
Integration of alignment features
Straight elliptical guide
NBPI Integration
  Several complex geometries, such as true elliptical curves, to be machined in NBPI.
  Space required for Window frame and lid reduced to accommodate guides
Alignment
  Heavy section drives design of features, both side and vertical alignment
  Compensated by double springs

## Slide 9: TALL Solutions
Windows and seals
  Largest set of windows (250x150mm).
  Size of gasket driven by largest size.
Heat load
  Standard solution sufficient.
  Calculated based on Tall use case
Heat map on FREIA NBOA

## Slide 10: FREIA
Multichannel bender (R130m)
Elliptical top and bottom section
M=1-4.4

## Slide 11: ESTIA
Initial 300mm collimator section
Elliptical right, tope and bottom sides
Uncoated left side
M=4

## Slide 12: WIDE Issues
Parameters
Width up to 100mm wide (+substrate)
Specific challenges related to this group
NBPI Integration,
  Horizontal space (clashes)
  Complex shapes (ellipses, transforming, etc.)
Alignment, width in NBPI for side alignment
Outstanding issues
Increased vertical view of moderator?
NBOA
WIDE
BEER
DREAM
T-REX

## Slide 13: WIDE Solutions
Straight elliptical guide
Window position
NBPI Integration
  Moved jacket section to second location to reduce clashes.
  Several complex geometries, such as true elliptical curves, to be machined in NBPI.
Alignment
  Alignment features can be placed on either side of NBOA.
  Wave spring solution reduces required space.

## Slide 14: BEER
Bispectral
Tapered left and right
Elliptical top and bottom
M=2.5-4

## Slide 15: DREAM
Bispectral
Double guide section
Tapered left and right
Elliptical top and bottom
M=2.5-4

## Slide 16: T-REX
Tapered left and right
Elliptical top and bottom
M=1.5-5

## Slide 17: SMALL Issues
Parameters
Height up to 30mm tall (+substrate)
Specific challenges related to this group
NBPI Integration,
  Deep and narrow cuts
Alignment
  Limited space for alignment features
Outstanding issues
Increased vertical view of moderator?
NBOA
SMALL
LOKI
NMX
SKADI

## Slide 18: SMALL Solutions
Vertical bend
Deep pocket
Integration of alignment features
NBPI Integration
  Deep cuts and ridge on NBPI due to vertical benders, solved in detail design of NBPI.
Alignment
  Optimized size alignment features.
  Potentially reduced dimension of alignment features.

## Slide 19: LOKI
Multichannel bender (R61,25m)
Constant cross-section
M=3

## Slide 20: NMX
Constant cross-section
M=2

## Slide 21: SKADI
Multichannel bender (R84m)
Constant cross-section
M=3

## Slide 22: INTERMEDIATE Issues
Parameters
Height up to 70mm tall (+substrate)
Width up to 70mm wide (+substrate)
Specific challenges related to this group
NBPI Integration,
  Complex shapes
Outstanding issues
Increased vertical view of moderator?
NBOA
INTERMEDIATE
BIFROST
C-SPEC
MIRACLES
ODIN
VESPA

## Slide 23: INTERMEDIATE Solutions
Issues covered by the other variants

## Slide 24: BIFROST
All sides elliptical
M=2,5-3.5

## Slide 25: C-SPEC
Constant cross-section
M=3-4

## Slide 26: MIRACLES
All sides tapered
M=4

## Slide 27: ODIN
Bispectral with blades
Initial 300mm open on right side
All sides elliptical
M=2,5-5

## Slide 28: VESPA
All sides tapered
M=6

## Slide 29: UNCOATED Issues
Parameters
Width up to 125mm wide (+substrate)
Specific challenges related to this group
No optical requirements
  More available space for geometry
Excluded from NBOA preliminary design
Outstanding issues
Need a conceptual design of NBEX without substrates -i.e. an empty cavity!
  Applicable for test beamline as well
NBOA
UNCOATED
MAGIC

## Slide 30: MAGIC
Bispectral
Tapered left and right
Constant height
No coated mirrors

## Slide 31: UNIQUE
Parameters
Width up to 125mm wide (+substrate)
Specific challenges related to this group
Dual guide
Specific integration and support requirements
Alignment issues
Excluded from NBOA preliminary design
Outstanding issues
NBOA standard preliminary design not suitable for HEIMDAL
Individual integration solution for HEIMDAL needed
NBOA
UNIQUE
HEIMDAL

## Slide 32: Dual Solutions
Potential jacket solution
Complex integration

## Slide 33: Outstanding issues
Clash checks and coating updates
NMX – No comments on clash issues
SKADI – No comments on clash issues
ODIN – No comments on clash or coating issues
VESPA – Unresolved coating issue
T-REX – Unresolved coating issue
Geometry updates
C-SPEC requested NBOA geometry update (changed radius)
FREIA geometry issues (Solved week 25)
Engineering issues
Conceptual design for MAGIC NBOA
Conceptual design for Heimdal NOBA