## Slide 1: Neutron Scattering Science and the European Spallation Source
Shane Kennedy
Deputy Director for Science
Neutron Scattering Systems Project Leader
ESS Engineering Lecture: 14th September 2017

## Slide 2
Evolution of Neutron Sources
2020
ESS
RA-10
RMB
FRM-II
OPAL
HANARO
SNS
CARR
CSNS
MRR
HIFAR
2030
Peak Neutron Flux (n/cm2/sec)
Year

## Slide 3: Nobel Prize for discoveries with neutron irradiation

## Slide 4: Nobel Prize for discoveries with neutron irradiation
The first nuclear pile (Argonne, 1942)

## Slide 5: Nobel Prize for discoveries with neutron irradiation
Chicago Pile #1:
Alternating layers of Uranium/graphite (U/C) and pure graphite
Total = 57 layers of U/C
Graphite:
brick size: 4¼” x 4¼” x 16½”
Total graphite = 385 tons
Uranium:
40 tons U2O3
+ 6 tons U-metal
Total Uranium = 46 tons
Control Rods:
Cadmium & Boron

## Slide 6: Nobel Prize for Neutron Scattering Science

## Slide 7: Nobel Prize for Neutron Scattering Science

## Slide 8: Nobel Prize for Neutron Scattering Science
Cliff Shull and Ernie Wollan doing neutron diffraction in ~1946

## Slide 9: Neutron production (fission, spallation), thermalization and research reactors
The nuclear fission process
The spallation process

## Slide 10
Neutron production by spallation
(The Spallation Neutron Source, USA)
5th AONSA Neutron School,
Peking Uni., China, 24 October 2012
Proton pulses
SNS (ORNL, USA)
The Liquid Mercury Target
Notes: See web page atomicarchive.com for many schematics on fission; including explosive and implosive

## Slide 11: OPAL’s core and multipurpose reflector vessel
Light Water
D2 Cold
Neutron Source
Provision for Hot NS or 2nd Cold NS
Neutron beams, radioisotopes & NTD Silicon
4x4 grid, plate type., 60 cm x 32 cm2; Power = 20 MWth, f0=4x1014 n/cm2/s
OPAL’s Compact LEU Core:
Zircaloy (D2O) reflector tank:
operational design life: 40 yrs

## Slide 12: OPAL’s core and multipurpose reflector vessel
Light Water
D2 Cold
Neutron Source
Provision for Hot NS or 2nd Cold NS
Neutron beams, radioisotopes & NTD Silicon
4x4 grid, plate type., 60 cm x 32 cm2; Power = 20 MWth, f0=4x1014 n/cm2/s
OPAL’s Compact LEU Core:
Zircaloy (D2O) reflector tank:
operational design life: 40 yrs

## Slide 13: OPAL’s core and multipurpose reflector vessel
Light Water
4x4 grid, plate type., 60 cm x 32 cm2; Power = 20 MWth, f0=4x1014 n/cm2/s
OPAL’s Compact LEU Core:

## Slide 14: Ancient History; the first cold neutrons
First cold neutrons; Argonne Pile
Anderson, Fermi & Marshall (1946)
Orphee (LLB) H2(liq)
CNS2 (1990) annular
Bepo (Harwell)
1957 H2(liq) –flow through system (~ 1-2 day capacity)
5th AONSA Neutron School,
Peking Uni., China, 24 October 2012

## Slide 15: OPAL’s cold neutron source
CG4 beam tube
CG1-3 beam tube
D2O moderator
D2 moderator
Reactor Core
50 cm
Liquid Deuterium moderator chamber
OPALs D2 moderator
Volume: 20 litres
Temperature: ~ 23 K
Heat load: < 4.5 kW
TM-B: ~ 45 K & 210 K
5th AONSA Neutron School,
Peking Uni., China, 24 October 2012

## Slide 16: Neutron beam transport: OPAL’s neutron reflecting guides

## Slide 17: OPAL’s neutron guide system
5th AONSA Neutron School,
Peking Uni., China, 24 October 2012

## Slide 18: Competitive advantages of neutron beam science
Comparison of neutron & X-ray scattering lengths
Fe
Gd
Effective magnetic scattering lengths
light elements
  H, Li, C, N, O…
magnetism
  long and short range
atomic motion
  vibration, libration, diffusion
in-situ studies
  T,H,P,V, gas…

## Slide 19: Seven decades of neutron scattering
Ref: European Spallation Source (ESS) report (ENSA, 1997)
.. and Imaging
radiography & tomography

## Slide 20: Capabilities for structural characterization at OPAL
Q (Å-1)
100
101
10-1
10-2
10-3
10-4
10-5
ECHIDNA & WOMBAT (Powder)
KOWARI (Strain)
KOALA (Crystal)
Length scale
10 mm
1 mm
100 nm
10 nm
1 nm
100 pm
10 pm
100 mm
QUOKKA (P-SANS)
3 settings
focusing lens
KOOKABURRA (U-SANS)
high-res
BILBY (P-SANS)
single setting
slit mode
DINGO (Imaging)
PLATYPUS (Reflectometer)
Polarised beam and polarization analysis options

## Slide 21: Spectroscopy: First ESS instruments
21
Q-Energy range covered by ESS spectrometers.
The instruments in italics have not yet been approved for construction

## Slide 22
LIB setup on the WOMBAT diffractometer at the OPAL reactor for in-situ study
In-situ/in-operando neutron diffraction;
Lithium ion battery charge-discharge cycles
N Sharma et. al., J S.S. Electrochem 16, 1849 (2012)
Notes: The figure represents a collection of in-situ neutron diffraction patterns that are a follow up to our 1st experiment with commercial Li-ion batteries. This time we have optimised sample geometry (cylindrical battery (pictured) as opposed to a prism) which has allowed us to probe aspects such as different cycling rates (pictured) and over-charging.
A reflection characteristic of the anode and cathode are identified.

## Slide 23
LIB setup on the WOMBAT diffractometer at the OPAL reactor for in-situ study
In-situ/in-operando neutron diffraction;
Lithium ion battery charge-discharge cycles
2 Amp charge & discharge
1.25 A charge 0.5 A discharge
Time
2q (degrees)
30
40
50
60
Anode peak
Cathode peak
Discharging
Charging
N Sharma et. al., J S.S. Electrochem 16, 1849 (2012)
Notes: The figure represents a collection of in-situ neutron diffraction patterns that are a follow up to our 1st experiment with commercial Li-ion batteries. This time we have optimised sample geometry (cylindrical battery (pictured) as opposed to a prism) which has allowed us to probe aspects such as different cycling rates (pictured) and over-charging.
A reflection characteristic of the anode and cathode are identified.

## Slide 24: Magnetic neutron diffraction
ND measurements performed at the OPAL research reactor
JL Wang et. al., PRB 87, 1104401 (2013)
PrMn2Ge2
Notes: Example of NPD and the intidactions of magnetic order in the PrMn2Ge2-xSix series

## Slide 25
Residual Stresses in Rail Squat Formation
(University of Queensland & Railcorp Australia)
Rails mounted on Kowari
Example from OPAL

## Slide 26: Neutron Tomography
Dingo Neutron Imaging Station
Images courtesy of Ulf Garbe, Bragg Institute (L/D = 1000)
Providing 3 dimensional images of internal structure
Example; a mechanical alarm clock
Example from OPAL
Radiograph

## Slide 27
Example; oil flow in an automobile engine.
Image courtesy of
Burkhardt Schillinger,
Technical University of Munich
Neutron Radiography
Providing real time images of internal structure & processes
Example from FRM-II

## Slide 28: Small Angle Neutron Scattering Spectrometers
QUOKKA: High resolution (40 m) pinhole SANS with beam focussing and Polarization Analysis (PA) option
PA mode
3He analyser with in-situ refilling
qmin ≈ 4 x 10-4 A-1 ; qmax ≈ 7 x 10-1 Å-1
focussing mode

## Slide 29: Small angle neutron scattering of magnetite nanoparticles
(a) Experimental setup of polarized SANS
(b) 2-D SANS images (at 1.2 T, 200 K)
Reference: K. L. Krycka et. al., PRL104 (2010)207203
(c) Composite model:
ferrimagnetic core  ~ 7.4 nm with 90°canted magnetic shell ~ 0.8-1.2 nm thick
Experiments at NCNR, NIST

## Slide 30: Small Angle Scattering for nanoscale structures; polymers, pores, inclusions, protein conformation, hierarchical materials…
Hierarchical polymer blend
(LMW-HMW-Polyethylene)
SANS and SAXS from (d-LMW-h-HMW) stretched polymer, elongation factor ~6
T Kanaya et. al., Macromol 40, 3650 (2007)
Experiments at JRR3, KENS and Spring8

## Slide 31
Proton diffusion in Alkali Metal Hydrogen Sulfates - Inelastic neutron scattering
Crystal structure of alkali metal hydrogen sulfates has chains of XO4 tetrahedra, linked by hydrogen bonds, O-H..O.
Above RT, phase has dynamically disordered tetrahedra, and very high protonic conductivity.
INS of RbHSO4 sulfate showing large amplitude proton motions at low Temp
T Yildirim et. al., SSI 145, 429 (2001)
Hydrogen motion most likely responsible for this excitation
Experiments at NCNR, NIST

## Slide 32
Proton diffusion in Alkali Metal Hydrogen Sulfates - Quasi-elastic neutron scattering (CsH(SO4)0.76(SeO4)0.24)
Images courtesy of Dan Neuman (NIST)
Experiments at NCNR, NIST

## Slide 33: Major Neutron Beam Facilities Worldwide
Underlined names show facilities in planning or construction phase
●
●
●
●
●
●
●
●
●
●
●
●
●
●
●
●
●
OPAL (AUS)
JRR-3 (JPN)
HANARO (KOR)
MRR (CHN)
CARR (CHN)
CSNS (CHN)
RSG-GAS (INA)
CIRUS (IND)
NRU (CAN)
IPNS (US)
NBSR (US)
HFIR (US)
SNS (US)
LANL (US)
RMB (BRA)
●
HMI (GER)
FRM-II (GER)
●
SAFARI-1 (RSA)
●
●
●
●
ORPHEE (FRA)
HFR – ILL (FRA)
J-RTR (JRD)
●
● Reactor
● Accelerator
SINQ (SUI)
RA-10 (ARG)
JSNS/J-PARC (JPN)
PIK (RUS)
IBR-2 (RUS)
●
ESS (EU)
●
ISIS (UK)
●
ETRR-2 (EGP)
●
●

## Slide 34: FUTURE SCENARIOS OUTLINED IN THE 2016 ESFRI REPORT
Pessimistic scenario: ILL operates at reduced output until 2023, ESS with 22 instruments beyond 2028. Earlier closer and/reduced operations for a number of medium power sources
Optimistic scenario: ILL operates until 2030, ESS with 35 instruments beyond 2035.
ESFRI = European Strategy Forum on Research Infrastructure

## Slide 35: Financing
Host Countries Sweden and Denmark
Construction 47.5% Cash Investment ~ 97%
Operations 15%
Non Host Member Countries
Construction 52.5% In-kind Deliverables ~ 70%
Operations 85%
(Jan 2013 pricing) | M €
Conventional Facilities | 531.9
Extra CF investment by host countries | -93.0
Accelerator Systems | 510.2
Target Systems | 155.2
Integrated Control System | 73.0
Design & Engineering | 33.7
Neutron Scattering Systems | 350.0
Project Support & Administration and Licensing | 123.8
Contingency | 158.2
Total Construction Budget | 1843.0

## Slide 36: ESS design
High Power
Linear Accelerator:
Energy: 2 GeV (1.4 GeV in construction budget)
Rep. Rate: 14 Hz
Current: 62.5 mA
Committed to deliver 22 instruments by 2028 (15 Instruments in Construction budget)
Peak flux ~30-100 brighter than the ILL
Target Station:
He-gas cooled rotating
W-target -5MW average
power (2 MW in
construction budget)
42 beam ports
Ion Source
Total cost: 1843 M€ 2013
Environmental goal (“Sustainability”)
Energy responsible
Renewable energy
Recyclable heat

## Slide 37: The European Spallation Source
High Power Accelerator means more neutrons
An Innovative Target Station that can host >30 instruments
Flat moderator delivering smaller and brighter neutron beams
High brightness and tuneable resolution makes new measurements possible

## Slide 38: Long-pulse performance – 2MW
4
time (ms)
Brightness (n/cm2/s/sr/Å)
x1013
ISIS TS1
128 kW
ISIS TS2
32 kW
SNS
1-2 MW
JPARC
0.3-1 MW
ILL 57 MW
ESS 5 MW
2015 design
0
1
2
3
15
5
10
λ = 5 Å
ESS 5 MW
2013 design (TDR)
Possibilities of pulse shaping
ESS 2 MW
2015 design

## Slide 39: Two strategies for neutron instrumentation at ESS
Intensity
0
time (ms)
1
2
3
4
0
time (ms)
1
2
3
4
Use as much as possible of the whole pulse:
Good for low wavelength resolution instruments.
SANS, Reflectometry, single crystal diffraction.
Estimated gains 10-100 times than currently available.
Cut the long pulse into smaller pulses:
Good for higher wavelength resolution instruments
Diffraction, cold/thermal spectrometers.
Long Instruments (80-100 m)
Estimated gains 10-30 times than currently available.
Thermal gains lower.

## Slide 40: Organisation and People
> 400
Employees
48
Nationalities
> 45
Collaborating Institutions

## Slide 41: ESS partners
41
Aarhus University
Atomki - Institute for Nuclear Research
Bergen University
CEA Saclay, Paris
Centre for Energy Research, Budapest
Centre for Nuclear Research, Poland, (NCBJ)
CNR, Rome
CNRS Orsay, Paris
Cockcroft Institute, Daresbury
Elettra – Sincrotrone Trieste
ESS Bilbao
Forschungszentrum Jülich
Helmholtz-Zentrum Geesthacht
Huddersfield University
IFJ PAN, Krakow
INFN, Catania
INFN, Legnaro
INFN, Milan
Institute for Energy Research (IFE)
Rutherford-Appleton Laboratory, Oxford(ISIS)
Kopenhagen University
Laboratoire Léon Brilouin (LLB)
Lund University
Nuclear Physics Institute of the ASCR
Oslo University
Paul Sherrer Institute
Polska Grupa Energetyczna - PGE
Roskilde University
Tallinn Technical University
Technical University of Denmark
Technical University Munich
Science and Technology Facilities Council
University of Tartu
Uppsala University
WIGNER Research Centre for Physics
Wroclaw University of technology
Warsaw University of Technology
Zurich University of Applied Sciences (ZHAW)

## Slide 42: NSS Neutron Instrument positions: Project scope -December 2016
ESS Instrument Layout (December 2016)
ESS In-Kind Partners also collaborate on sample environment, data management systems etc.
ESS Lead Partners for instrument construction
+
Nuclear Physics Institute
+
ODIN
DREAM
NMX
MIRACLES
BEER
C-SPEC
T-REX
MAGIC
BIFROST
HEIMDAL
FREIA
LoKI
SKADI
VESPA
ESTIA
+

## Slide 43
Target
LINAC
Central Utilities Building (CUB)
Site
Offices
West sector (160 m) Instruments
East sector Instruments
South sector Instruments
August 2017
ESS Major Milestones:
First Neutrons – Beam on Target - Oct 2020
First Instrument– Beam on Instrument #1 – Feb 2021
First 8 Instruments – Start of open user program – Aug 2021
Full User Program – first 15 instruments – Jan 2026
Full scale operations – 22 user instruments – 2028 -> 2030