## Slide 1: RF Power Sources
Anders Sunesson
Morten Jensen
High Power RF Section Leader
www.europeanspallationsource.se
12 October 2017

## Slide 2: Background
The RF system provides energy to accelerate beam
  For acceleration
  To make up for energy losses
  Longitudinal focussing
The RF system converts the high DC voltage to RF energy.
The RF energy is directed to the cavities to accelerate the beam (charged particles).

## Slide 3: RF Sources
Common RF sources for Accelerating Cavities

## Slide 4: How to pick the technology
Frequency
Power CW/pulsed
Gain
Efficiency, capital cost, operating cost
Technical risk
Reliability, availability
Stability

## Slide 5: The Typical RF Chain
Splitters and distribution
Master Oscillator
Pre-Driver
High Power Amplifier
RF Load
Cavity
Beam
LLRF
Auxiliary supplies, interlocks etc
Books are written about amplifiers so consider this a taster…

## Slide 6: Solid State Amplifiers
1925 theory, Julius Edgar Lilienfeld
1947 Germanium US first transistor, John Bardeen, Walter Brattain, William Shockley
1948 Germanium European first transistor, Herbert Mataré and Heinrich Welker
1953 first high-frequency transistor, Philco
1954 Silicon transistor, Morris Tanenbaum
1960 MOS, Kahng and Atalla
1966 Gallium arsenide (GaAs)
1980 VDMOS
1989 Silicon-Germanium (SiGe)
1997 Silicon carbide (SiC)
2004 Carbon graphene
First transistor invented at BELL labs in 1947
XXI century LDMOS

## Slide 7: Solid State Amplifiers
NPN BJT
PNP BJT
Vout
Vin
Vdc
Use two transistors
Power each for half RF cycle
Transistor efficiency continuously improving
but many are combined to achieve high power
No high voltage source
but many low voltage power supplies
Cost per W is still high
-but dropping!
Size also dropping

## Slide 8: Solid State Amplifiers
Solid State has been used as drivers for many years
Soleil (3rd generation light source in France) – first light source to operate with high power RF from SSAs
Transistor technology has been pushed by huge market opportunities
Solid state amplifiers are largely replacing broadcast systems

## Slide 9: Solid State Amplifiers
RF input signal is amplified and split
Each split is amplified by many amplifiers in parallel
Each output is recombined in high power combiner
Each amplifier has status and control input and output

## Slide 10: Solid State Amplifiers
Take many individual stages and keep combining
Soleil Synchrotron Light Source

## Slide 11: Solid State Amplifiers
Soleil’s famous 45 kW towers
First SSA for a storage ring
Exceptional uptime
Highly redundant
Has led the way of thinking about the use of SSA for more and more high power applications

## Slide 12: Tetrodes
Diode, John Ambrose Fleming
Audion (first triode), Lee de Forest
Triode as amplifier, Fritz Lowenstein
Triode ‘higher vacuum’, Harold Arnold
first transcontinental telephone line, Bell
1916 Tetrode, Walter Schottky
Pentode, Bernardus Tellegen
1994 Diacrode, Thales Electron Devices
12
The first diode prototype Fleming Diode, 1904
Thales TH 595

## Slide 13: Tetrodes
Gridded tube with an intensity modulated beam
Good efficiency and power levels from few kW to few MW (pulsed or CW)
Transit time effects (time for electrons to travel from cathode to grid) limit the frequency to 300-400 MHz
Combined input and output circuit!
e-
Diode
Current controlled by DC supply
e-
Triode
Current modulated by grid voltage
Grid
e-
Tetrode
Grid
Screen grid
Second grid reduces the internal capacitance between grid and anode allowing higher frequencies and higher gain

## Slide 14: Klystrons
Officially invented by the Varian brothers and Bill Hansen in 1937 in Stanford (but papers on velocity modulation had already been published some years before by Rozhansky and the Heils in Europe and Russia).
The device was named “klystron” from the Ancient Greek verb κλυζω, which refers to waves hitting the shore + the suffix –tron, for the electrons.
D. A. Rozhansky
Oskar and Agnessa Heil
Russel and Sigurd Varian
The Stanford “model A” klystron
A picture explaining the klystron principle from the Varian patent
Klystrons cutaway models in the Stanford main quad

## Slide 15: Klystrons
Key to accelerators for > 50 years
For CW machines power is limited by cooling capacity since collector size can be increased
For pulsed machines power is limited by RF and DC breakdown
Klystrons are generally cost effective at high power and high frequency

## Slide 16: Klystrons
Heater
Metal surface
Adding like charges to the same volume increases the charge of the volume.
Perveance (k) is a constant describing how the space charge limited current varies as a function of voltage
It is largely determined by geometry
Electrons ‘boiling’ off the surface
Metal surface
The ‘voltage’ above the surface ‘pushes’ electrons back into the metal
Heater
0V
Positive Voltage
Charged particles, eg electrons, emitted from the cathode surface affect the voltage of the volume which they occupy. Describes the ‘charge of the volume’ occupied by the collection of point charges.
Applying a voltage allows a current to flow

## Slide 17: Klystrons
Typical heater curve
(APS 350 MHz)
Thermally limited cathode current
Space charge limited cathode current

## Slide 18: Klystrons
Cathode (-HV)
A Power Point Klystron
(DC Beam)
Magnetic Focussing
Magnetic Focussing
RF input
I=kV3/2

## Slide 19: Klystrons
Early Applegate diagram
(SLAC-pub-10620)
A two Cavity Example

## Slide 20: Klystrons
Klystron
(Velocity modulated)
Cathode (-HV)
A Power Point Klystron
(DC Beam)
Magnetic Focussing
Magnetic Focussing
RF input
RF output

## Slide 21: Klystrons
B-factory klystron (1.2 MW CW, 476 MHz) collector
Final assembly of the 75-XP3 klystron (SLAC)
Cut of a 5045 electron gun
B-factory klystron with solenoid
CPI-XL5 during commissioning at SLAC
Final assembly of the B-factory klystron at SLAC
Array of four 5045 bakeout ovens (SLAC)

## Slide 22: Klystrons
Klystrons reach maximum efficiency at saturation (65% for our 704 MHz klystrons, and 55-57% for the 352 MHz klystrons).
Typically need to be operated below saturation to allow overhead for control
Operation at full voltage for machines with varying power requirements reduces efficiency dramatically. For ESS the efficiency would be as low as 11% for the first amplifiers of the section!
It is then important that we are able to operate the klystrons at reduced beam voltages

## Slide 23: Klystrons
1 RFQ (1.6 MW input power at 352.21 MHz)
5 DTL tanks (2.2 MW input power at 352.21 MHz for each DTL, two couplers per DTL)
2.1 MW saturated power from the RFQ klystron
2.9 MW saturated power from the DTL klystrons
Klystron specs:
Thales TH2179
CPI VKP-8352A
25% overhead + 5% losses in RF distribution
Nominal output power | 3 MW
Frequency | 352.21 MHz
BW | ≥ +/- 1 MHz
Pulse width | 3.5 ms
Repetition rate | 14 Hz
Perveance | 1.3*10-6
Efficiency | >52%
VSWR | Up to 1.2
Power Gain | ≥ 40 dB
Group Delay | ≤ 250 ns
Harmonic Spectral content | ≤ -30 dBc
Spurious Spectral content | ≤ -60 dBc
Two klystrons currently available:
Dimensions: 5.3 m x 1.5 m x 1 m
Saturation

## Slide 24: Klystron
Nominal output power | 1.5 MW (for ESS)
Frequency | 704.42 MHz
Beam Voltage | 115 kV (max)
Beam current | 25 A (max)
Repetition rate | 14 Hz
Pulse length | 3.5 ms
Efficiency | 66%
Saturated Gain | 45.15 dB
Group Delay | 130 ns
Klystron at CERN with very similar parameters to ESS

## Slide 25: Klystrons for ESS 704 MHz linac sections
Toshiba
Thales
CPI

## Slide 26
The Inductive Output Tube (IOT)
Invented in 1938 by Andrew V. Haeff as a source for radar
To overcome limitation of output power by grid interception (notice transit time limitation is back)
Pass beam trough a resonant cavity
Achieved: 100 W at 450 MHz, 35% efficiency
Used first in 1939 to transmit television images from the Empire State Building to the New York World Fair
IOTs then lay dormant
Intense competition with velocity modulated tubes (klystron had just been invented by the Varian Brothers.)
Difficult to manufacture
The IOT is often described as a cross between a klystron and a triode hence Eimac’s trade name ‘Klystrode’

## Slide 27: IOT
Source
Control
Acceleration
Deceleration = RF Output
Bunching

## Slide 28: IOT
IOT
(Density modulated)
Biased
Control Grid
RF input
RF output
Reduced velocity spread compared to klystrons
Higher efficiency
No pulsed high voltage
Magnetic field
k = perveance (constant)
μ = amplification factor (constant)
Vg = grid voltage
Va=anode voltage
n=1.5-2.5 (typical)

## Slide 29
Pin
Pout
Klystron/MBK
IOT
MB-IOT
Operating
Power Level
+6 dB
hsat ~ 65-68%
ESS ~ 45%
Back-off for feedback
High gain
Low Gain
Long-pulse
excursions possible
Short-pulse
excursions possible
IOT’s don’t saturate.
Built-in headroom for feedback.
~ 70%
Courtesy of CPI
The Performance Comparison
Klystrons: Back-off for feedback cost 30%
IOTs: Operate close to max efficiency
Chart: Tuned for 80 kW @ 36 kV
| 387 | 370 | 324 | 277 | 212 | 168 | 133 | 106 | 82.4 | 65.7 | 32.299999999999997
80 kW, 36 kV | 83.1 | 80.6 | 72.7 | 62.2 | 46.3 | 34.8 | 25.9 | 19.1 | 13.7 | 10.1 | 3.85
Courtesy of e2v
Typical Example of 80 kW IOT

## Slide 30
Klystrons
IOTs
Electrical Power Consumed
Power delivered to beam
Power delivered to beam
High Beam Current
Low
Beam Current
Another
Cartoon!

## Slide 31: Efficiency comparison of Klystrons and IOTs
Klystron
IOT
IOT measurements courtesy of M. Boyle, L3
Based on broadcast IOT L-4444
System setup limited by drive power and beam voltage
IOT setup for maximum gain (not efficiency) without breakdown
No optimisation of coupling, grid voltages etc. for different power levels
Klystron assumed to have same saturated efficiency as the IOT
No optimisation of coupling, voltages, perveance for different power levels
traditional

## Slide 32: Key advantages of IOTs
High efficiency even when operating ‘backed-off’ for reduced RF output or regulation
Good linearity
Small and compact
Power is pulsed by RF instead of HV
Lower operating voltage
Lower Gain therefore needs more drive
Particularly beneficial for machines with:
  Varying power loads
  Non uniform power profiles
  Margins for overhead for regulation
  One-to-one relationship with amplifier to accelerating structure
  High average power applications

## Slide 33
Typical Broadcast IOT
Courtesy of e2v

## Slide 34: 3rd Generation Light Sources
Three 500 MHz 300 kW amplifier for Storage Ring: 4 x 80 kW IOT combined
IOT 1
IOT 2
IOT 3
IOT 4
Output

## Slide 35
700 MHz HOM IOT Experience
Design Parameters value units
Power Output 1000 kW (min)
Beam Voltage 45 kV (max)
Beam Current 31 A (max)
Frequency 700 MHz
1dB Bandwidth ± 0.7 MHz (min)
Gain 23 dB (min)
Efficiency 71 % (min)
Diameter 30/76 in/cm
Height 51/130 in/cm
Weight 1000/450 lbs./kg
Collector Coolant Flow 220 gpm
Body Coolant Flow 10 gpm
O/P Window Cooling (Air) 35 cfm
@ 31kV
RF Input
Collector
Solenoid,
O/P Cavity
Gun
RF Output
Test Results (pulsed)
  VHP-8330A IOT

## Slide 36: Elliptical (704 MHz) RF System Layout Power needs space
Klystrons
Modulator
Installed RF Power 8 x 1.5 MW = 12 MW
Space available = 130 m2 > 90 kW / m2
Solid State solution:
15 kW/rack = 100 racks excl. combiners etc.

## Slide 37: Multi-Beam IOTs for ESS
10 Beam Multi-Beam IOT
1.2 MW
704 MHz
Broadcast IOTs are limited in power to 100 kW
Operate with a single cathode
So how to achieve > 1 MW?

## Slide 38
Parameter |  | Comment
Frequency | 704.42 MHz | Bandwidth > +/- 0.5 MHz
Maximum Power | 1.2 MW | Average power during the pulse
RF Pulse length | Up to 3.5 ms | Beam pulse 2.86 ms
Duty factor | Up to 5% | Pulse rep. frequency fixed to 14 Hz
Efficiency | Target > 65% | 
High Voltage | Low | Expected < 50 kV
Design Lifetime | > 50,000 hrs | 
The IOT for ESS
Saving:
3.3 MW power reduction by using IOTs for High Beta

## Slide 39: Current Status of the first ESS MB IOT
Output Cavity under cold test

## Slide 40: ESS accelerator power profile
Normal-conducting Linac:
One RFQ and 5 DTL tanks
6 off 352 MHz klystrons
3 MW
3 Solid state amplifiers for bunchers
352 MHz, 30 kW
Average beam power: 5 MW > 130 MW peak
Pulse repetition rate: 14 Hz
Beam pulse length: 2.86 ms
26 spoke cavities:
352 MHz
Tetrodes
36 Medium beta cavities: 704 MHz
1.5 MW Klystrons
84 High beta cavities: 704 MHz
1.2 MW MB IOTs (klystrons as backup)

## Slide 41: What will power (ESS)? The most powerful proton linac built.
  Average beam power of 5 MW (Peak > 130 MW RF)
  Over 150 individual high power RF sources
352 MHz
704 MHz
3 MW Klystrons
30 kW Solid State Amplifiers
200 kW Tetrodes
1.5 MW Klystrons
1.2 MW IOTs
Solid state Drivers (100 W – 10 kW)

## Slide 42: Summary
Accelerators have different requirements
  Power, frequency, cost, space, …
Technology choice depends on what is available or what can be developed subject to time, budget, risk, …
Main RF sources for accelerating cavities include:
  Solid State Amplifiers
  Tetrodes
  Klystrons
  IOTs

## Slide 43: Summary
Solid State amplifiers:
  Modern and rapidly improving performance
  Broad frequency range but high power means 1000s of units combined for MW power levels
  Efficiencies up to > 60% depending on power and frequency.
  Very competitive and compact for small supplies up to a few kW
  No HV supply required
  Still costly for large systems and needs space
Tetrodes
  Good efficiency at point of operation, particularly at lower frequency
  Power capability reduces as frequency increases (200 kW at 350 MHz)
  Max frequency around 400 MHz
  Tetrode is ‘cheap’ but full amplifier is costly
  Tetrode life expectancy up to 30k hours subject to application

## Slide 44: Summary
Klystrons
  Has been workhorse for > 50 years
  Suitable from > 300 MHz to many GHz
  MW in CW, 10s MW pulsed
  Life expectancy can by > 100k hours depending on application
  Efficiency up to 65% at saturation but often lower at point of operation
IOT
  Suitable frequency range 400 MHz – 1.3 GHz
  Available in units of 100 kW which can be combined
  MW class IOT under development
  >60% efficiency at point of operation
  Life expectancy 50k – 100 k hours