## Slide 1: Extending mbbiDirect and mbboDirect Records to 32 Bit
Dirk Zimoch :: Controls Section :: Paul Scherrer Institut
EPICS Collaboration Meeting at ICALEPCS 2017

## Slide 2: Current mbbiDirect
Input (RVAL) is 32 bit
Output (VAL, B0 … BF) is only 16 bit
Why?
mbbiDirect
RVAL 32 bit
VAL 16 bit
B0
BF
⁞
SHFT
Device support

## Slide 3: Future mbbiDirect
Input (RVAL) stays 32 bit
Output (VAL, B0 … BF, B10 … B1F) will be 32 bit as well
Mostly backward compatible
mbbiDirect
RVAL 32 bit
VAL 32 bit
B0
B1F
⁞
SHFT
Device support

## Slide 4: Same for mbboDirect
Output (RVAL) stays 32 bit
Input (VAL, B0 … BF, B10 … B1F) will be 32 bit as well
mbboDirect
VAL 32 bit
RVAL 32 bit
B0
B1F
⁞
SHFT
Device support

## Slide 5: Compatibility
RVAL was and will be ULONG
  Most device supports only access RVAL and need no change
  Record memory layout changes: re-compile all device supports!
VAL was USHORT and will be LONG
  For 16 bit values nothing will change
  Channel Access Clients have always seen a LONG
Device support accessing VAL or B* fields need modification to support higher bits.
  Use 32 bit variables when accessing prec->val
  Using pointer &prec->val is not safe!
  When iterating bit fields check for macros like mbboDirectRecordB1F

## Slide 6: Why not 64 bit?
64 bit integers are not supported by Channel Access
Changing RVAL to 64 bit would break all existing device support
Possible as new record type
What do you think?