## Slide 1
Beam commissioning of the high intensity proton source developed at INFN-LNS for ESS
Lorenzo Neri
Notes: I want to thanks the scientific committee to had given me this opportunity.
I'm proud to be here on behalf of the INFN-LNS Accelerator R&D team to present the:...

## Slide 3: Phases
Source
Phases 1 and 2
Phases 3 and 4 = Lund commissioning

## Slide 4: Proton Source and LEBT at INFN-LNS
H2 injection
Extraction
Plasma chamber
Magnetic system
ATU
2x TMP
RGA
Gauges
Gas injection
(ESS)
Solenoid
Solenoid
Collimator
2x EMU
FC
Doppler
(CEA, ESS)
2x TMP
Gauges
Gas injection
(ESS)
Six blade
iris
Magnetron
Chopper

## Slide 5: ISRC&LEBT Documentations
INFN is providing a shared INFN
collecting:
Drawings
Diagrams
Cable specifications
Manuals
Factory acceptance test
Guides
Certification of conformities
Interface drawings
Non conformity reports
The documentation is collected in folders organized following the Product Breackdown Structure.
Notes: product breackdown structure e visione sito cloud: isrc-estrazione-drawings+ps+certificato rame, insulating column-drawings+certificato vuoto, magneti sorgente con documento completo, magnetron con manuale, lebt solenoidi drawings+ps+fat, chopper+disegni+diagramma blocchi+schematics+signal list, irisdisegni+manuale,supporti-disegni, base-disegni, fug, cavi,
Interfacce documento edgar, cartella interfacce
Standard dentro i disegni, guide, slide andrea+ornella^2

## Slide 6: Physics design of Ion Source and LEBT equipment
Thermomecanical (Comsol)
Stationary and time dependent beam transport in space charge compensation regime (Particle in cell simulation code)
Differential pressure gap between plasma chamber and LEBT
(Comsol)
Flexible magnetic system design
(OPERA, Comsol)
Plasma dynamics and species fraction composition (Particle in cell simulation code)
Beam extraction
(Axcel)
Reduction of electric field (Comsol)
Improvements starting from IFMIF design (in collaboration with CEA)
Pulse rise and fall time using LEBT chopper (Prototype tested on BETSI)
Microwave to plasma coupling (3D Full wave simulation code)
Defocusing chopper (Comsol, TraceWin)

## Slide 7: Increase electronics strength against discharge
FC voltage protection
Shielded sub-rack at ground
Shielded sub-rack on the HV platform
Wide use of optical fibers
Grounding grid

## Slide 8: Improvements in the extraction system
Lower the useless electric field close to the extraction
X Ray protection
Beam dynamics through electrodes
Single alumina to minimize the electric field on the external surface (< 6.6 kV/cm)
New triple point design (< 6.4 kV/cm)
We had not serious problems of discharge during beam extraction at 75 kV.
Extraction column was tested up to 90 kV.
air
LEBT
Plasma chamber
Plasma chamber
Beam axis

## Slide 9: Plasma modeling
RF energy adsorption
Electron Energy Distribution Function
Generation maps
e-
p+
Ion formation
L. Neri et al. "Recent progress in plasma modelling at INFN-LNS", Rev. Sci. Instrum. 2016 Feb, 87(2):02(A)505
Magnetic system flexibility helps to tailor the EEDF

## Slide 10: Microwave to plasma coupling
3D full wave e-m simulation in presence of the electron plasma density and strong magnetic field has driven the design of the matching transformer
Empty cavity
Cold tensor plasma approximation
Low measured reflected power
G. Torrisi et al. "Microwave injection and coupling optimization in ECR and MDIS ion sources”, this conference
High measured stability of forward and reflected power
Measured forward and reflected pulsed power
G. Torrisi et al. "Full-wave FEM simulations of electromagnetic waves in strongly magnetized non-homogeneous plasma", JEWA 2014 vol. 20, no. 9, 1085-1099
< 1%
< 1‰
Forward
Reflected

## Slide 11: Magnetic system control interface
Plasma chamber
Matching transformer
Extraction
0 mm
35 mm
84 mm
Fine tuning ± 5 Gauss
Coarse tuning ± 50 Gauss
ECR
Very high magnetic flexibility required a dedicated interface developed at INFN that enable direct control and high reproducibility

## Slide 12
Semi-automatic characterization tool
From the 23/01/2017 the source is extracting beam seamless, more than 300˙000 tested configurations, no stops due to sparks.
Watt
SCCM
Time left
Configurations
left
Coil 1
Coil 2
Coil 3
Plasma modelling 
parameters range to be tested:
Field @ 0 mm ==> 835:20:975 Gauss
Field @ 35 mm ==> 795:40:1395 Gauss
Field @ 84 mm ==> 675:40:1995 Gauss
H2 flow ==> 2:1:5 SCCM
RF power ==> 600:200:1200 Watt
40ֺ192 configurations

## Slide 13
ACCT
HV cable
GND grid
HV Platform
Experimental setup for source commissioning
Source
Faraday Cup
Emittance Measurement Unit
Doppler Shift Measurement Unit
2 xTMP
Gauges
RGA
Extraction

## Slide 14: Semi-automatic characterization
In the graphical interface: average, maximum and minimum are evaluated and the trend showed for the beam pulse between 2.9 ms and 5.9 ms .
In the semi-automatic characterization code 26 parameters and two wave forms (@1Ms/s) are saved for each pulse produced at nominal repletion rate of 14Hz.
40ֺ192 configurations
10 seconds each
=
4.7 days

## Slide 15
ACCT [mA]
Ripple [au]
ACCT(ESS) [mA]
FC [mA]
Data analysis of thousands of different configurations

## Slide 16
ACCT [mA]
Ripple [au]
ACCT(.5xESS) [mA]
* ACCT(ESS) [mA]
FC [mA]
Data analysis of thousands of different configurations

## Slide 17
Doppler shift measurement beam characterization
Proton fraction > 75% SATISFIED
p+ [%]
H2+ [%]
H3+ [%]
ACCT [mA]

## Slide 18
ESS stable configurations versus injected H2 gas flux and microwave power
Increasing the injected microwave power increase the energy transfer and consequently the plasma density
Each point is a large operative range (20 Gauss x 40 Gauss x 40 Gauss x 1 SCCM x 200 Watt)
Lower current (2-5 sccm)
High current (2-4 sccm)
Total current = 100 mA SATISFIED

## Slide 19
Minimum proton current range 67-74 mA SATISFIED
Doppler shift measurement
Candidate nominal configuration
Intra-pulse stability < ±2% SATISFIED
Pulse to pulse stability < ± 3.5% SATISFIED
109 A coil1; 67 A coil2; 228 A coil3; 3 SCCM H2

## Slide 20
Chopping performaces
Total current
LEBT ACCT
FC current

## Slide 21
Iris performaces

## Slide 22
Candidate nominal configuration
Transverse emittance SATISFIED
Emit [rms] < 0.25 Pi.mm.mrad
Emit [rms] < 2.25 Pi.mm.mrad
109 A coil1; 67 A coil2; 228 A coil3; 3 SCCM H2
Emittance measured after 100 mm of the RFQ beam lattice interface.

## Slide 24
EMU (CEA) had long period of stop during phase 2
Commissioning tank (ESS) was not suitable for Phase 1 and 2

## Slide 25
NPM (ESS) worked ones during preliminary test but never working after installation in the beam line

## Slide 26
EMU (CEA) is not stable and was provided late to have enough time to allow a better match
NPM (ESS) worked ones during a test but never working after installation in the beam line
Chopper (INFN) electronics need to be calibrated for a faster transition
Chopper (INFN) non conformity didn’t affect beam performances

## Slide 27: Conclusion
The flexibility inserted in the design enabled the satisfaction of ESS requirements
NO sparks relevant problems remain unsolved
No delay for the RFI date: Monday 18 September is planned to dismount the Source and LEBT

## Slide 28
Thanks for your attention
Comments are welcome
Thanks to all INFN-LNS staff to valuable support provided during all the phases of the project.
The collaboration with ESS and CEA was intense, profitable, always solution oriented.